Detailed Design

Requested by: 		Mr. Ken Swarner

Systems Administrator

Computer Science Department of Siena College

TCP/IP Packet Descriptor

Mirage Incorporated

“We are there…even if you cannot see us”

Mirageinc2003@yahoo.com

Prepared by:			Paul Aiuto

Richard Connell

Lauren Englisbe

Jayme Gresen, Team Leader

Jeffrey Habiniak

Preliminary Design

Table of Contents

| External Design Specifications | 4 |
| --- | --- |
| 1.1 User Displays | 4-14 |
| 1.2 User Command Summary | 15 |
| 1.3 Detailed Data Flow Diagrams | 16-18 |
| 2.0 Architectural Design Specification | 19 |
| 2.1 User Commands (AKA “Clickable Buttons”) | 19 |
| 2.2 Functional Descriptions | 20 |
| 2.2.1 IP PDU for the selected FTP PDU | 20-33 |
| 2.2.2 TCP PDU for the selected FTP PDU | 34-44 |
| 2.2.3 FTP PDU for the selected FTP PDU | 45 |
| 2.2.4 IP PDU for the selected ICMP PDU | 46-58 |
| 2.2.5 ICMP PDU for the selected ICMP PDU | 59-65 |
| 2.2.6 IP PDU for the selected SMTP PDU | 66-79 |
| 2.2.7 TCP PDU for the selected SMTP PDU | 80-90 |
| 2.2.8 SMTP PDU for the selected SMTP PDU | 91-93 |
| 2.2.9 IP PDU for the selected UDP PDU | 94-113 |
| 2.2.10 UDP PDU for the selected UDP PDU | 114-118 |
| 2.2.11 IP PDU for the selected SNMP PDU | 119-130 |
| 2.2.12 UDP PDU for the selected SNMP PDU | 131-135 |
| 2.2.13 SNMP PDU for the selected SNMP PDU | 136-144 |
| 2.2.14 IP PDU for the selected TELNET PDU | 145-156 |
| 2.2.15 TCP PDU for the selected TELNET PDU | 157-167 |
| 2.2.16 TELNET PDU for the selected TELNET PDU | 168 |
| 2.2.17 IP PDU for the selected SSH PDU | 169-180 |
| 2.2.18 TCP PDU for the selected SSH PDU | 181-190 |
| 2.2.19 SSH PDU for the selected SSH PDU | 191-192 |
| 2.2.20 ARP PDU for the selected ARP PDU | 193-204 |
| 2.2.21 IP PDU for the selected PING PDU | 205-212 |
| 2.2.22 ICMP PDU for the selected PING PDU | 213-220 |
| 2.2.23 IP PDU for the selected HTTP PDU | 221-234 |
| 2.2.24 TCP PDU for the selected HTTP PDU | 235-244 |
| 2.2.25 HTTP PDU for the selected HTTP PDU | 245-262 |
| 3.0 Testing Requirements | 263 |
| 3.1 Testing Overview | 263 |
| 3.2 Test Cases | 263 |
| 3.3 Testing Sheets | 264 |
| 3.3.1 Functional Requirements Testing Sheet | 264-265 |
| 3.3.2 Ethernet Testing Sheet | 266-267 |
| 3.3.3 IP Testing Sheet | 268-270 |
| 3.3.4 TCP Testing Sheet | 271-273 |
| 3.3.5 FTP Testing Sheet | 274 |
| 3.3.6 ICMP Testing Sheet | 275-276 |
| 3.3.7 SMTP Testing Sheet | 277 |
| 3.3.8 UDP Testing Sheet | 278 |
| 3.3.9 SNMP Testing Sheet | 279-280 |
| 3.3.10 TELNET Testing Sheet | 281 |
| 3.3.11 SSH Testing Sheet | 282 |
| 3.3.10 ARP Testing Sheet | 283-284 |
| 3.3.11 PING Testing Sheet | 285-287 |
| 3.3.12 HTTP Testing Sheet | 288-289 |
| 4.0 Detailed Design Specification | 290 |
| 4.1 Packaging and Deployment Specifications | 290 |
| 5.0 Appendix | 291 |
| 5.1 Gantt Chart | 291 |
| 5.1 Glossary | 292-294 |

1.0	External Design Specifications

  - User Displays

This will be the first screen the user sees.  It is the introduction screen to our software, and presents our mascot, “The Descript-roar”.

This is the first functional screen the user will see.  It allows the user to see what an Ethernet Packet looks like, and eventually each frame within that packet will be clickable and able to display information about that frame.

The “Choose a Protocol” menu gives the user a graphical representation of how protocols are interrelated, and allows the desired protocol to be selected.

Once a protocol has been selected by the user, this screen will display.  The basis for our protocol suite, the IP PDU is displayed on the left, filled in with the given data for the selected protocol.  The user is able to click on any field in the IP PDU, and an information box will display on the right, describing that field.  In the IP PDU Data field, “TCP PDU” is written – this indicates that the entire TCP PDU is contained within the IP Data field.  If the user clicks on this field, the TCP PDU will be displayed.

The PDU’s are tabbed on their lower left corners: this allows the user to navigate between them.  Additionally, there is a key at the top right corner to display what PDUs make up the chosen protocol.  The user may also click on any PDU in this map to navigate.  If at any point, the user wants to choose a different protocol to view, he or she may click on the “Choose a Protocol” button in the top left corner.

The next screen shows the TCP PDU on top of the IP PDU.  This is meant to show that the TCP PDU is contained within the IP PDU.  Additionally, the Telnet PDU is contained within the TCP PDU Data field, so clicking on that field will display the Telnet PDU.  As with IP, if a TCP field is clicked, the information for that field will be displayed in the information box at the right.

This is the software with all the information displayed for the selected Telnet PDU.  The IP PDU gives rise to the TCP PDU, and the TCP Data field has been clicked, which allows us to see the information field for the Telnet PDU on the right.

This is a screenshot of the ARP protocol and its information field.

FTP Protocol

HTTP Protocol

PING Protocol

SSH Protocol

UDP Protocol

1.2 User Command Summary

## Main Screen

This is the screen giving the user the option to choose many different packets.

## PDU Hierarchy Tree

Allows the user to see their progression through the many packets, and also able to choose their desired packet.

# IP Version

Allows the user two chooses of two different IP Versions.

# Radix (Base) Selection

Allows the user to select a radix to display.

# Information Box

Allows the user to see the given information for a selected field.

1.3 Detailed Data Flow Diagrams

Level 0 Diagram:

Context Diagram:

Detailed Diagram:

2.0 Architectural Design Specifications

2.1 User Commands (AKA “Clickable Buttons”)

# IP PDU

IP Version

Internet Header Length

Type of Service

Total Length of Ethernet Frame

Identification

Flags

Fragment Offset

Time to Live

Protocol

Header Checksum

Source IP Address

Destination IP Address

Options

Data

# TCP PDU

Source Port Number

Destination Port Number

Sequence Number

Acknowledgement Number

Header Lengths

Reserved

Window Size

TCP Checksum

Urgent Pointer

Options

Data

2.2 Functional Descriptions

2.2.1 IP PDU for the selected FTP PDU

IP PDU > IP Version for the selected FTP PDU

Field Name: IP Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be IP_IPVersion_FTP.

IP PDU > Internet Header Length for the selected FTP PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4-bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |
| Decimal | 5 |

Programming Hint: The name for this variable in code will be IP_IHL_FTP.

IP PDU > Type of Service for the selected FTP PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Inter-network Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 10

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |
| Decimal | 16 |

Programming Hint: The name for this variable in code will be IP_TypeOfService_FTP.

IP PDU > Total Length of Ethernet Frame for the selected FTP PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key:  Not applicable

Data values (hexadecimal):  69

Data values in other bases:

| Hexadecimal | 0 | 0 | 6 | 9 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0110 | 1001 |
| Decimal | 0 | 105 |
| ASCII | © | i |

Programming Hint: The name for this variable in code will be IP_TotalLength_FTP.

IP PDU > Identification for the selected FTP PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet.

Field Key:  Not applicable

Data value (hexadecimal): AA 41

Data values in other bases:

| Hexadecimal | A | A | 4 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 1010 | 1010 | 0100 | 0001 |

Programming Hint: The name for this variable in code will be IP_Idenfification_FTP.

IP PDU > Flags for the selected FTP PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_Flags_FTP.

IP PDU > Fragment Offset for the selected FTP PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0 0000 0000 0000

Programming Hint: The name for this variable in code will be IP_FragmentOffset_FTP.

IP PDU > Time to Live for the selected FTP PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_FTP.

IP PDU > Protocol for the selected FTP PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	 10	Telnet						116		74	   WIDEBAND Monitoring

17	 11	XNET						117		75	   WIDEBAND EXPAK

20	 14	Chaos						120-376	78-0178  Unassigned

21	 15	User Datagram				377		0179	    Reserved

Data value (hexadecimal): 06

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |
| Decimal | 6 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming Hint: The name for this variable in code will be IP_Protocol_FTP.

IP PDU > Header Checksum for the selected FTP PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): 0E 85

Data values in other bases:

| Hexadecimal | 0 | E | 8 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 1110 | 1000 | 0101 |

Programming Hint: The name for this variable in code will be IP_HeaderChecksum_FTP.

IP PDU > Source Address for the selected FTP PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value (decimal):  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |
| Decimal | 192 | 168 | 0 | 39 |

Programming Hint: The name for this variable in code will be IP_SourceAddress_FTP.

IP PDU > Destination Address for the selected FTP PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key: Not applicable

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192 | 168 | 0 | 101 |

Programming Hint: The name for this variable in code will be IP_DestinationAddress_FTP.

IP PDU > Options and Padding for the selected FTP PDU

Field Name:  Options and Padding

Purpose and Definition:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Field Key:  Not applicable

Data values:  Not applicable

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_OptionsPadding_FTP.

IP PDU > Data for the selected FTP PDU

Field Name:  Data

Purpose and Definition:  The Data is a variable length field which contains the actual data that is being sent from one host to another.  The data field may start with a Layer 4 header, which will give additional instructions to the application that will be receiving the data; alternately, it may be an ICMP header and not contain any user data at all.

Field Key:  Not applicable

Data values (hexadecimal) :  (TCP) 80 30 00 15 81 A5 16 6C 87 A3 53 5D 80 18 16 D0 11 F4 00 00 01 01 08 0A 1B 25 F3 A1 0b DD 73 58

(FTP) 50 41 53 53 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

Data values in other bases:

Hexadecimal: (TCP) 0 x 80 30 00 15 81 A5 16 6C 87 A3 53 5D 80 18 16 D0 11 F4 00 00 01 01 08 0A 1B 25 F3 A1 0B DD 73 58

(FTP) 50 41 53 53 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

ASCII:  (TCP) ↑ 0 © © ↑ ↑ © ↑ ↑ S ] ↑ © © ↑ © ↑ © © © © © © © % ↑ ↑ © ↑ s X

(FTP) P A S S S © f 1 a 2 k 3 u s e r © ©

Programming Hint: The name for this variable in code will be IP_Data_FTP.

2.2.2 TCP PDU for the selected FTP PDU

IP > TCP PDU > Source Port for the selected FTP PDU

Field Name:  Source Port

Purpose and Definition:

This 16-bit number represents the name of the application that sent the data in the IP packet.

Field Key:  Not applicable

Data value (decimal): 32816

Data values in other bases:

| Hexadecimal | 8 | 0 | 3 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 0000 | 0011 | 0000 |
| Decimal | 128 | 48 |
| ASCII |  | 0 |

Programming Hint: The name for this variable in code will be IP_TCP_SourcePort_FTP.

IP > TCP PDU > Destination Port for the selected FTP PDU

Field Name: Destination Port

Purpose and Definition:
This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

Field Key:

This key indicates assigned port number values:

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (decimal): 21 (indicates FTP)

Data values in other bases:

| Hexadecimal | 0 | 0 | 1 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0101 |
| Decimal | 0 | 21 |
| ASCII | © | © |

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

Programming Hint: The name for this variable in code will be IP_TCP_DestinationPort_FTP.

IP > TCP PDU > Sequence Number for the selected FTP PDU

Field Name:  Sequence Number

Purpose and Definition: 
TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Field Key:  Not applicable

Data value (decimal): 2175080044

Data values in other bases:

| Hexadecimal | 8 | 1 | A | 5 | 1 | 6 | 6 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 0001 | 1010 | 0101 | 0001 | 0110 | 0110 | 1100 |
| Decimal | 0 | 60 | 176 | 60 |
| ASCII | © | ‘ |  | ‘ |

Programming Hint: The name for this variable in code will be IP_TCP_SequenceNumber_FTP.

IP > TCP PDU > Acknowledgement Number for the selected FTP PDU

Field Name: Acknowledgement Number

Purpose and Definition: 
This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Field Key:  Not applicable

Data value: 2275627869

Data values in other bases:

| Hexadecimal | 8 | 7 | A | 3 | 5 | 3 | 5 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 0111 | 1010 | 0011 | 0101 | 0011 | 0101 | 1101 |
| Decimal | 135 | 163 | 83 | 93 |
| ASCII |  |  | S | ] |

Programming Hint: The name for this variable in code will be IP_TCP_AcknowledgementNumber_FTP.

IP > TCP PDU > Header Length or Offset for the selected FTP PDU

Field Name:  Header Length or Offset

Purpose and Definition: 
This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header.

Field Key:  Not applicable

Data value (bytes): 32

Data values in other bases:

| Hexadecimal | 8 | 0 |
| --- | --- | --- |
| Binary | 1000 | 0000 |
| Decimal | 128 |
| ASCII |  |

Programming Hint: The name for this variable in code will be IP_TCP_HeaderLength_FTP.

IP > TCP PDU > Reserved for the selected FTP PDU

Field Name:  Reserved

Purpose and Definition: 
These 6 bits are unused and are always set to 0.

Field Key:  Not applicable

Data value (binary): 0000 00

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 |
| Decimal | 0 | 0 | 0 |
| ASCII | © | © | © |

Programming Hint: The name for this variable in code will be IP_TCP_Reserved_FTP.

IP > TCP PDU > Control Flags for the selected FTP PDU

Field Name:  Control Flags

Purpose and Definition: 
Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:

- Urgent (URG)

- Acknowledgement (ACK)

- Push (PSH)

- Reset (RST)

- Synchronize (SYN)

- Finish (FIN)

Data value (binary): 01 1000

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_TCP_ControlFlags_FTP.

IP > TCP PDU > Window Size for the selected FTP PDU

Field Name:  Window Size

Purpose and Definition: 
Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:  Not applicable

Data value (decimal): 5840

Data values in other bases:

| Hexadecimal | 1 | 6 | D | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0110 | 1110 | 0000 |
| Decimal | 22 | 224 |
| ASCII | © |  |

Programming Hint: The name for this variable in code will be IP_TCP_WindowSize_FTP.

IP > TCP PDU > Checksum for the selected FTP PDU

Field Name:  Checksum

Purpose and Definition: 
Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Field Key:  Not applicable

Data value (hexadecimal): 11 F4

Data values in other bases:

| Hexadecimal | 1 | 1 | F | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0001 | 1111 | 0100 |
| Decimal | 17 | 244 |
| ASCII | © | © |

Programming Hint: The name for this variable in code will be IP_TCP_Checksum_FTP.

IP > TCP PDU > Urgent Pointer for the selected FTP PDU

Field Name: Urgent Pointer

Purpose and Definition: 
If the Urgent flag is set to on, this value indicates where the urgent data is located.

Information Key:  Not applicable

Data value:  Not applicable

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_TCP_UrgentPointer_FTP.

IP > TCP PDU > Options and Padding for the selected FTP PDU

Field Name: Options and Padding

Purpose and Definition: 
Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits.

Field Key:  Not applicable

Data value (hexadecimal): 01 01 08 0A 1B 25 F3 A1 0B DD 73 58

Data values in other bases:

| Hexadecimal | 0 | 1 | 0 | 1 | 0 | 8 | 0 | A | 1 | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0001 | 0000 | 0001 | 0000 | 1000 | 0000 | 1010 | 0001 | 1011 |
| Decimal | 1 | 1 | 8 | 10 | 27 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 2 | 5 | F | 3 | A | 1 | 0 | B | D | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0101 | 1111 | 0011 | 1010 | 0001 | 0000 | 1011 | 1101 | 1101 |
| Decimal | 37 | 243 | 161 | 11 | 221 |
| ASCII | % |  |  | © |  |

| Hexadecimal | 7 | 3 | 5 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0101 | 0011 | 0101 | 1000 |
| Decimal | 115 | 96 |
| ASCII |  |  |

Programming Hint: The name for this variable in code will be IP_TCP_OptionsPadding_FTP.

2.2.3 FTP PDU for the selected FTP PDU

IP >TCP > FTP Header for the FTP Packet

RFC Link:  http://www.ietf.org/rfc/rfc0959.txt?number=959

PASS (Password)

The argument field is a Telnet string specifying the user’s password.  This command must be immediately preceded by the user name command, and, for some sites, completes the user’s identification for access control.

What is Contained in the Packet

Request:	PASS

Request Arg:	f1a2k3user

Data Values (hexadecimal): 50 41 53 53 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

Data Values in Other Bases:

| ASCII | P | A | S | S | SPC | f | 1 | a | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hexadecimal | 5 0 | 4 1 | 5 3 | 5 3 | 2 0 | 6 6 | 3 1 | 6 1 | 3 2 |
| Binary | 0101 0000 | 0100 0001 | 0101 0011 | 0101 0011 | 0010 0000 | 0110 0110 | 0011 0001 | 0110 0001 | 0011 0010 |
| Decimal | 80 | 65 | 83 | 83 | 32 | 102 | 49 | 97 | 59 |

| ASCII | k | 3 | u | s | e | r | \r | \n |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hexadecimal | 6 B | 3 3 | 7 5 | 7 3 | 6 5 | 7 2 | 0 D | 0 A |
| Binary | 0110 1011 | 0011 0011 | 0111 0101 | 0111 0011 | 0110 0101 | 0111 0010 | 0000 1101 | 0000 1010 |
| Decimal | 107 | 51 | 117 | 115 | 101 | 114 | 13 | 10 |

Programming Hint: The name for this variable in code will be IP_TCP_FTP_PDU_FTP.

2.2.4 IP PDU for the selected ICMP PDU

IP PDU > Version for the selected ICMP PDU

Field Name: Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be IP_Version_ICMP.

IP PDU > Internet Header Length for the selected ICMP PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4 bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |
| Decimal | 5 |

Programming Hint: The name for this variable in code will be IP_Version_ICMP.

IP PDU > Type of Service for the selected ICMP PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 00

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |
| Decimal | 0 |

Programming Hint: The name for this variable in code will be IP_TypeOfService_ICMP.

IP PDU > Total Length of Ethernet Frame for the selected ICMP PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key: Not applicable

Data values (decimal):  84

Data values in other bases:

| Hexadecimal | 0 | 0 | 5 | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0101 | 0100 |
| Decimal | 0 | 84 |
| ASCII | © | T |

Programming Hint: The name for this variable in code will be IP_TotalLength_ICMP.

IP PDU > Identification for the selected ICMP PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet

Field Key: Not applicable

Data value (hexadecimal): 00 00

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |

Programming Hint: The name for this variable in code will be IP_Identification_ICMP.

IP PDU > Flags for the selected ICMP PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_Flags_ICMP.

IP PDU > Fragment Offset for the selected ICMP PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0000 0000 0000

Programming Hint: The name for this variable in code will be IP_FragmentOffset_ICMP.

IP PDU > Time to Live for the selected ICMP PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_ICMP.

IP PDU > Protocol for the selected ICMP PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	  Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	 10	Telnet						116		74	   WIDEBAND Monitoring

17	 11	XNET						117		75	   WIDEBAND EXPAK

20	 14	Chaos						120-376	78-0178  Unassigned

21	 15	User Datagram				377		0179	    Reserved

Data value (hexadecimal): 01

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0001 |
| Decimal | 1 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming Hint: The name for this variable in code will be IP_Protocol_ICMP.

IP PDU > Header Checksum for the Selected ICMP PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  This CRC algorithm is the 16-bit one’s complement sum of all the 16-bit words in the header.  For purposes of computing the checksum, the value of the checksum field is initially zero.  When both header checksums are the same, then the header bits are correct.  If either checksums vary, then a packet will need to be resent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): B8 CC

Data values in other bases:

| Hexadecimal | B | 8 | C | C |
| --- | --- | --- | --- | --- |
| Binary | 1011 | 1000 | 1100 | 1100 |

Programming Hint: The name for this variable in code will be IP_HeaderChecksum_ICMP.

IP PDU > Source Address for the Selected ICMP PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value:  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |
| Decimal | 192 | 168 | 0 | 39 |

Programming Hint: The name for this variable in code will be IP_SourceAddress_ICMP.

IP PDU > Destination Address for the selected ICMP PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key:  Not applicable

Data value:  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192. | 168. | 0. | 101 |

Programming Hint: The name for this variable in code will be IP_DestinationAddress_ICMP.

IP PDU > Options and Padding for the selected ICMP PDU

Field Name:  Options and Padding

Purpose and Definition:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Field Key:  Not applicable

Data values:  Not applicable

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_OptionsPadding_ICMP.

2.2.5 ICMP PDU for the selected ICMP PDU

IP > ICMP Header > Type for the selected ICMP PDU

Field Name:  Type

Purpose and Definition:  The type is an 8-bit field that identifies what sort of message the ICMP protocol is sending.

Field Key:

# Dec	 Hex	Message Type		Dec	  Hex	   Message Type

0	00	Echo Reply			16	  10	   Information Reply

1	01	Unassigned			17	  11	   Address Mask Request

2	02	Unassigned			18	  12	   Address Mask Reply

3	03	Destination Unreachable	19	  13	   Reserved (for Security)

4	04	Source Quench		20-29	  14-1D   Reserved (for Robustness Experiment)

5	05	Redirect			30	  1E	   Traceroute

6	06	Alternate Host Address	31	  1F	   Datagram Conversion Error

7	07	Unassigned			32	  20	   Mobile Host Redirect

8	08	Echo				33	  21	   IPv6 Where-Are-You

9	09	Router Advertisement		34	  22	   IPv6 I-Am-Here

10	0A	Router Solicitation		35	  23	   Mobile Registration Request

11	0B	Time Exceeded		36	  24	   Mobile Registration Reply

12	0C	Parameter Problem		37	  25	   Domain Name Request

13	0D	Timestamp			38	  26	   Domain Name Reply

14	0E	Timestamp Reply		39	  27	   SKIP

15	0F	Information Request		40	  28	   Photuris

41-255	  29-FF Reserved

Data value: 8 (Echo (ping) Request)

Data values in other bases:

| Hexadecimal | 0 | 8 |
| --- | --- | --- |
| Binary | 0000 | 1000 |
| Decimal | 8 |

RFC Link: http://www.iana.org/assignments/icmp-parameters

Programming Hint: The name for this variable in code will be IP_ICMP_Type_ICMP.

IP > ICMP Header > Code for the selected ICMP PDU

Field Name:  Code

Purpose and Definition: Code is an 8-bit field that provides further information about the associated type field.

Field Key:

Type     Name					Type     Name

0             Echo Reply (used by “PING”)			   7            Unassigned

0     No Code			    	   8            Echo (used by "PING")

1             Unassigned 					    0     No Code

2             Unassigned				   9            Router Advertisement

3             Destination Unreachable 			                       0    No Code

0     Net Unreachable			  10           Router Selection

1     Host Unreachable				     0    No Code

2     Protocol Unreachable			  11           Time Exceeded

3     Port Unreachable				     0    Time to Live exceeded in Transit

- Fragmentation needed and 			     1    Fragment Reassembly Time Exceeded

Don't Fragment was Set			  12            Parameter Problem

5     Source Route Failed				     0    Pointer indicates the error

6     Destination Network Unknown			     1    Missing a Required Option

7     Destination Host Unknown			     2    Bad Length

8     Source Host Isolated			  13           Timestamp

- Communication with Destination		  	     0    No Code

Network is Administratively Prohibited	  14           Timestamp Reply

- Communication with Destination		  	     0    No Code

Host is Administratively Prohibited		  15           Information Request

- Destination Network Unreachable		  	     0    No Code

for Type of Service                                               16           Information Reply

- Destination Host Unreachable for 		  	     0    No Code

Type of Service			  17           Address Mask Request

4            Source Quench                           			  	     0    No Code

0     No Code				  18           Address Mask Reply

5            Redirect                                 			  	    0     No Code

0    Redirect Datagram for the Network		  19           Reserved (for Security)

1    Redirect Datagram for the Host		  20-29   Reserved (for Robustness Experiment)

2    Redirect Datagram for the Type of 		  30        Traceroute

Service and Network			  31        Datagram Conversion Error

- Redirect Datagram for the Type of		  32        Mobile Host Redirect

Service and Host			  33        IPv6 Where-Are-You

6            Alternate Host Address 			  34        IPv6 I-Am-Here

0    Alternate Address for Host		  35        Mobile Registration Request

36        Mobile Registration Reply

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |
| Decimal | 0 |
| ASCII | © |

Programming Hint: The name for this variable in code will be IP_ICMP_Header_ICMP.

IP > ICMP Header > Checksum for the selected ICMP PDU

Field Name:  Checksum

Purpose and Definition:  The checksum is the 16-bit one’s complement of the one’s complement sum of the ICMP message, starting with the ICMP type.  For computing the checksum, the checksum field should initially be zero.

Field Key:  Not applicable

Data value (hexadecimal): C9 15

Data values in other bases:

| Hexadecimal | C | 9 | 1 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 1100 | 1001 | 0001 | 0101 |
| Decimal | 201 | 21 |
| ASCII |  | © |

Programming Hint: The name for this variable in code will be IP_ICMP_Checksum_ICMP.

IP > ICMP Header > Identifier for the selected ICMP PDU

Field Name:  Identifier

Purpose and Definition:  The identifier is a 16-bit field that is used in matching echoes and replies for when the code field is zero.

Field Key:  Not applicable

Data value (hexadecimal): 70 60

Data values in other bases:

| Hexadecimal | 7 | 0 | 6 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 0000 | 0110 | 0000 |
| Decimal | 112 | 96 |
| ASCII | P | ‘ |

Programming Hint: The name for this variable in code will be IP_ICMP_Identifier_ICMP.

IP > ICMP Header > Sequence for the selected ICMP PDU

Field Name:  Sequence

Purpose and Definition:  The sequence is a 16-bit field that is used in matching echoes and replies for when the code field is zero.

Field Key:  Not applicable

Data value (hexadecimal): 70 60

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |
| Decimal | 0 | 0 |
| ASCII | © | © |

Programming Hint: The name for this variable in code will be IP_ICMP_Sequence_ICMP

IP > ICMP Header > Data for the selected ICMP PDU

Field Name:  Data

Purpose and Definition:  The data is a variable-length field that contains the actual information that is sent in the ping packet.

Field Key:  Not applicable

Data value (hexadecimal): 42 B1 89 3F 00 00 00 00 2C C6 07 00 00 00 00 00 10 11 12 13 14 15 16 17 18 19 1A 1B 1C 1D 1E 1F 20 21 22 23 24 25 26 27 28 29 2A 2B 2C 2D 2E 2F 30 31 32 33 34 35 36 37

Data values in other bases:

| Hexadecimal | 4 | 2 | B | 1 | 8 | 9 | 3 | F | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0010 | 1011 | 0001 | 1000 | 1001 | 0011 | 1111 | 0000 | 0000 |
| Decimal | 66 | 177 | 137 | 63 | 0 |
| ASCII | B |  |  | ? | © |

| Hexadecimal | 0 | 0 | 0 | 0 | 0 | 0 | 2 | C | C | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0010 | 1100 | 1100 | 0110 |
| Decimal | 0 | 0 | 0 | 44 | 198 |
| ASCII | © | © | © | , |  |

| Hexadecimal | 0 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0111 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 |
| Decimal | 7 | 0 | 0 | 0 | 0 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 2 | 1 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0000 | 0001 | 0001 | 0001 | 0010 | 0001 | 0011 |
| Decimal | 0 | 16 | 17 | 18 | 19 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 1 | 4 | 1 | 5 | 1 | 6 | 1 | 7 | 1 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0001 | 0100 | 0001 | 0101 | 0001 | 0110 | 0001 | 0111 | 0001 | 1000 |
| Decimal | 20 | 21 | 22 | 23 | 24 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 1 | 9 | 1 | A | 1 | B | 1 | C | 1 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0001 | 1001 | 0001 | 1010 | 0001 | 1011 | 0001 | 1100 | 0001 | 1101 |
| Decimal | 25 | 26 | 27 | 28 | 29 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 1 | E | 1 | F | 2 | 0 | 2 | 1 | 2 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0001 | 1110 | 0001 | 1111 | 0010 | 0000 | 0010 | 0001 | 0010 | 0010 |
| Decimal | 30 | 31 | 32 | 33 | 34 |
| ASCII | © | © | SPACE | ! | “ |

| Hexadecimal | 2 | 3 | 2 | 4 | 2 | 5 | 2 | 6 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0011 | 0010 | 0100 | 0010 | 0101 | 0010 | 0110 | 0010 | 0111 |
| Decimal | 35 | 36 | 37 | 38 | 39 |
| ASCII | # | $ | % | & | ‘ |

| Hexadecimal | 2 | 8 | 2 | 9 | 2 | A | 2 | B | 2 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1000 | 0010 | 1001 | 0010 | 1010 | 0010 | 1011 | 0010 | 1100 |
| Decimal | 40 | 41 | 42 | 43 | 44 |
| ASCII | ( | ) | * | + | , |

| Hexadecimal | 2 | D | 2 | E | 2 | F | 3 | 0 | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1101 | 0010 | 1110 | 00010 | 1111 | 0011 | 0000 | 0011 | 0001 |
| Decimal | 45 | 46 | 47 | 48 | 49 |
| ASCII | - | . | / | 0 | 1 |

| Hexadecimal | 3 | 2 | 3 | 3 | 3 | 4 | 3 | 5 | 3 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0010 | 0011 | 0011 | 0011 | 0100 | 0011 | 0101 | 0011 | 0110 |
| Decimal | 50 | 51 | 52 | 53 | 54 |
| ASCII | 2 | 3 | 4 | 5 | 6 |

| Hexadecimal | 3 | 7 |
| --- | --- | --- |
| Binary | 0011 | 0111 |
| Decimal | 55 |
| ASCII | 7 |

Programming Hint: The name for this variable in code will be IP_ICMP_Data_ICMP.

2.2.6 IP PDU for the selected SMTP PDU

IP PDU > IP Version for the selected SMTP PDU

Field Name: IP Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be IP_IPVersion_SMTP.

IP PDU > Internet Header Length for the selected SMTP PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4-bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |
| Decimal | 5 |

Programming Hint: The name for this variable in code will be IP_IHL_SMTP.

IP PDU > Type of Service for the selected SMTP PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 00

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |
| Decimal | 00 |

Programming Hint: The name for this variable in code will be IP_TypeOfService_SMTP.

IP PDU > Total Length of Ethernet Frame for the selected SMTP PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key:  Not applicable

Data values (hexadecimal):  02 12

Data values in other bases:

| Hexadecimal | 0 | 2 | 1 | 2 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0010 | 0001 | 0010 |
| Decimal | 2 | 18 |
| ASCII | © | © |

Programming Hint: The name for this variable in code will be IP_TotalLength_SMTP.

IP PDU > Identification for the selected SMTP PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet.

Field Key:  Not applicable

Data value (hexadecimal): 6128

Data values in other bases:

| Hexadecimal | 6 | 1 | 2 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0110 | 0001 | 0010 | 1000 |

Programming Hint: The name for this variable in code will be IP_Idenfification_SMTP.

IP PDU > Flags for the selected SMTP PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 0100

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_Flags_SMTP.

IP PDU > Fragment Offset for the selected SMTP PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0000 0000 0000

Programming Hint: The name for this variable in code will be IP_FragmentOffset_SMTP.

IP PDU > Time to Live for the selected SMTP PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_SMTP.

IP PDU > Protocol for the selected SMTP PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	  Protocol

0 	  00	Reserved					22		16	  Multiplexing

1 	  01	ICMP						23		17	  DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	  SATNET and Backroom EXPAK

6	  06	TCP						101		65	  MIT Subnet Support

7	  07	UCL						102-104	66-68	  Unassigned

10	  0A	Unassigned					105		69	   SATNET Monitoring

11	  0B	Secure						106		6A	  Unassigned

12	  0C	BBN RCC Monitoring			107		6B	  Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	  Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	10	Telnet						116		74	   WIDEBAND Monitoring

17	11	XNET						117		75	  WIDEBAND EXPAK

20	14	Chaos						120-376	78-0178  Unassigned

21	15	User Datagram				377		0179	    Reserved

Data value (hexadecimal): 06

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |
| Decimal | 6 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming Hint: The name for this variable in code will be IP_Protocol_SMTP.

IP PDU > Header Checksum for the selected SMTP PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): F1 F3

Data values in other bases:

| Hexadecimal | F | 1 | F | 3 |
| --- | --- | --- | --- | --- |
| Binary | 1111 | 0001 | 1111 | 0011 |

Programming Hint: The name for this variable in code will be IP_HeaderChecksum_SMTP.

IP PDU > Source Address for the selected SMTP PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 1 | 0 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0001 | 0010 | 0001 |
| Decimal | 192 | 168 | 101 |

Programming Hint: The name for this variable in code will be IP_SourceAddress_SMTP.

IP PDU > Destination Address for the selected SMTP PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key: Not applicable

Data value (decimal):  192.168.100.20

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192 | 168 | 100 | 20 |

Programming Hint: The name for this variable in code will be IP_DestinationAddress_SMTP.

IP PDU > Options and Padding for the selected SMTP PDU

Field Name:  Options and Padding

Purpose and Definition:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Field Key:  Not applicable

Data values:  Not applicable

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_OptionsPadding_SMTP.

IP PDU > Data for the selected SMTP PDU

Field Name:  Data

Purpose and Definition:  The Data is a variable length field which contains the actual data that is being sent from one host to another.  The data field may start with a Layer 4 header, which will give additional instructions to the application that will be receiving the data; alternately, it may be an ICMP header and not contain any user data at all.

Field Key:  Not applicable

Data values (hexadecimal) :  (TCP) 0D 0A 2D 2D 2D 31 34 36 33 37 38 36 32 34 30 2D 37 32 33 37 38 33 33 32 38 2D 31 30 36 37 36 33 34 33 35 30 3D 3A 32 36 36 30 36 0D 0A 43 6F 6E 74 2D 54 79 70 65 3A 20 54 45 58 54 2F 70 6C 61 69 6E 3B 20 6E 61 6D 65 3D 22 6D 69 6d 65 74 65 73 74 2E 74 78 74 22 0D 0A 43 6F 6E 74 65 6E 74 2D 54 72 61 6E 73 66 65 72 2D 45 6E 63 6F 64 69 6E 67 3A 20 42 41 53 45 36 34 0D 0A 43 6F 6E 74 65 6E 74 2D 49 44 3A 20 3C 50 69 6E 65 2E 4C 4E 58 2E 34 2E 32 31 2E 32 31 2E 30 33 31 31 36 30 35 35 30 30 2E 32 36 36 30 36 40 63 62 31 31 38 6B 73 2E 63 73 2E 73 69 65 6E 61 2E 65 64 75 3E 0D 0A 43 6F 6E 74 65 6E 74 2D 44 65 73 63 72 69 70 74 69 6F 6E 3A 20 0D 0A 43 6F 6E 74 65 6E 74 2D 44 69 73 70 6F 73 69 74 69 6F 6E 3A 20 61 74 74 61 63 68 6D 65 6E 74 3B 20 66 69 6C 65 6E 61 6D 65 3D 22 6D 69 6D 65 74 65 73 74 2E 74 78 74 22 0D 0A 0D 0A 56 47 68 70 63 79 42 70 63 79 42 30 61 47 55 67 62 57 56 7A 63 32 46 6E 5A 53 42 30 61 47 46 30 49 48 64 70 62 47 77 67 59 57 78 73 62 33 63 67 64 58 4D 67 64 47 38 67 5A 47 6C 7A 0D 0A 63 47 78 68 65 53 42 33 61 58 52 6F 49 45 56 30 61 47 56 79 5A 57 46 73 49 41 30 4B 59 53 42 4E 53 55 31 46 49 47 46 30 64 47 46 6A 61 47 31 6C 62 6E 51 57 61 57 35 7A 61 57 52 6C 0D 0A 49 47 46 75 49 46 4E 4E 56 46 41 67 5A 6E 4A 68 62 57 55 75 44 51 6F 3D 0D 0A 2D 2D 2D 31 34 36 33 37 38 36 32 34 30 2D 37 32 33 37 38 33 33 32 38 2D 31 30 36 37 36 33 34 33 35 30 3D 3A 32 36 36 30 36 2D 2D 0D 0A 2E 0D 0A

Programming Hint: The name for this variable in code will be IP_Data_SMTP.

2.2.7 TCP PDU for the selected SMTP PDU

IP > TCP PDU > Source Port for the selected SMTP PDU

Field Name:  Source Port

Purpose and Definition:

This 16-bit number represents the name of the application that sent the data in the IP packet.

Field Key:  Not applicable

Data value (decimal): 3651

Data values in other bases:

| Hexadecimal | 0 | D | E | 9 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 1101 | 1110 | 1001 |
| Decimal | 13 | 233 |
| ASCII | /n |  |

Programming Hint: The name for this variable in code will be IP_TCP_SourcePort_SMTP.

IP > TCP PDU > Destination Port for the selected SMTP PDU

Field Name: Destination Port

Purpose and Definition: 
This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

Field Key:

This key indicates assigned port number values:

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (decimal): 25 (indicates SMTP)

Data values in other bases:

| Hexadecimal | 0 | 0 | 1 | 9 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 1001 |
| Decimal | 0 | 25 |
| ASCII | © | © |

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

Programming Hint: The name for this variable in code will be IP_TCP_DestinationPort_SMTP.

IP > TCP PDU > Sequence Number for the selected SMTP PDU

Field Name:  Sequence Number

Purpose and Definition: 
TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Field Key:  Not applicable

Data value (decimal): 2069207327

Data values in other bases:

| Hexadecimal | 7 | B | 5 | 5 | 9 | 9 | 1 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 1011 | 0101 | 0101 | 1001 | 1001 | 0001 | 1111 |
| Decimal | 123 | 85 | 153 | 31 |
| ASCII | { | U |  | © |

Programming Hint: The name for this variable in code will be IP_TCP_SequenceNumber_SMTP.

IP > TCP PDU > Acknowledgement Number for the selected SMTP PDU

Field Name: Acknowledgement Number

Purpose and Definition: 
This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Field Key:  Not applicable

Data value (decimal): 3827794966

Data values in other bases:

| Hexadecimal | E | 4 | 2 | 7 | 8 | 4 | 1 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1110 | 0100 | 0010 | 0111 | 1000 | 0100 | 0001 | 0110 |
| Decimal | 228 | 39 | 132 | 22 |
| ASCII |  | ' |  | © |

Programming Hint: The name for this variable in code will be IP_TCP_AcknowledgementNumber_SMTP.

IP > TCP PDU > Header Length or Offset for the selected SMTP PDU

Field Name:  Header Length or Offset

Purpose and Definition: 
This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header.

Field Key:  Not applicable

Data value (bytes): 32

Data values in other bases:

| Hexadecimal | 8 | 0 |
| --- | --- | --- |
| Binary | 1000 | 0000 |
| Decimal | 128 |
| ASCII |  |

Programming Hint: The name for this variable in code will be IP_TCP_HeaderLength_SMTP.

IP > TCP PDU > Reserved for the selected SMTP PDU

Field Name:  Reserved

Purpose and Definition: 
These 6 bits are unused and are always set to 0.

Field Key:  Not applicable

Data value (binary): 0000 00

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 |
| Decimal | 0 | 0 | 0 |
| ASCII | © | © | © |

Programming Hint: The name for this variable in code will be IP_TCP_Reserved_SMTP

IP > TCP PDU > Control Flags for the selected SMTP PDU

Field Name:  Control Flags

Purpose and Definition: 
Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:

- Urgent (URG)

- Acknowledgement (ACK)

- Push (PSH)

- Reset (RST)

- Synchronize (SYN)

- Finish (FIN)

Data value (binary): 0001 1000

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_TCP_ControlFlags_SMTP.

IP > TCP PDU > Window Size for the selected SMTP PDU

Field Name:  Window Size

Purpose and Definition:
Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:  Not applicable

Data value (decimal): 32120

Data values in other bases:

| Hexadecimal | 7 | D | 7 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 1101 | 0111 | 1000 |
| Decimal | 125 | 120 |
| ASCII | } | x |

Programming Hint: The name for this variable in code will be IP_TCP_WindowSize_SMTP.

IP > TCP PDU > Checksum for the selected SMTP PDU

Field Name:  Checksum

Purpose and Definition: 
Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Field Key:  Not applicable

Data value (hexadecimal): 72 B5

Data values in other bases:

| Hexadecimal | 7 | 2 | B | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 1011 | 0101 |
| Decimal | 114 | 181 |
| ASCII | r |  |

Programming Hint: The name for this variable in code will be IP_TCP_Checksum_SMTP.

IP > TCP PDU > Urgent Pointer for the selected SMTP PDU

Field Name: Urgent Pointer

Purpose and Definition: 
If the Urgent flag is set to on, this value indicates where the urgent data is located.

Information Key:  Not applicable

Data value:  Not applicable

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_TCP_UrgentPointer_SMTP.

IP > TCP PDU > Options and Padding for the selected SMTP PDU

Field Name: Options and Padding

Purpose and Definition: 
Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits.

Field Key:  Not applicable

Data value (hexadecimal): 01 01 08 0A 07 AE F6 75 00 21 66 A4

Data values in other bases:

| Hexadecimal | 0 | 1 | 0 | 1 | 0 | 8 | 0 | A | 0 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0001 | 0000 | 0001 | 0000 | 1000 | 0000 | 1010 | 0000 | 0111 |
| Decimal | 1 | 1 | 8 | 10 | 7 |
| ASCII | © | © | © | © | © |

| Hexadecimal | A | E | F | 6 | 7 | 5 | 0 | 0 | 2 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1010 | 1110 | 1111 | 0110 | 0111 | 0101 | 0000 | 0000 | 0010 | 0001 |
| Decimal | 174 | 246 | 117 | 0 | 33 |
| ASCII |  |  | u | © | ! |

| Hexadecimal | 6 | 6 | A | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0101 | 0011 | 0101 | 1000 |
| Decimal | 102 | 164 |
| ASCII | f |  |

Programming Hint: The name for this variable in code will be IP_TCP_OptionsPadding_SMTP.

2.2.8 SMTP PDU for the selected SMTP PDU

IP > SMTP Header > Command for the selected SMTP PDU

RFC Link:  http://www.ietf.org/rfc/rfc0821.txt?number=821

Field Name:  Command

Purpose and Definition:  ASCII messages sent between SMTP hosts.

Field Key:

| Command | Description |
| --- | --- |
| DATA | Begins message composition. |
| EXPN <string> | Returns names on the specified mail list. |
| HELO <domain> | Returns identity of mail server. |
| HELP <command> | Returns information on the specified command. |
| MAIL FROM <host> | Initiates a mail session from host. |
| NOOP | Causes no action, except acknowledgement from server. |
| QUIT | Terminates the mail session. |
| RCPT TO <user> | Designates who receives mail. |
| RSET | Resets mail connection. |
| SAML FROM <host> | Sends mail to user terminal and mailbox. |
| SEND FROM <host> | Sends mail to user terminal. |
| SOML FROM <host> | Sends mail to user terminal or mailbox. |
| TURN | Switches role of receiver and sender. |
| VRFY <user> | Verifies the identity of a user. |

Data value: Content_TEXT\Plain;name=”mimetest.txt”

Data values in other bases:

| Hexadecimal | 4 | 3 | 6 | F | 6 | E | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0011 | 0110 | 1111 | 0110 | 1110 | 0111 | 0100 |
| Decimal | 67 | 111 | 110 | 116 |
| ASCII | C | o | n | t |

| Hexadecimal | 6 | 5 | 6 | E | 7 | 4 | 2 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 1110 | 0111 | 0100 | 0010 | 1101 |
| Decimal | 101 | 110 | 116 | 45 |
| ASCII | e | n | t | - |

| Hexadecimal | 5 | 4 | 4 | 5 | 5 | 8 | 5 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0100 | 0100 | 0101 | 0101 | 1000 | 0101 | 0100 |
| Decimal | 84 | 69 | 88 | 84 |
| ASCII | T | E | X | T |
| Hexadecimal | 2 | F | 5 | 0 | 6 | C | 6 | 1 |
| Binary | 0010 | 1111 | 0101 | 0000 | 0110 | 1100 | 0110 | 0001 |
| Decimal | 47 | 80 | 108 | 97 |
| ASCII | / | P | l | a |

| Hexadecimal | 6 | 9 | 6 | E | 3 | B | 6 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0110 | 1110 | 0011 | 1011 | 0110 | 1001 |
| Decimal | 105 | 110 | 59 | 110 |
| ASCII | i | n | ; | n |

| Hexadecimal | 6 | 1 | 6 | D | 6 | 5 | 3 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0001 | 0110 | 1101 | 0110 | 0101 | 0011 | 1101 |
| Decimal | 97 | 109 | 101 | 61 |
| ASCII | a | m | e | = |

| Hexadecimal | 2 | 0 | 6 | 3 | 6 | 8 | 6 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 0011 | 0110 | 1000 | 0110 | 0001 |
| Decimal | 32 | 99 | 104 | 97 |
| ASCII | “ | M | I | m |

| Hexadecimal | 2 | 2 | 7 | 4 | 6 | 5 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0010 | 0111 | 0100 | 0110 | 0101 | 0111 | 0011 |
| Decimal | 34 | 116 | 101 | 115 |
| ASCII | e | t | e | s |

| Hexadecimal | 7 | 4 | 2 | E | 7 | 4 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0100 | 0010 | 1110 | 0111 | 0100 | 0111 | 1000 |
| Decimal | 116 | 46 | 116 | 120 |
| ASCII | t | . | t | x |

| Hexadecimal | 7 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 0100 | 0010 | 0000 |
| Decimal | 116 | 32 |
| ASCII | t | “ |

Programming Hint: The name for this variable in code will be IP_SMTP_Command_SMTP.

IP > SMTP Header > Message for the selected SMTP PDU

Field Name:  Message

Purpose and Definition:  Response messages consist of a response code followed by explanatory text

Field Key:

| Response Code | Explanatory Text |
| --- | --- |
| 211 | (Response to system status or help request). |
| 214 | (Response to help request). |
| 220 | Mail service ready. |
| 221 | Mail service closing connection. |
| 250 | Mail transfer completed. |
| 251 | User not local, forward to <path>. |
| 354 | Start mail message, end with <CRLF><CRLF>. |
| 421 | Mail service unavailable. |
| 450 | Mailbox unavailable. |
| 451 | Local error in processing command. |
| 452 | Insufficient system storage. |
| 500 | Unknown command. |
| 501 | Bad parameter. |
| 502 | Command not implemented. |
| 503 | Bad command sequence. |
| 504 | Parameter not implemented. |
| 550 | Mailbox not found. |
| 551 | User not local, try <path>. |
| 552 | Storage allocation exceeded. |
| 553 | Mailbox name not allowed. |
| 554 | Mail transaction failed. |

Data value: Not applicable.

Programming Hint: The name for this variable in code will be IP_SMTP_Command_SMTP.

2.2.9 IP PDU for the selected UDP PDU

IP PDU > IP Version for the selected UDP PDU

Field Name: IP Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be IP_IPVersion_UDP.

IP PDU > Internet Header Length for the selected UDP PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4-bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |
| Decimal | 5 |

Programming Hint: The name for this variable in code will be IP_IHL_UDP.

IP PDU > Type of Service for the selected UDP PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 10

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |
| Decimal | 16 |

Programming Hint: The name for this variable in code will be IP_TypeOfService_UDP.

IP PDU > Total Length of Ethernet Frame for the selected UDP PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key:  Not applicable

Data values (hexadecimal):  128

Data values in other bases:

| Hexadecimal | 0 | 1 | 2 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0001 | 0010 | 1000 |
| Decimal | 1 | 40 |
| ASCII ( |

Programming Hint: The name for this variable in code will be IP_TotalLength_UDP.

IP PDU > Identification for the selected UDP PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet.

Field Key:  Not applicable

Data value (hexadecimal): BBD7

Data values in other bases:

| Hexadecimal | B | B | D | 7 |
| --- | --- | --- | --- | --- |
| Binary | 1011 | 1011 | 1101 | 0111 |

Programming Hint: The name for this variable in code will be IP_Idenfification_UDP.

IP PDU > Flags for the selected UDP PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 0000

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_Flags_UDP.

IP PDU > Fragment Offset for the selected UDP PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0000 0000

Programming Hint: The name for this variable in code will be IP_FragmentOffset_UDP.

IP PDU > Time to Live for the selected UDP PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_UDP.

IP PDU > Time to Live for the selected UDP PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 60

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 60 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_UDP.

IP PDU > Protocol for the selected UDP PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	 10	Telnet						116		74	   WIDEBAND Monitoring

17	 11	XNET						117		75	   WIDEBAND EXPAK

20	 14	Chaos						120-376	78-0178  Unassigned

21	 15	User Datagram				377		0179	    Reserved

Data value (hexadecimal): 11

Data values in other bases:

| Hexadecimal | 1 | 1 |
| --- | --- | --- |
| Binary | 0001 | 0001 |
| Decimal | 17 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming Hint: The name for this variable in code will be IP_Protocol_UDP

IP PDU > Header Checksum for the selected UDP PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): 3F 47

Data values in other bases:

| Hexadecimal | 3 | F | 4 | 7 |
| --- | --- | --- | --- | --- |
| Binary | 0011 | 1111 | 0100 | 0111 |

Programming Hint: The name for this variable in code will be IP_HeaderChecksum_UDP.

IP PDU > Source Address for the selected UDP PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value (decimal):  192.168.0.71

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 4 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0100 | 0111 |
| Decimal | 192 | 168 | 0 | 71 |

Programming Hint: The name for this variable in code will be IP_SourceAddress_UDP.

IP PDU > Destination Address for the selected UDP PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key: Not applicable

Data value (decimal):  192.168.0.255

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | F | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 1111 | 1111 |
| Decimal | 192 | 168 | 0 | 255 |

Programming Hint: The name for this variable in code will be IP_DestinationAddress_UDP.

IP PDU > Options and Padding for the selected UDP PDU

Field Name:  Options and Padding

Purpose and Definition:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Field Key:  Not applicable

Data values:  Not applicable

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_OptionsPadding_UDP.

IP PDU > Data for the selected UDP PDU

Field Name:  Data

Purpose and Definition:  The Data is a variable length field which contains the actual data that is being sent from one host to another.  The data field may start with a Layer 4 header, which will give additional instructions to the application that will be receiving the data; alternately, it may be an ICMP header and not contain any user data at all.

Field Key:  Not applicable

Data values (hexadecimal) :  (UDP) FF FF FF FF FF FF 08 00 69 07 9A C5 08 00 45 10

01 28 BB D7 00 00 3C 11 3F 47 C0 A8 00 47 C0 A8 00 FF 02 0D 01 14 E9 DB 18 01 C2 5A 0A FF 13 D0 00 00 00 00 69 6E 64 79 00 00 00 00 7F FF 11 DB 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 13 F0 00 00 00 00 7F FF 11 F6 00 00 00 00 00 00 00 00 00 00 00 00 7F FF FF FF 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 17 E3 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 10 05 9D D8 00 00 00 00 10 00 DB A8 00 00 00 00 0F B5 B1 74 00 00 00 00 0F AB 01 C8 00 00 00 00 10 05 9D F8 00 00 00 00 0F B5 9D D8 00 00 00 00 10 05 9D FC 00 00 00 00 0F B5 B1 74 00 00 00 00 10 05 9B 18 00 00 00 00 0F AB 02 80 00 00 00 00 00 00 00 00 00 00 00 00 00 00

Data values in other bases:

ASCII:  (UDP) ( Extended ASCII

Programming Hint: The name for this variable in code will be IP_Data_UDP.

IP PDU > Source Port for the selected UDP PDU

RFC Link: http://www.ietf.org/rfc/rfc0768.txt?number=768

Field Name: Source Port

Purpose and Definition:  Source Port is an optional field, when meaningful, it indicates the port of the sending  process,  and may be assumed  to be the port  to which a  reply should  be addressed  in the absence of any other information.  If not used, a value of zero is inserted.

Field Key:  Not applicable

Data value (decimal): 525

Data values in other bases:

| Hexadecimal | 02 | 0D |
| --- | --- | --- |
| Binary | 0010 | 1101 |
| Decimal | 525 |

Programming Hint: The name for this variable in code will be IP_SourcePort_UDP.

IP PDU > Destination Port for the selected UDP PDU

Field Name: Destination Port

Purpose and Definition:  Destination Port has a meaning within the context of a particular internet destination address.

Field Key:  Not applicable

Data value (decimal): 525

Data values in other bases:

| Hexadecimal | 02 | 0D |
| --- | --- | --- |
| Binary | 0010 | 1101 |
| Decimal | 525 |

Programming Hint: The name for this variable in code will be IP_DestinationPort_UDP.

IP PDU > Length for the selected UDP PDU

Field Name: Length

Purpose and Definition:  Length is the length in octets of this user datagram including this header and the data (This means the minimum value of the length is eight).

Field Key:  Not applicable

Data value (decimal): 276

Data values in other bases:

| Hexadecimal | 01 | 14 |
| --- | --- | --- |
| Binary | 0001 | 00001 0100 |
| Decimal | 276 |

Programming Hint: The name for this variable in code will be IP_Length_UDP.

IP PDU > Checksum for the selected UDP PDU

Field Name: Checksum

Purpose and Definition:  Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the UDP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.

Field Key:  Not applicable

Data value (decimal): E9 DB

Data values in other bases:

| Hexadecimal | E | 9 | D | B |
| --- | --- | --- | --- | --- |
| Binary | 1110 | 1001 | 1101 | 1011 |

Programming Hint: The name for this variable in code will be IP_Checksum_UDP.

IP PDU > Data for the selected UDP PDU

Field Name: Data

Purpose and Definition:

Field Key:  Not applicable

Data value (hexadecimal): 18 01 C2 5A 0A FF 13 D0 00 00 00 00 69 6E 64 79 00 00 00 00 7F FF 11 DB 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 13 F0 00 00 00 00 7F FF 11 F6 00 00 00 00 00 00 00 00 00 00 00 00 7F FF FF FF 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 17 E3 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 10 05 9D D8 00 00 00 00 10 00 DB A8 00 00 00 00 0F B5 B1 74 00 00 00 00 0F AB 01 C8 00 00 00 00 10 05 9D F8 00 00 00 00 0F B5 9D D8 00 00 00 00 10 05 9D FC 00 00 00 00 0F B5 B1 74 00 00 00 00 10 05 9B 18 00 00 00 00 0F AB 02 80 00 00 00 00 00 00 00 00 00 00 00 00 00 00

Data values in other bases:

(ASCII): ( Extended ASCII

Programming Hint: The name for this variable in code will be IP_Data_UDP.

2.2.10 UDP PDU for the selected UDP PDU

IP > UDP Header> Source Port for the selected UDP PDU

RFC Link: http://www.ietf.org/rfc/rfc0768.txt?number=768

Field Name: Source Port

Purpose and Definition:  Source Port is an optional field, when meaningful, it indicates the port of the sending  process,  and may be assumed  to be the port  to which a  reply should  be addressed  in the absence of any other information.  If not used, a value of zero is inserted.

Field Key:  Not applicable

Data value (decimal): 525

Data values in other bases:

| Hexadecimal | 02 | 0D |
| --- | --- | --- |
| Binary | 0010 | 1101 |
| Decimal | 525 |

Programming Hint: The name for this variable in code will be IP_SourcePort_UDP.

IP > UDP Header > Destination Port for the selected UDP PDU

Field Name: Destination Port

Purpose and Definition:  Destination Port has a meaning within the context of a particular internet destination address.

Field Key:  Not applicable

Data value (decimal): 525

Data values in other bases:

| Hexadecimal | 02 | 0D |
| --- | --- | --- |
| Binary | 0010 | 1101 |
| Decimal | 525 |

Programming Hint: The name for this variable in code will be IP_DestinationPort_UDP.

IP > UDP Header> Length for the selected UDP PDU

Field Name: Length

Purpose and Definition:  Length is the length in octets of this user datagram including this header and the data (This means the minimum value of the length is eight).

Field Key:  Not applicable

Data value (decimal): 276

Data values in other bases:

| Hexadecimal | 01 | 14 |
| --- | --- | --- |
| Binary | 0001 | 00001 0100 |
| Decimal | 276 |

Programming Hint: The name for this variable in code will be IP_Length_UDP.

IP > UDP Header > Checksum for the selected UDP PDU

Field Name: Checksum

Purpose and Definition:  Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the UDP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.

Field Key:  Not applicable

Data value (decimal): E9 DB

Data values in other bases:

| Hexadecimal | E | 9 | D | B |
| --- | --- | --- | --- | --- |
| Binary | 1110 | 1001 | 1101 | 1011 |

Programming Hint: The name for this variable in code will be IP_Checksum_UDP.

IP > UDP Header > Data for the selected UDP PDU

Field Name: Data

Purpose and Definition:

Field Key:  Not applicable

Data value (hexadecimal): 18 01 C2 5A 0A FF 13 D0 00 00 00 00 69 6E 64 79 00 00 00 00 7F FF 11 DB 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 13 F0 00 00 00 00 7F FF 11 F6 00 00 00 00 00 00 00 00 00 00 00 00 7F FF FF FF 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 17 E3 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 10 05 9D D8 00 00 00 00 10 00 DB A8 00 00 00 00 0F B5 B1 74 00 00 00 00 0F AB 01 C8 00 00 00 00 10 05 9D F8 00 00 00 00 0F B5 9D D8 00 00 00 00 10 05 9D FC 00 00 00 00 0F B5 B1 74 00 00 00 00 10 05 9B 18 00 00 00 00 0F AB 02 80 00 00 00 00 00 00 00 00 00 00 00 00 00 00

Data values in other bases:

(ASCII): ( Extended ASCII

Programming Hint: The name for this variable in code will be IP_Data_UDP.

2.2.11 IP PDU for the selected SNMP PDU

IP PDU > IP Version for the selected SNMP PDU

Field Name: IP Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be IP_IPVersion_SNMP.

IP PDU > Internet Header Length for the selected SNMP PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4-bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |
| Decimal | 5 |

Programming Hint: The name for this variable in code will be IP_IHL_SNMP.

IP PDU > Type of Service for the selected SNMP PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 10

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |
| Decimal | 16 |

Programming Hint: The name for this variable in code will be IP_TypeOfService_SNMP.

IP PDU > Total Length of Ethernet Frame for the selected SNMP PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key:  Not applicable

Data values (decimal):  109

Data values in other bases:

| Hexadecimal | 6 | D |
| --- | --- | --- |
| Binary | 110 | 1101 |
| Decimal | 109 |

Programming Hint: The name for this variable in code will be IP_TotalLength_SNMP.

IP PDU > Identification for the selected SNMP PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet.

Field Key:  Not applicable

Data value (hexadecimal): D5 1A

Data values in other bases:

| Hexadecimal | D | 5 | 1 | A |
| --- | --- | --- | --- | --- |
| Binary | 1101 | 0101 | 0001 | 1010 |

Programming Hint: The name for this variable in code will be IP_Idenfification_SNMP.

IP PDU > Flags for the selected SNMP PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_Flags_SNMP.

IP PDU > Fragment Offset for the selected SNMP PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0000 0000 0000

Programming Hint: The name for this variable in code will be IP_FragmentOffset_SNMP.

IP PDU > Time to Live for the selected SNMP PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_SNMP.

IP PDU > Protocol for the selected SNMP PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	 10	Telnet						116		74	   WIDEBAND Monitoring

17	 11	XNET						117		75	   WIDEBAND EXPAK

20	 14	Chaos						120-376	78-0178  Unassigned

21	 15	User Datagram				377		0179	    Reserved

Data value (hexadecimal): 06

Data values in other bases:

| Hexadecimal | 1 | 1 |
| --- | --- | --- |
| Binary | 1 | 0001 |
| Decimal | 17 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming Hint: The name for this variable in code will be IP_Protocol_SNMP.

IP PDU > Header Checksum for the selected SNMP PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): 22 F0

Data values in other bases:

| Hexadecimal | 2 | 2 | F | 0 |
| --- | --- | --- | --- | --- |
| Binary | 10 | 0010 | 1111 | 0000 |

Programming Hint: The name for this variable in code will be IP_HeaderChecksum_SNMP

IP PDU > Source Address for the selected SNMP PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value (decimal):  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |
| Decimal | 192 | 168 | 0 | 39 |

Programming Hint: The name for this variable in code will be IP_SourceAddress_SNMP

.

IP PDU > Destination Address for the selected SNMP PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key: Not applicable

Data value (decimal):  192.168.0.143

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 8 | f |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 1000 | 1111 |
| Decimal | 192 | 168 | 0 | 143 |

Programming Hint: The name for this variable in code will be IP_DestinationAddress_SNMP

2.2.12 UDP PDU for the selected SNMP PDU

IP > UDP PDU > Source Port for the selected SNMP PDU

RFC Link: http://www.ietf.org/rfc/rfc0768.txt?number=768

Field Name: Source Port

Purpose and Definition:  Source Port is an optional field, when meaningful, it indicates the port of the sending  process,  and may be assumed  to be the port  to which a  reply should  be addressed  in the absence of any other information.  If not used, a value of zero is inserted.

Field Key:  Not applicable

Data value (decimal): 161

Data values in other bases:

| Hexadecimal | A | 1 |
| --- | --- | --- |
| Binary | 1010 | 0001 |
| Decimal | 161 |

Programming Hint: The name for this variable in code will be IP_SourcePort_UDP_SMNP.

IP > UDP PDU> Destination Port for the selected SNMP PDU

Field Name: Destination Port

Purpose and Definition:  Destination Port has a meaning within the context of a particular internet destination address.

Field Key:  Not applicable

Data value (decimal): 1034

Data values in other bases:

| Hexadecimal | 40 | 0A |
| --- | --- | --- |
| Binary | 0010 | 1101 |
| Decimal | 1034 |

Programming Hint: The name for this variable in code will be IP_DestinationPort_UDP_SMNP.

IP > UDP Length for the selected SNMP PDU

Field Name: Length

Purpose and Definition:  Length is the length in octets of this user datagram including this header and the data (This means the minimum value of the length is eight).

Field Key:  Not applicable

Data value (decimal): 89

Data values in other bases:

| Hexadecimal | 5 | 9 |
| --- | --- | --- |
| Binary | 0101 | 1001 |
| Decimal | 89 |

Programming Hint: The name for this variable in code will be IP_Length_UDP_SNMP.

IP > UDP PDU > Checksum for the selected SNMP PDU

Field Name: Checksum

Purpose and Definition:  Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the UDP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.

Field Key:  Not applicable

Data value (hexadecimal): 9A25

Data values in other bases:

| Hexadecimal | 9 | A | 2 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 1001 | 0000 | 0010 | 0101 |
| Decimal | 154 | 37 |

Programming Hint: The name for this variable in code will be IP_Checksum_UDP_SNMP.

IP > UDP PDU > Data for the selected SNMP PDU

Field Name: Data

Purpose and Definition:

Field Key:  Not applicable

Data value (hexadecimal): see SNMP

Data values in other bases:

(ASCII): ( Extended ASCII

Programming Hint: The name for this variable in code will be IP_Data_UDP_SNMP.

2.2.13 SNMP PDU for the selected SNMP PDU

IP > UDP > SNMP Header > Version for the selected SNMP PDU

Field Name:  Version

Purpose and Definition:  Version is a 6-bit field that indicates the format of the protocol

Field Key: Not applicable

Data value (hexadecimal):  02 01 00

Data values in other bases:

| Hexadecimal | 0 | 2 | 0 | 1 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0010 | 0000 | 0001 | 0000 | 0000 |
| Decimal | 2 | 1 | 0 |

Programming Hint: The name for this variable in code will be IP_UDP_SNMP_Version.

IP > UDP > SNMP Header > Community for the selected SNMP PDU

Field Name:  Community

Purpose and Definition:

Field Key:  	Public: all users

Private: Selected users

Data value:  The value contained in our field determines who view the information

Data values in other bases:

| Hexadecimal | 0 | 6 | 7 | 0 | 7 | 5 | 6 | 2 | 6 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0110 | 0111 | 0000 | 0111 | 0101 | 0110 | 0010 | 0110 | 1100 |
| Decimal | 1 | 1 | 8 | 10 | 7 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 6 | 9 | 6 | 3 |
| --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0110 | 0011 |
| Decimal | 105 | 99 |
| ASCII | i | c |

Programming Hint: The name for this variable in code will be IP_UDP_SNMP_Community.

IP > UDP > SNMP Header > PDU Type for the selected SNMP PDU

Field Name: PDU Type

Purpose and Definition: The type of data.

Field Key:  Not applicable

Data value (hexadecimal):  A2 42

Values in other bases:

| Hexadecimal | A | 2 | 4 | 2 |
| --- | --- | --- | --- | --- |
| Binary | 1010 | 0010 | 0100 | 0010 |
| Decimal | 162 | 66 |
| ASCII |  | B |

Programming Hint: The name for this variable in code will be IP_UDP_SNMP_PDUType

IP > UDP > SNMP Header > Request ID for the selected SNMP PDU

Field Name:  Request ID

Purpose and Definition: ID of the requester.

Field Key:  Not applicable

Data value (hexadecimal):  51 EB

Data values in other bases:

| Hexadecimal | 5 | 1 | E | B |
| --- | --- | --- | --- | --- |
| Binary | 0101 | 0001 | 1110 | 1011 |
| Decimal | 81 | 235 |
| ASCII | Q |  |

Programming Hint: The name for this variable in code will be IP_UDP_SNMP_Request.

IP > UDP > SNMP Header > Error Status for the selected SNMP PDU

Field Name:  Error Status

Purpose and Definition: If there is an error, it will show here

Field Key:  Not applicable.

Data value:  No error

Data values in other bases: Not applicable

Programming Hint: The name for this variable in code will be IP_UDP_SNMP_ErrorStatus.

IP > UDP > SNMP Header > Error ID for the selected SNMP PDU

Field Name:  Error Index

Purpose and Definition: How the error is defined.

Field Key: Not applicable.

Data value (hexadecimal):  02 01 00

Data values in other bases:

| Hexadecimal | 0 | 2 | 0 | 1 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0010 | 0000 | 0001 | 0000 | 0000 |
| Decimal | 2 | 1 | 0 |

Programming Hint: The name for this variable in code will be IP_UDP_SNMP_ErrorIndex.

IP > UDP > SNMP Header > Object ID for the selected SNMP PDU

Field Name:  Object ID

Purpose and Definition: How the packet is identified.

Field Key:  Not applicable

Data value:  1.3.6.1.2.1.25.3.5.1.1.1

Data values in other bases:

| Hexadecimal | 1 | 3 | 6 | 1 | 2 | 1 | 2 | 5 | 3 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0011 | 0110 | 0001 | 0010 | 0001 | 0010 | 0101 | 0011 | 0101 |
| Decimal | 1 | 3 | 6 | 1 | 2 | 1 | 37 | 3 | 5 |
| ASCII | © | © | © | © | © | © | % | © | © |

| Hexadecimal | 1 | 1 | 1 |
| --- | --- | --- | --- |
| Binary | 0001 | 0001 | 0001 |
| Decimal | 1 | 1 | 1 |
| ASCII | © | © | © |

Programming Hint: The name for this variable in code will be IP_UDP_SNMP_ObjectID

IP > UDP > SNMP Header > Value Integer for the selected SNMP PDU

Field Name:  Value Integer

Purpose and Definition: The size of the integer

Field Key:  Not applicable.

Data value (hexadecimal):  3

Data values in other bases:

| Hexadecimal | 3 |
| --- | --- |
| Binary | 11 |
| Decimal | 3 |

Programming Hint: The name for this variable in code will be IP_UDP_SNMP_Value_Integer

IP > UDP > SNMP Header > Object ID for the selected SNMP PDU

Field Name:  Object ID

Purpose and Definition: How the packet is identified.

Field Key:  Not applicable

Data value:  1.3.6.1.2.1.25.3.5.1.1.1

Data values in other bases:

| Hexadecimal | 1 3 6 1 2 1 25 3 5 1 1 1 |  |
| --- | --- | --- |
| Binary | 0001 0011 0110 0001 0010 0001 11001 0011 0101 0001 0001 0001 |  |
| Decimal | n/a |

Programming Hint: The name for this variable in code will be SNMP_Object Id

2.2.14 IP PDU for the TELNET PDU

IP PDU > IP Version for the selected TELNET PDU

Field Name: IP Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be IP_IPVersion_TELNET.

IP PDU > Internet Header Length for the selected TELNET PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4-bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 5 |
| --- | --- |
| Binary | 0101 |
| Decimal | 5 |

Programming Hint: The name for this variable in code will be IP_IHL_TELNET.

IP PDU > Type of Service for the selected TELNET PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 10

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |
| Decimal | 16 |

Programming Hint: The name for this variable in code will be IP_TypeOfService_TELNET.

IP PDU > Total Length of Ethernet Frame for the selected TELNET PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key:  Not applicable

Data values (decimal):  128

Data values in other bases:

| Hexadecimal | 8 | 0 |
| --- | --- | --- |
| Binary | 1000 | 0000 |
| Decimal | 128 |

Programming Hint: The name for this variable in code will be IP_TotalLength_TELNET.

IP PDU > Identification for the selected TELNET PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet.

Field Key:  Not applicable

Data value (hexadecimal): C7 57

Data values in other bases:

| Hexadecimal | C | 7 | 5 | 7 |
| --- | --- | --- | --- | --- |
| Binary | 1100 | 0111 | 0101 | 0111 |
| Decimal | 199 | 87 |

Programming Hint: The name for this variable in code will be IP_Idenfification_TELNET.

IP PDU > Flags for the selected TELNET PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 001

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_Flags_TELNET.

IP PDU > Fragment Offset for the selected TELNET PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0000 0000 0000

Programming Hint: The name for this variable in code will be IP_FragmentOffset_TELNET.

IP PDU > Time to Live for the selected TELNET PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_TELNET.

IP PDU > Protocol for the selected TELNET PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	 10	Telnet						116		74	   WIDEBAND Monitoring

17	 11	XNET						117		75	   WIDEBAND EXPAK

20	 14	Chaos						120-376	78-0178  Unassigned

21	 15	User Datagram				377		0179	    Reserved

Data value (hexadecimal): 06

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |
| Decimal | 6 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming Hint: The name for this variable in code will be IP_Protocol_TELNET

IP PDU > Header Checksum for the selected TELNET PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): F1 85

Data values in other bases:

| Hexadecimal | F | 1 | 8 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 1111 | 0001 | 0100 | 0101 |

Programming Hint: The name for this variable in code will be IP_HeaderChecksum_TELNET.

IP PDU > Source Address for the selected TELNET PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192 | 168 | 0 | 101 |

Programming Hint: The name for this variable in code will be IP_SourceAddress_TELNET.

IP PDU > Destination Address for the selected TELNET PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key: Not applicable

Data value (decimal):  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |
| Decimal | 192 | 168 | 0 | 39 |

Programming Hint: The name for this variable in code will be IP_DestinationAddress_TELNET.

2.2.15 TCP PDU for TELNET PDU

IP > TCP PDU > Source Port for the selected TELNET PDU

Field Name:  Source Port

Purpose and Definition:

This 16-bit number represents the name of the application that sent the data in the IP packet.

Field Key:  Not applicable

Data value: TELNET (23)

Data values in other bases:

| Hexadecimal | 0 | 0 | 1 | 7 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0111 |
| Decimal | 0 | 23 |
| ASCII | © | © |

Programming Hint: The name for this variable in code will be IP_TCP_SourcePort_TELNET.

IP > TCP PDU > Destination Port for the selected TELNET PDU

Field Name: Destination Port

Purpose and Definition:
This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

Field Key:

This key indicates assigned port number values:

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (hexadecimal): 8025

Data values in other bases:

| Hexadecimal | 8 | 0 | 2 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 0000 | 0010 | 0101 |
| Decimal | 128 | 37 |
| ASCII |  | % |

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

Programming Hint: The name for this variable in code will be IP_TCP_DestinationPort_TELNET.

IP > TCP PDU > Sequence Number for the selected TELNET PDU

Field Name:  Sequence Number

Purpose and Definition:
TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Field Key:  Not applicable

Data value (decimal): 2635302920

Data values in other bases:

| Hexadecimal | 9 | D | 1 | 3 | 8 | 8 | 0 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1001 | 1101 | 0001 | 0011 | 1000 | 1000 | 0000 | 1000 |
| Decimal | 157 | 19 | 136 | 8 |
| ASCII |  | © |  | © |

Programming Hint: The name for this variable in code will be IP_TCP_SequenceNumber_TELNET.

IP > TCP PDU > Acknowledgement Number for the selected TELNET PDU

Field Name: Acknowledgement Number

Purpose and Definition:
This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Field Key:  Not applicable

Data value: 2526101253

Data values in other bases:

| Hexadecimal | 9 | 6 | 9 | 1 | 3 | F | 0 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1001 | 0110 | 1001 | 0001 | 0011 | 1111 | 0000 | 0101 |
| Decimal | 150 | 145 | 63 | 5 |
| ASCII |  |  | ? | © |

Programming Hint: The name for this variable in code will be IP_TCP_AcknowledgementNumber_TELNET.

IP > TCP PDU > Header Length or Offset for the selected TELNET PDU

Field Name:  Header Length or Offset

Purpose and Definition:
This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header.

Field Key:  Not applicable

Data value (bytes): 32

Data values in other bases:

| Hexadecimal | 8 | 0 |
| --- | --- | --- |
| Binary | 1000 | 0000 |
| Decimal | 128 |
| ASCII |  |

Programming Hint: The name for this variable in code will be IP_TCP_HeaderLength_TELNET.

IP > TCP PDU > Control Flags for the selected TELNET PDU

Field Name:  Control Flags

Purpose and Definition:
Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:

- Urgent (URG)

- Acknowledgement (ACK)

- Push (PSH)

- Reset (RST)

- Synchronize (SYN)

- Finish (FIN)

Data value (binary): 0001 1000

Data values in other bases:

| Hexadecimal | 1 | 8 |
| --- | --- | --- |
| Binary | 0001 | 1000 |
| Decimal | 24 |
| ASCII | © |

Programming Hint: The name for this variable in code will be IP_TCP_ControlFlags_TELNET.

IP > TCP PDU > Window Size for the selected TELNET PDU

Field Name:  Window Size

Purpose and Definition:
Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:  Not applicable

Data value (decimal): 32120

Data values in other bases:

| Hexadecimal | 7 | D | 7 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 1101 | 0111 | 1000 |
| Decimal | 125 | 120 |
| ASCII | } | x |

Programming Hint: The name for this variable in code will be IP_TCP_WindowSize_TELNET.

IP > TCP PDU > Checksum for the selected TELNET PDU

Field Name:  Checksum

Purpose and Definition:
Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Field Key:  Not applicable

Data value (hexadecimal): 59 89

Data values in other bases:

| Hexadecimal | 5 | 9 | 8 | 9 |
| --- | --- | --- | --- | --- |
| Binary | 0101 | 1001 | 1000 | 1001 |
| Decimal | 89 | 137 |
| ASCII | Y |  |

Programming Hint: The name for this variable in code will be IP_TCP_Checksum_TELNET.

IP > TCP PDU > No Operation for the selected TELNET PDU

Field Name:  No Operation

Purpose and Definition:
This option may be used between options, for example, to align the beginning of a subsequent option on a 32 bit boundary.  May be copied, introduced, or deleted on fragmentation, or for any other reason.  This option may be created by one or many octet fields.

Field Key:  Not applicable

Data value (hexadecimal): 01 01

Data values in other bases:

| Hexadecimal | 0 | 1 | 0 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0001 | 0000 | 0001 |
| Decimal | © | © |

Programming Hint: The name for this variable in code will be IP_TCP_NoOperation_TELNET.

IP > TCP PDU > Timestamp for the selected TELNET PDU

Field Name:  Timestamp

Purpose and Definition:
Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Field Key:

This key indicates assigned flag options:

# Dec		Port Numbers

0		time stamps only, stored in consecutive 32-bit words,

1	            each timestamp is preceded with internet address of the registering entity,

3 	the internet address fields are pre-specified. An IP module only registers its timestamp if it matches its own address with the next specified internet address.

Data value (hexadecimal): 08 0A 0B D1 8D EC 1A AC 06 AB

Data values in other bases:

| Hexadecimal | 0 | 8 | 0 | A | 0 | B | D | 1 | 8 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 1000 | 0000 | 1010 | 0000 | 1011 | 1101 | 0001 | 1000 | 1101 |
| Decimal | 8 | 10 | 11 | 209 | 141 |
| ASCII | © | © | © |  |  |

| Hexadecimal | E | C | 1 | A | A | C | 0 | 6 | A | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1110 | 1100 | 0001 | 1010 | 1010 | 1100 | 0000 | 0110 | 1010 | 1011 |
| Decimal | 236 | 26 | 172 | 6 | 171 |
| ASCII |  | © |  | © |  |

Programming Hint: The name for this variable in code will be IP_TCP_Timestamp_TELNET.

IP > TCP PDU > Options and Padding for the selected TELNET PDU

Field Name: Options and Padding

Purpose and Definition:
Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits.

Field Key:  Not applicable

Data value (hexadecimal): 01 01 08	0A 0B D1 8D EC 1A AC 06 AB

Data values in other bases:

| Hexadecimal | 0 | 1 | 0 | 1 | 0 | 8 | 0 | A | 0 | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0001 | 0000 | 0001 | 0000 | 1000 | 0000 | 1010 | 0000 | 1011 |
| Decimal | 1 | 1 | 8 | 10 | 11 |
| ASCII | © | © | © | © | © |

| Hexadecimal | D | 1 | 8 | D | E | C | 1 | A | A | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1101 | 0001 | 1000 | 1101 | 1110 | 1100 | 0001 | 1010 | 1010 | 1100 |
| Decimal | 209 | 141 | 236 | 26 | 172 |
| ASCII |  |  |  | © |  |

| Hexadecimal | 0 | 6 | A | B |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0110 | 1010 | 1011 |
| Decimal | 6 | 171 |
| ASCII | © |  |

Programming Hint: The name for this variable in code will be IP_TCP_OptionsPadding_TELNET.

2.2.16 TELNET PDU for the TELNET PDU

IP >TCP > TELNET PDU for the TELNET Packet

RFC Link: http://www.ietf.org/rfc/rfc0959.txt?number=959

PASS (Password)

The argument field is a Telnet string specifying the user’s password.  This command must be immediately preceded by the user name command, and, for some sites, completes the user’s identification for access control.

What is Contained in the Packet

Request:	PASS

Data Values (hexadecimal): 50 61 73 73 77 6F 72 64 3A 20

Data Values in Other Bases

| Hexadecimal | 5 | 0 | 6 | 1 | 7 | 3 | 7 | 7 | 6 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0000 | 0110 | 0001 | 0111 | 0011 | 0111 | 0111 | 0110 | 1111 |
| Decimal | 80 | 97 | 115 | 119 | 111 |
| ASCII | P | a | s | w | o |

| Hexadecimal | 7 | 2 | 6 | 4 | 3 | A | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0110 | 0100 | 0011 | 1010 | 0010 | 0000 |
| Decimal | 114 | 100 | 58 | 32 |
| ASCII | r | d | : | © |

Programming Hint: The name for this variable in code will be IP_TCP_TELNET_PDU_TELNET.

2.2.17 IP PDU for the selected SSH PDU

IP PDU > IP Version for the selected SSH PDU

Field Name: IP Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be IP_Version_SSH.

IP PDU > Internet Header Length for the selected SSH PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4-bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 5 |
| --- | --- |
| Binary | 0101 |
| Decimal | 5 |

Programming Hint: The name for this variable in code will be IP_IHL_SSH.

IP PDU > Type of Service for the selected SSH PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 00

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |
| Decimal | 0 |

Programming Hint: The name for this variable in code will be IP_TypeOfService_SSH.

IP PDU > Total Length of Ethernet Frame for the selected SSH PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key:  Not applicable

Data values (hexadecimal):  00 64

Data values in other bases:

| Hexadecimal | 0 | 0 | 6 | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0110 | 0100 |
| Decimal | 0 | 100 |
| ASCII | . | d |

Programming Hint: The name for this variable in code will be IP_TotalLength_SSH.

IP PDU > Identification for the selected SSH PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet.

Field Key:  Not applicable

Data value (hexadecimal): 30 CA

Data values in other bases:

| Hexadecimal | 3 | 0 | C | A |
| --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 1100 | 1010 |

Programming Hint: The name for this variable in code will be IP_Idenfification_SSH.

IP PDU > Flags for the selected SSH PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 001

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_Flags_SSH.

IP PDU > Fragment Offset for the selected SSH PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0 0000 0000 0000

Programming Hint: The name for this variable in code will be IP_FragmentOffset_SSH.

IP PDU > Time to Live for the selected SSH PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_SSH.

IP PDU > Protocol for the selected SSH PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	 10	SSH						116		74	   WIDEBAND Monitoring

17	 11	XNET						117		75	   WIDEBAND EXPAK

20	 14	Chaos						120-376	78-0178  Unassigned

21	 15	User Datagram				377		0179	    Reserved

Data value (hexadecimal): 11

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |
| Decimal | 6 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming Hint: The name for this variable in code will be IP_Protocol_SSH

IP PDU > Header Checksum for the selected SSH PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): 87 AE

Data values in other bases:

| Hexadecimal | 8 | 7 | A | E |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 0111 | 1010 | 1110 |

Programming Hint: The name for this variable in code will be IP_HeaderChecksum_SSH.

IP PDU > Source Address for the selected SSH PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192 | 168 | 0 | 101 |

Programming Hint: The name for this variable in code will be IP_SourceAddress_SSH.

IP PDU > Destination Address for the selected SSH PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key: Not applicable

Data value (decimal):  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |
| Decimal | 192 | 168 | 0 | 39 |

Programming Hint: The name for this variable in code will be IP_DestinationAddress_SSH.

2.2.18 TCP PDU for the selected SSH PDU

IP > TCP PDU > Source Port for the selected SSH PDU

Field Name:  Source Port

Purpose and Definition:

This 16-bit number represents the name of the application that sent the data in the IP packet.

Field Key:  Not applicable

Data value: 1243

Data values in other bases:

| Hexadecimal | 0 | 4 | D | B |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0100 | 1101 | 1011 |
| Decimal | 4 | 219 |
| ASCII | © |  |

Programming Hint: The name for this variable in code will be IP_TCP_SourcePort_SSH.

IP > TCP PDU > Destination Port for the selected SSH PDU

Field Name: Destination Port

Purpose and Definition:
This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

Field Key:

This key indicates assigned port number values:

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (decimal): 1243

Data values in other bases:

| Hexadecimal | 0 | 4 | D | B |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0100 | 1101 | 1011 |
| Decimal | 4 | 219 |
| ASCII | © |  |

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

Programming Hint: The name for this variable in code will be IP_TCP_DestinationPort_SSH.

IP > TCP PDU > Sequence Number for the selected SSH PDU

Field Name:  Sequence Number

Purpose and Definition:
TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Field Key:  Not applicable

Data value (decimal): 4008673261

Data values in other bases:

| Hexadecimal | E | E | E | F | 7 | F | E | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1110 | 1110 | 1110 | 1111 | 0111 | 1111 | 1110 | 1101 |
| Decimal | 238 | 239 | 127 | 237 |
| ASCII |  |  |  |  |

Programming Hint: The name for this variable in code will be IP_TCP_SequenceNumber_SSH.

IP > TCP PDU > Acknowledgement Number for the selected SSH PDU

Field Name: Acknowledgement Number

Purpose and Definition:
This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Field Key:  Not applicable

Data value: 3798775616

Data values in other bases:

| Hexadecimal | E | 2 | 6 | C | B | 7 | 4 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1110 | 0010 | 0110 | 1100 | 1011 | 0111 | 0100 | 0000 |
| Decimal | 226 | 108 | 183 | 64 |
| ASCII |  | l |  | @ |

Programming Hint: The name for this variable in code will be IP_TCP_AcknowledgementNumber_SSH.

IP > TCP PDU > Header Length or Offset for the selected SSH PDU

Field Name:  Header Length or Offset

Purpose and Definition:
This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header.

Field Key:  Not applicable

Data value (bytes): 32

Data values in other bases:

| Hexadecimal | 8 | 0 |
| --- | --- | --- |
| Binary | 1000 | 0000 |
| Decimal | 128 |
| ASCII |  |

Programming Hint: The name for this variable in code will be IP_TCP_HeaderLength_SSH.

IP > TCP PDU > Control Flags for the selected SSH PDU

Field Name:  Control Flags

Purpose and Definition:
Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:

- Urgent (URG)

- Acknowledgement (ACK)

- Push (PSH)

- Reset (RST)

- Synchronize (SYN)

- Finish (FIN)

Data value (binary): 0001 1000

Data values in other bases:

| Hexadecimal | 1 | 8 |
| --- | --- | --- |
| Binary | 0001 | 1000 |
| Decimal | 24 |
| ASCII | © |

Programming Hint: The name for this variable in code will be IP_TCP_ControlFlags_SSH.

IP > TCP PDU > Window Size for the selected SSH PDU

Field Name:  Window Size

Purpose and Definition:
Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:  Not applicable

Data value (decimal): 32120

Data values in other bases:

| Hexadecimal | 7 | D | 7 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 1101 | 0111 | 1000 |
| Decimal | 125 | 120 |
| ASCII | } | x |

Programming Hint: The name for this variable in code will be IP_TCP_WindowSize_SSH.

IP > TCP PDU > Checksum for the selected SSH PDU

Field Name:  Checksum

Purpose and Definition:
Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Field Key:  Not applicable

Data value (hexadecimal): 8B CA

Data values in other bases:

| Hexadecimal | 8 | B | C | A |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 1011 | 1100 | 1010 |
| Decimal | 139 | 202 |
| ASCII |  |  |

Programming Hint: The name for this variable in code will be IP_TCP_Checksum_SSH.

IP > TCP PDU > Options and Padding for the selected SSH PDU

Field Name: Options and Padding

Purpose and Definition:
Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits.

Field Key:  Not applicable

Data value (hexadecimal): 01 01 08	0A 0B D1 8D EC 1A AC 06 AB

Data values in other bases:

| Hexadecimal | 0 | 1 | 0 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0001 | 0000 | 0001 |
| Decimal | © | © |

Programming Hint: The name for this variable in code will be IP_TCP_OptionsPadding_SSH.

IP > TCP PDU > Timestamp for the selected SSH PDU

Field Name:  Timestamp

Purpose and Definition:
Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Field Key:

This key indicates assigned flag options:

# Dec		Port Numbers

0		time stamps only, stored in consecutive 32-bit words,

1	            each timestamp is preceded with internet address of the registering entity,

3 	the internet address fields are pre-specified. An IP module only registers its timestamp if it matches its own address with the next specified internet address.

Data value (hexadecimal): 08 0A 14 42 6F 30 27 47 32 1F

Data values in other bases:

| Hexadecimal | 0 | 8 | 0 | A | 1 | 4 | 4 | 2 | 6 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 1000 | 0000 | 1010 | 0001 | 0100 | 0100 | 0010 | 0110 | 1111 |
| Decimal | 8 | 10 | 20 | 66 | 111 |
| ASCII | © | © | © | B | o |

| Hexadecimal | 3 | 0 | 2 | 7 | 4 | 7 | 3 | 2 | 1 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0010 | 0111 | 0100 | 0111 | 0011 | 0010 | 0001 | 1111 |
| Decimal | 48 | 39 | 71 | 50 | 31 |
| ASCII | 0 | ‘ | G | 2 | © |

Programming Hint: The name for this variable in code will be IP_TCP_Timestamp_SSH.

2.2.18 SSH PDU for the selected SSH PDU

IP >TCP > SSH PDU for the SSH Packet

RFC Link:  http://www.ietf.org/rfc/rfc0959.txt?number=959

PASS (Password)

The argument field is a SSH string specifying the user’s password.  This command must be immediately preceded by the user name command, and, for some sites, completes the user’s identification for access control.  All information below is encrypted.

What is Contained in the Packet

Request:	PASS

Data Values (hexadecimal): 03 B6 51 11 6A 46 12 36 4F 46 C9 63 B1 A4 B5 48 A2 BA 68 1C 42 17 AB D2 CE 8E 6D 3F 49 7E EB 36 A0 1B 16 62 E4 0F D7 55 DD 5F EB 52 64 B9 A7 62

Data Values in Other Bases

| Hexadecimal | 0 | 3 | B | 6 | 5 | 1 | 1 | 1 | 6 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0011 | 1011 | 0110 | 0101 | 0001 | 0001 | 0001 | 0110 | 1010 |
| Decimal | 3 | 182 | 81 | 17 | 106 |
| ASCII | © |  | Q | © | j |

| Hexadecimal | 4 | 6 | 1 | 2 | 3 | 6 | 4 | F | 4 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0110 | 0001 | 0010 | 0011 | 0110 | 0100 | 1111 | 0100 | 0110 |
| Decimal | 70 | 18 | 54 | 79 | 70 |
| ASCII | F | © | 6 | O | F |

| Hexadecimal | C | 9 | 6 | 3 | B | 1 | A | 4 | B | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 1001 | 0110 | 0011 | 1011 | 0001 | 1010 | 0100 | 1011 | 0101 |
| Decimal | 201 | 99 | 177 | 164 | 181 |
| ASCII |  | c |  |  |  |

| Hexadecimal | 4 | 8 | A | 2 | B | A | 6 | 8 | 1 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1000 | 1010 | 0010 | 1011 | 1010 | 0110 | 1000 | 0001 | 1000 |
| Decimal | 72 | 162 | 178 | 104 | 28 |
| ASCII | H |  |  | H | © |

| Hexadecimal | 4 | 2 | 1 | 7 | A | B | D | 2 | C | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0010 | 0001 | 0111 | 1010 | 1011 | 1101 | 0010 | 1100 | 1110 |
| Decimal | 66 | 23 | 171 | 210 | 206 |
| ASCII | B | © |  |  |  |

| Hexadecimal | 8 | E | 6 | D | 3 | F | 4 | 9 | 7 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 1110 | 0110 | 1101 | 0011 | 1111 | 0100 | 1001 | 0111 | 1110 |
| Decimal | 142 | 109 | 63 | 73 | 126 |
| ASCII |  | m | ? | I | ~ |

| Hexadecimal | E | B | 3 | 6 | A | 0 | 1 | B | 1 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1110 | 1011 | 0011 | 0110 | 1010 | 0000 | 0001 | 1011 | 0001 | 0110 |
| Decimal | 235 | 54 | 160 | 27 | 22 |
| ASCII |  | 6 |  | © | © |

| Hexadecimal | 6 | 2 | E | 4 | 0 | F | D | 7 | 5 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0010 | 1110 | 0100 | 0000 | 1111 | 1101 | 0111 | 0101 | 0101 |
| Decimal | 98 | 228 | 15 | 215 | 85 |
| ASCII | b |  | © |  | U |

| Hexadecimal | D | D | 5 | F | E | B | 5 | 2 | 6 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1101 | 1101 | 0101 | 1111 | 1110 | 1011 | 0101 | 0010 | 0110 | 0100 |
| Decimal | 221 | 95 | 235 | 82 | 100 |
| ASCII |  | _ |  | R | d |

| Hexadecimal | B | 9 | A | 7 | 6 | 2 |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 1011 | 1001 | 1010 | 0111 | 0110 | 0010 |
| Decimal | 185 | 167 | 98 |
| ASCII |  |  | b |

Programming Hint: The name for this variable in code will be IP_TCP_SSH_PDU_SSH.

2.2.20 ARP PDU for the selected ARP PDU

ARP PDU> Hardware Address Type > for the selected ARP PDU

Field Name: Hardware Address Type

Purpose and Definition:  The physical media that communicates on the network.

Field Key:  1 for Ethernet

2 for IEEE 802 LAN

Data value (hexadecimal):  00 01

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0001 |
| Decimal | 0 | 1 |

Programming Hint: The name for this variable in code will be ARP_HardwareAddressType

ARP PDU > Protocol Address Type > for the selected ARP PDU

Field Name: Protocol Address Type

Purpose and Definition:  Defines the protocol that the terminals are using to connect with each other.

Field Key:  2048 IPv4 (0x0800)

Data value (hexadecimal): 08 00

Data values in other bases:

| Hexadecimal | 0 | 8 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 1000 | 0000 | 0000 |
| Decimal | 8 | 0 |

Programming Hint: The name for this variable in code will be ARP_ProtocolAddressType.

ARP PDU > Hardware Address Length > for the selected ARP PDU

Field Name:  Hardware Address Length

Purpose and Definition: This field determines the type of hardware used.

Field Key:  6 Ethernet / IEE 802

Data value (hexadecimal): 00 06

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 6 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 1000 | 0000 | 0110 |
| Decimal | 0 | 6 |

Programming Hint: The name for this variable in code will be ARP_HardwareAddressLength.

ARP PDU >Protocol Address Length>for the selected ARP PDU

Field Name:  Protocol Address Length

Purpose and Definition: Determines the protocol used in the request or response.   .

Field Key:  4 for IPv4

Data value (hexadecimal):  02 01 00

Data values in other bases:

| Hexadecimal | 0 | 2 | 0 | 1 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0010 | 0000 | 0001 | 0000 | 0000 |
| Decimal | 2 | 1 | 0 |

Programming Hint: The name for this variable in code will be ARP_ProtocolAddressLength.

ARP PDU > Operation > for the selected ARP PDU

Field Name: Operation

Purpose and Definition: Determines weather a request or a response is being called upon.

Field Key:  1 for request

2 for reply

Data value (hexadecimal):  00 01

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0001 |
| Decimal | 0 | 1 |

Programming Hint: The name for this variable in code will be ARP_Operation

# ARP PDU > Sender Hardware Address > for the selected ARP PDU

Field Name:  Sender Hardware Address

Purpose and Definition: The Physical address or MAC address of the network adapter of the sender’s terminal.

Field Key:

00000C  Cisco

00000E  Fujitsu

00000F  NeXT

000010  Sytek

00001D  Cabletron

000020  DIAB (Data Intdustrier AB)

000022  Visual Technology

00002A  TRW

000032  GPT Limited (reassigned from GEC Computers Ltd)

00005A  S & Koch

00005E  IANA

000065  Network General

00006B  MIPS

000077  MIPS

00007A  Ardent

000089  Cayman Systems  Gatorbox

000093  Proteon

00009F  Ameristar Technology

0000A2  Wellfleet

0000A3  Network Application Technology

0000A6  Network General (internal assignment, not for products)

0000A7  NCD             X-terminals

0000A9  Network Systems

0000AA  Xerox           Xerox machines

0000B3  CIMLinc

0000B7  Dove            Fastnet

0000BC  Allen-Bradley

0000C0  Western Digital

0000C5  Farallon phone net card

0000C6  HP Intelligent Networks Operation (formerly Eon Systems)

0000C8  Altos

0000C9  Emulex          Terminal Servers

0000D7  Dartmouth College (NED Router)

0000D8  3Com? Novell?   PS/2

0000DD  Gould

0000DE  Unigraph

0000E2  Acer Counterpoint

0000EF  Alantec

0000FD  High Level Hardvare (Orion, UK)

000102  BBN             BBN internal usage (not registered)

0020AF  3COM ???

001700  Kabel

008064  Wyse Technology / Link Technologies

00802B  IMAC ???

00802D  Xylogics, Inc.  Annex terminal servers

00808C  Frontier Software Development

0080C2  IEEE 802.1 Committee

0080D3  Shiva

00AA00  Intel

00DD00  Ungermann-Bass

00DD01  Ungermann-Bass

020701  Racal InterLan

020406  BBN             BBN internal usage (not registered)

026086  Satelcom MegaPac (UK)

02608C  3Com            IBM PC; Imagen; Valid; Cisco

02CF1F  CMC             Masscomp; Silicon Graphics; Prime EXL

080002  3Com (Formerly Bridge)

080003  ACC (Advanced Computer Communications)

080005  Symbolics       Symbolics LISP machines

080008  BBN

080009  Hewlett-Packard

08000A  Nestar Systems

08000B  Unisys

080011  Tektronix, Inc.

080014  Excelan         BBN Butterfly, Masscomp, Silicon Graphics

080017  NSC

08001A  Data General

08001B  Data General

08001E  Apollo

080020  Sun             Sun machines

080022  NBI

080025  CDC

080026  Norsk Data (Nord)

080027  PCS Computer Systems GmbH

080028  TI              Explorer

08002B  DEC

08002E  Metaphor

08002F  Prime Computer  Prime 50-Series LHC300

080036  Intergraph      CAE stations

080037  Fujitsu-Xerox

080038  Bull

080039  Spider Systems

080041  DCA Digital Comm. Assoc.

080045  ???? (maybe Xylogics, but they claim not to know this number)

080046  Sony

080047  Sequent

080049  Univation

08004C  Encore

08004E  BICC

080056  Stanford University

080058  ???             DECsystem-20

08005A  IBM

080067  Comdesign

080068  Ridge

080069  Silicon Graphics

08006E  Concurrent      Masscomp

080075  DDE (Danish Data Elektronik A/S)

08007C  Vitalink        TransLAN III

080080  XIOS

080086  Imagen/QMS

080087  Xyplex          terminal servers

080089  Kinetics        AppleTalk-Ethernet interface

08008B  Pyramid

08008D  XyVision        XyVision machines

080090  Retix Inc       Bridges

484453  HDS ???

800010  AT&T

AA0000  DEC             obsolete

AA0001  DEC             obsolete

AA0002  DEC             obsolete

AA0003  DEC             Global physical address for some DEC machines

AA0004  DEC             Local logical address for systems running DECNET

Data value (hexadecimal):  00:00:E6: 34:ED:A3

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 | E | 6 | 3 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 1110 | 0110 | 0011 | 0100 |
| Decimal | 0 | 0 | 230 | 52 |

| Hexadecimal | E | D | A | 3 |
| --- | --- | --- | --- | --- |
| Binary | 1110 | 1101 | 1010 | 0011 |
| Decimal | 237 | 163 |

Programming Hint: The name for this variable in code will be ARP_SenderAddress

ARP PDU > Sender Protocol Address > for the selected ARP PDU

Field Name:  Sender Protocol Address

Purpose and Definition:  The protocol of the sender computer. This is used to identify the  senders Protocol.

Field Key:  N/A

Data value (decimal): 192.168.0.101

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192 | 168 | 0 | 101 |

Programming Hint: The name for this variable in code will be ARP_SenderProtocolAddress

ARP PDU > Target Hardware Address > for the selected ARP PDU

Field Name:  Target Hardware Address

Purpose and Definition: The Physical address or MAC address of the network adapter of the target terminal.

Field Key:

00000C  Cisco

00000E  Fujitsu

00000F  NeXT

000010  Sytek

00001D  Cabletron

000020  DIAB (Data Intdustrier AB)

000022  Visual Technology

00002A  TRW

000032  GPT Limited (reassigned from GEC Computers Ltd)

00005A  S & Koch

00005E  IANA

000065  Network General

00006B  MIPS

000077  MIPS

00007A  Ardent

000089  Cayman Systems  Gatorbox

000093  Proteon

00009F  Ameristar Technology

0000A2  Wellfleet

0000A3  Network Application Technology

0000A6  Network General (internal assignment, not for products)

0000A7  NCD             X-terminals

0000A9  Network Systems

0000AA  Xerox           Xerox machines

0000B3  CIMLinc

0000B7  Dove            Fastnet

0000BC  Allen-Bradley

0000C0  Western Digital

0000C5  Farallon phone net card

0000C6  HP Intelligent Networks Operation (formerly Eon Systems)

0000C8  Altos

0000C9  Emulex          Terminal Servers

0000D7  Dartmouth College (NED Router)

0000D8  3Com? Novell?   PS/2

0000DD  Gould

0000DE  Unigraph

0000E2  Acer Counterpoint

0000EF  Alantec

0000FD  High Level Hardvare (Orion, UK)

000102  BBN             BBN internal usage (not registered)

0020AF  3COM ???

001700  Kabel

008064  Wyse Technology / Link Technologies

00802B  IMAC ???

00802D  Xylogics, Inc.  Annex terminal servers

00808C  Frontier Software Development

0080C2  IEEE 802.1 Committee

0080D3  Shiva

00AA00  Intel

00DD00  Ungermann-Bass

00DD01  Ungermann-Bass

020701  Racal InterLan

020406  BBN             BBN internal usage (not registered)

026086  Satelcom MegaPac (UK)

02608C  3Com            IBM PC; Imagen; Valid; Cisco

02CF1F  CMC             Masscomp; Silicon Graphics; Prime EXL

080002  3Com (Formerly Bridge)

080003  ACC (Advanced Computer Communications)

080005  Symbolics       Symbolics LISP machines

080008  BBN

080009  Hewlett-Packard

08000A  Nestar Systems

08000B  Unisys

080011  Tektronix, Inc.

080014  Excelan         BBN Butterfly, Masscomp, Silicon Graphics

080017  NSC

08001A  Data General

08001B  Data General

08001E  Apollo

080020  Sun             Sun machines

080022  NBI

080025  CDC

080026  Norsk Data (Nord)

080027  PCS Computer Systems GmbH

080028  TI              Explorer

08002B  DEC

08002E  Metaphor

08002F  Prime Computer  Prime 50-Series LHC300

080036  Intergraph      CAE stations

080037  Fujitsu-Xerox

080038  Bull

080039  Spider Systems

080041  DCA Digital Comm. Assoc.

080045  ???? (maybe Xylogics, but they claim not to know this number)

080046  Sony

080047  Sequent

080049  Univation

08004C  Encore

08004E  BICC

080056  Stanford University

080058  ???             DECsystem-20

08005A  IBM

080067  Comdesign

080068  Ridge

080069  Silicon Graphics

08006E  Concurrent      Masscomp

080075  DDE (Danish Data Elektronik A/S)

08007C  Vitalink        TransLAN III

080080  XIOS

080086  Imagen/QMS

080087  Xyplex          terminal servers

080089  Kinetics        AppleTalk-Ethernet interface

08008B  Pyramid

08008D  XyVision        XyVision machines

080090  Retix Inc       Bridges

484453  HDS ???

800010  AT&T

AA0000  DEC             obsolete

AA0001  DEC             obsolete

AA0002  DEC             obsolete

AA0003  DEC             Global physical address for some DEC machines

AA0004  DEC             Local logical address for systems running DECNET

Data value (hexadecimal): 00:00:00:00:00:00

Data values in other bases: Not applicable

Programming hint:  ARP_TargetHardwareAddress.

ARP PDU>Target Protocol Address> for the selected ARP PDU

Field Name: Target Protocol Address

Purpose and Definition:  The protocol of the sender computer. This is used to identify the targets Protocol.

Field Key:  4 for IPv4

Data value (decimal): 192.168.0.145

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 9 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 1001 | 0001 |
| Decimal | 192 | 168 | 0 | 145 |

Programming hint: ARP_TargetProtocolAddress

2.2.21 IP PDU for the selected PING PDU

IP PDU > Differentiated Services Field for the selected PING

RFC Link: http://www.ietf.org/rfc/rfc0768.txt?number=768

Field Name: Differentiated Services Field

Purpose and Definition: Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (decimal): 00

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |
| Decimal | 0 |

Programming Hint: The name for this variable in code will be

IP_DSF_PING.

IP PDU> Flags for the selected PING

Field Name: Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:  Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (hexadecimal): 04

Data values in other bases:

| Hexadecimal | 0 | 4 |
| --- | --- | --- |
| Binary | 0000 | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be

IP_Flags_PING.

IP PDU> Fragment offset for the selected PING

Field Name: Fragment offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

Binary: 0000

Programming Hint: The name for this variable in code will be

IP_Fragment Offset_PING.

IP PDU > Time to Live for the selected PING

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 40

Data values in other bases:

| Hexadecimal | 2 | 8 |
| --- | --- | --- |
| Binary | 0010 | 1000 |
| Decimal | 40 |

Programming Hint: The name for this variable in code will be

IP_TimetoLive_PING.

IP PDU> Protocol for the selected PING

Field Name: Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

# Field Key:

# Dec Hex	Protocol					Dec		Hex	 Protocol

0 	  00	Reserved					22		16	  Multiplexing

1 	  01	ICMP						23		17	  DCN

2	  02	Unassigned					24		18	  TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	  Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	  Any local network

5	  05	ST						100		64	  SATNET and Backroom EXPAK

6	  06	TCP						101		65	  MIT Subnet Support

7	  07	UCL						102-104	66-68	  Unassigned

10	  0A	Unassigned					105		69	  SATNET Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	  Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	  Unassigned

16	10	Telnet						116		74	   WIDEBAND Monitoring

17	11	XNET						117		75	  WIDEBAND EXPAK

20	14	Chaos						120-376	78-0178  Unassigned

21	15	User Datagram				377		0179	    Reserved

Data value (decimal): 01

Data values in other bases:

| Hexadecimal | 0 | 1 |
| --- | --- | --- |
| Binary | 0000 | 0001 |
| Decimal | 1 |

Programming Hint: The name for this variable in code will be IP_Protocol_PING.

IP PDU> Header Checksum for the selected PING

Field Name: Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

Field Key:  Not applicable

Data value (decimal): B8 CC

Data values in other bases:

| Hexadecimal | B | 8 | C | C |
| --- | --- | --- | --- | --- |
| Binary | 1011 | 1000 | 1100 | 1100 |

Programming Hint: The name for this variable in code will be

IP_HeaderChecksum_PING.

IP PDU> Source for the selected PING

Field Name: Source

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value (decimal): 192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |
| Decimal | 192 | 168 | 0 | 39 |

Programming Hint: The name for this variable in code will be

IP_Source_PING.

IP PDU > Destination for the selected PING

Field Name: Destination

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key:  Not applicable

Data value (decimal): 192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192 | 168 | 0 | 101 |

Programming Hint: The name for this variable in code will be

Ethernet_Destination_PING.

2.2.22 ICMP PDU for the selected PING PDU

IP > ICMP Header > Type for the selected PING PDU

Field Name:  Type

Purpose and Definition:  The type is an 8-bit field that identifies what sort of message the ICMP protocol is sending.

Field Key:

# Dec	Hex	Message Type		Dec	  Hex	   Message Type

0	00	Echo Reply			16	  10	   Information Reply

1	01	Unassigned			17	  11	   Address Mask Request

2	02	Unassigned			18	  12	   Address Mask Reply

3	03	Destination Unreachable	19	  13	   Reserved (for Security)

4	04	Source Quench		20-29	  14-1D   Reserved (for Robustness Experiment)

5	05	Redirect			30	  1E	   Traceroute

6	06	Alternate Host Address	31	  1F	   Datagram Conversion Error

7	07	Unassigned			32	  20	   Mobile Host Redirect

8	08	Echo				33	  21	   IPv6 Where-Are-You

9	09	Router Advertisement		34	  22	   IPv6 I-Am-Here

10	0A	Router Solicitation		35	  23	   Mobile Registration Request

11	0B	Time Exceeded		36	  24	   Mobile Registration Reply

12	0C	Parameter Problem		37	  25	   Domain Name Request

13	0D	Timestamp			38	  26	   Domain Name Reply

14	0E	Timestamp Reply		39	  27	   SKIP

15	0F	Information Request		40	  28	   Photuris

41-255	  29-FF Reserved

Data value: 8 (Echo (ping) Request)

Data values in other bases:

| Hexadecimal | 0 | 8 |
| --- | --- | --- |
| Binary | 0000 | 1000 |
| Decimal | 8 |

RFC Link: http://www.iana.org/assignments/icmp-parameters

Programming Hint: The name for this variable in code will be IP_ICMP_Type_PING.

IP > ICMP Header > Code for the selected PING PDU

Field Name:  Code

Purpose and Definition: Code is an 8-bit field that provides further information about the associated type field.

Field Key:

Type     Name					Type     Name

0             Echo Reply (used by “PING”)			   7            Unassigned

0     No Code			    	   8            Echo (used by "PING")

1             Unassigned 					    0     No Code

2             Unassigned				   9            Router Advertisement

3             Destination Unreachable 			                       0    No Code

0     Net Unreachable			  10           Router Selection

1     Host Unreachable				     0    No Code

2     Protocol Unreachable			  11           Time Exceeded

3     Port Unreachable				     0    Time to Live exceeded in Transit

- Fragmentation needed and 			     1    Fragment Reassembly Time Exceeded

Don't Fragment was Set			  12            Parameter Problem

5     Source Route Failed				     0    Pointer indicates the error

6     Destination Network Unknown			     1    Missing a Required Option

7     Destination Host Unknown			     2    Bad Length

8     Source Host Isolated			  13           Timestamp

- Communication with Destination		  	     0    No Code

Network is Administratively Prohibited	  14           Timestamp Reply

- Communication with Destination		  	     0    No Code

Host is Administratively Prohibited		  15           Information Request

- Destination Network Unreachable		  	     0    No Code

for Type of Service                                               16           Information Reply

- Destination Host Unreachable for 		  	     0    No Code

Type of Service			  17           Address Mask Request

4            Source Quench                           			  	     0    No Code

0     No Code				  18           Address Mask Reply

5            Redirect                                 			  	    0     No Code

0    Redirect Datagram for the Network		  19           Reserved (for Security)

1    Redirect Datagram for the Host		  20-29   Reserved (for Robustness Experiment)

2    Redirect Datagram for the Type of 		  30        Traceroute

Service and Network			  31        Datagram Conversion Error

- Redirect Datagram for the Type of		  32        Mobile Host Redirect

Service and Host			  33        IPv6 Where-Are-You

6            Alternate Host Address 			  34        IPv6 I-Am-Here

0    Alternate Address for Host		  35        Mobile Registration Request

36        Mobile Registration Reply

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |
| Decimal | 0 |
| ASCII | © |

Programming Hint: The name for this variable in code will be IP_ICMP_Header_PING.

IP > ICMP Header > Checksum for the selected PING PDU

Field Name:  Checksum

Purpose and Definition:  The checksum is the 16-bit one’s complement of the one’s complement sum of the ICMP message, starting with the ICMP type.  For computing the checksum, the checksum field should initially be zero.

Field Key:  Not applicable

Data value (hexadecimal): C9 15

Data values in other bases:

| Hexadecimal | C | 9 | 1 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 1100 | 1001 | 0001 | 0101 |
| Decimal | 201 | 21 |
| ASCII |  | © |

Programming Hint: The name for this variable in code will be IP_ICMP_Checksum_PING.

IP > ICMP Header > Identifier for the selected PING PDU

Field Name:  Identifier

Purpose and Definition:  The identifier is a 16-bit field that is used in matching echoes and replies for when the code field is zero.

Field Key:  Not applicable

Data value (hexadecimal): 70 60

Data values in other bases:

| Hexadecimal | 7 | 0 | 6 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 0000 | 0110 | 0000 |
| Decimal | 112 | 96 |
| ASCII | P | ‘ |

Programming Hint: The name for this variable in code will be IP_ICMP_Identifier_PING.

IP > ICMP Header > Sequence for the selected PING PDU

Field Name:  Sequence

Purpose and Definition:  The sequence is a 16-bit field that is used in matching echoes and replies for when the code field is zero.

Field Key:  Not applicable

Data value (hexadecimal): 70 60

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |
| Decimal | 0 | 0 |
| ASCII | © | © |

Programming Hint: The name for this variable in code will be IP_ICMP_Sequence_PING.

IP > ICMP Header > Data for the selected PING PDU

Field Name:  Data

Purpose and Definition:  The data is a variable-length field that contains the actual information that is sent in the ping packet.

Field Key:  Not applicable

Data value (hexadecimal): 00 01 03 1E E2 24 00 00 F8 1F 00 85 08 00 45 00 00 54 00 00 40 00 40 01 B8 CC C0 A8 00 27 C0 A8 00 65 08 00 C9 15 70 60 00 00 42 B1 89 3F 00 00 00 00 2C C6 07 00 00 00 00 00 10 11 12 13 14 15 26 27 28 29 2A 2B 2C 2D 2E 2F 30 31 32 33 34 35 36 37

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 1 | 0 | 3 | 1 | E | E | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 000 | 0011 | 0001 | 1110 | 1110 | 0010 |
| Decimal | 0 | 1 | 3 | 30 | 226 |
| ASCII | ( | ( | ( | ( |  |

| Hexadecimal | 2 | 4 | 0 | 0 | 0 | 0 | F | 8 | 1 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0100 | 0000 | 0000 | 0000 | 0000 | 1111 | 1000 | 0001 | 1111 |
| Decimal | 36 | 0 | 0 | 242 | 31 |
| ASCII | $ | © | © |  | ( |

| Hexadecimal | 0 | 0 | 8 | 5 | 0 | 8 | 0 | 0 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 1000 | 0101 | 0000 | 1000 | 0000 | 0000 | 0100 | 0101 |
| Decimal | 0 | 133 | 8 | 0 | 69 |
| ASCII | © |  | © | © | E |

| Hexadecimal | 0 | 0 | 0 | 0 | 5 | 4 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0101 | 0100 | 0000 | 0000 | 0000 | 0000 |
| Decimal | 0 | 0 | 84 | 0 | 0 |
| ASCII | © | © | T | © | © |

| Hexadecimal | 4 | 0 | 0 | 0 | 4 | 0 | 0 | 1 | B | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0000 | 0000 | 0000 | 0100 | 0000 | 0000 | 0001 | 1011 | 1000 |
| Decimal | 64 | 0 | 64 | 1 | 184 |
| ASCII | @ | © | @ | © |  |

| Hexadecimal | C | C | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 1100 | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |
| Decimal | 204 | 192 | 168 | 0 | 39 |
| ASCII |  |  |  | © | ‘ |

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 | 0 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 | 0000 | 1000 |
| Decimal | 192 | 168 | 0 | 101 | 8 |
| ASCII |  |  | ( | e | ( |

| Hexadecimal | 0 | 0 | C | 9 | 1 | 5 | 7 | 0 | 6 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 1100 | 1001 | 0001 | 0101 | 0111 | 0000 | 0110 | 0000 |
| Decimal | 0 | 201 | 21 | 112 | 96 |
| ASCII | ( |  | ( | p | ‘’ |

| Hexadecimal | 0 | 0 | 0 | 0 | 4 | 2 | b | 1 | 8 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0100 | 0010 | 1011 | 0001 | 1000 | 1001 |
| Decimal | 0 | 0 | 66 | 177 | 137 |
| ASCII | ( | ( | B |  |  |

| Hexadecimal | 3 | F | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1111 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 |
| Decimal | 63 | 0 | 0 | 0 | 0 |
| ASCII | ? | ( | ( | ( | ( |

| Hexadecimal | 2 | C | c | 6 | 0 | 7 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1100 | 1100 | 0110 | 0000 | 0111 | 0000 | 0000 | 0000 | 0000 |
| Decimal | 44 | 198 | 7 | 0 | 0 |
| ASCII | , |  | ( | ( | ( |

| Hexadecimal | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0001 | 0000 | 0001 | 0001 |
| Decimal | 0 | 0 | 0 | 16 | 17 |
| ASCII | ( | ( | ( | ( | ( |

| Hexadecimal | 1 | 2 | 1 | 3 | 1 | 4 | 1 | 5 | 2 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0001 | 0010 | 0001 | 0011 | 0001 | 0100 | 0001 | 0101 | 0010 | 0110 |
| Decimal | 18 | 19 | 20 | 21 | 38 |
| ASCII | ( | ( | ( | ( | & |

| Hexadecimal | 2 | 7 | 2 | 8 | 2 | 9 | 2 | A | 2 | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0111 | 0001 | 1000 | 0010 | 1001 | 0010 | 1010 | 0010 | 1011 |
| Decimal | 39 | 40 | 41 | 42 | 43 |
| ASCII | ‘ | ( | ) | * | + |

| Hexadecimal | 2 | C | 2 | F | 3 | 0 | 3 | 1 | 3 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1100 | 0010 | 111 | 0011 | 0000 | 0011 | 0001 | 0011 | 0010 |
| Decimal | 44 | 47 | 48 | 49 | 50 |
| ASCII | , | / | 0 | 1 | 2 |
| Hexadecimal | 3 | 3 | 3 | 4 | 3 | 5 | 3 | 6 | 3 | 7 |
| Binary | 0011 | 0011 | 0011 | 0100 | 0000 | 0101 | 0011 | 0110 | 0011 | 0111 |
| Decimal | 51 | 52 | 53 | 54 | 55 |
| ASCII | 3 | 4 | 5 | 6 | 7 |

Programming Hint: The name for this variable in code will be IP_ICMP_Data_PING.

2.2.23 IP PDU for the selected HTTP PDU

IP PDU > IP Version for the selected HTTP PDU

Field Name: IP Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming hint: The name for this variable in code will be IP_Version_HTTP.

IP PDU> Internet Header Length for the selected HTTP PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4-bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |
| Decimal | 5 |

Programming hint: The name for this variable in code will be IP_IHL_HTTP.

IP PDU > Type of Service for the selected HTTP PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 00

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |
| Decimal | 00 |

Programming hint: The name for this variable in code will be IP_TypeOfService_HTTP.

IP PDU > Total Length of Ethernet Frame for the selected HTTP PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key:  Not applicable

Data values (hexadecimal):  570

Data values in other bases:

| Hexadecimal | 0 | 2 | 3 | A |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0010 | 0011 | 1010 |
| Decimal | 2 | 58 |
| ASCII | © | : |

Programming hint: The name for this variable in code will be IP_TotalLength_HTTP.

IP PDU > Identification for the selected HTTP PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet.

Field Key:  Not applicable

Data value (hexadecimal): 3C 05

Data values in other bases:

| Hexadecimal | 3 | C | 0 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0000 | 0101 |

Programming hint: The name for this variable in code will be IP_Identification_HTTP,

IP PDU > Flags for the selected HTTP PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Programming hint: The name for this variable in code will be IP_Flags_HTTP.

IP PDU > Fragment Offset for the selected HTTP PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0 0000 0000 0000

Programming hint: The name for this variable in code will be IP_FragmentOffset_HTTP.

IP PDU > Time to Live for the selected HTTP PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bound the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming hint: The name for this variable in code will be IP_TimeToLive_HTTP.

IP PDU > Protocol for the selected HTTP PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	 Protocol

0 	  0	Reserved					22		16	 Multiplexing

1 	  1	ICMP						23		17	 DCN

2	  2	Unassigned					24		18	 TAC Monitoring

3 	  3	Gateway-to-Gateway				25-76		19-4C	 Unassigned

4 	  4	CMCC Gateway Monitoring Message	77		4D	 Any local network

5	  5	ST						100		64	 SATNET and Backroom EXPAK

6	  6	TCP						101		65	 MIT Subnet Support

7	  7	UCL						102-104	66-68	 Unassigned

10	  A	Unassigned					105		69	 SATNET Monitoring

11	  B	Secure						106		6A	 Unassigned

12	  C	BBN RCC Monitoring			107		6B	 Internet Packet Core Utility

13	  D	NVP						110-113	6E-71	 Unassigned

14	  E	PUP						114		72	 Backroom SATNET Monitoring

15	  F	Pluribus					115		73	 Unassigned

16	 10	Telnet						116		74	 WIDEBAND Monitoring

17	 11	XNET						117		75	 WIDEBAND EXPAK

20	 14	Chaos						120-376	78-178  Unassigned

21	 15	User Datagram				377		179	  Reserved

Data value (hexadecimal): 06

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |
| Decimal | 6 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming hint: The name for this variable in code will be IP_Protocol_HTTP.

IP PDU > Header Checksum for the selected HTTP PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): 7A F7

Data values in other bases:

| Hexadecimal | 7 | A | 5 | 7 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 1010 | 0101 | 0111 |

Programming hint: The name for this variable in code will be IP_HeaderChecksum_HTTP.

IP PDU > Source Address for the selected HTTP PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value (decimal):  192.168.0.12

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 0 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0000 | 1100 |
| Decimal | 192 | 168 | 0 | 12 |

Programming hint: The name for this variable in code will be IP_SourceAddress_HTTP.

IP PDU > Destination Address for the selected HTTP PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key: Not applicable

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192 | 168 | 0 | 101 |

Programming hint: The name for this variable in code will be IP_DestinationAddress_HTTP.

IP PDU > Options and Padding for the selected HTTP PDU

Field Name:  Options and Padding

Purpose and Definition:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Field Key:  Not applicable

Data values:  Not applicable

Data values in other bases:  Not applicable

Programming hint: The name for this variable in code will be IP_OptionsPadding_HTTP.

IP PDU > Data for the selected HTTP PDU

Field Name:  Data

Purpose and Definition:  The Data is a variable length field which contains the actual data that is being sent from one host to another.  The data field may start with a Layer 4 header, which will give additional instructions to the application that will be receiving the data; alternately, it may be an ICMP header and not contain any user data at all.

Field Key:  Not applicable

Data values (hexadecimal) :  (TCP) 80 30 00 15 81 A5 16 6C 87 A3 53 5D 80 18 16 D0 11 F4 00 00 01 01 08 0A 1B 25 F3 A1 0b DD 73 58

(FTP) 50 41 53 53 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

Data values in other bases:

Hexadecimal: (TCP) 0 x 80 30 00 15 81 A5 16 6C 87 A3 53 5D 80 18 16 D0 11 F4 00 00 01 01 08 0A 1B 25 F3 A1 0B DD 73 58

(FTP) 50 41 53 53 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

ASCII:  (TCP) ↑ 0 © © ↑ ↑ © ↑ ↑ S ] ↑ © © ↑ © ↑ © © © © © © © % ↑ ↑ © ↑ s X

(FTP) P A S S S © f 1 a 2 k 3 u s e r © ©

Programming hint: The name for this variable in code will be IP_Data_HTTP.

2.2.24 TCP PDU for the selected HTTP PDU

IP > TCP PDU > Source Port for the selected HTTP PDU

Field Name:  Source Port

Purpose and Definition:

This 16-bit number represents the name of the application that sent the data in the IP packet.

Field Key:  Not applicable

Data value: www (80)

Data values in other bases:

| Hexadecimal | 0 | 0 | 5 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0101 | 0000 |
| Decimal | 0 | 80 |
| ASCII | © | P |

Programming hint: The name for this variable in code will be IP_TCP_SourcePort_HTTP.

IP > TCP PDU > Destination Port for the selected HTTP PDU

Field Name: Destination Port

Purpose and Definition:
This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

Field Key:

This key indicates assigned port number values:

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (decimal): 4255

Data values in other bases:

| Hexadecimal | 1 | 0 | 9 | F |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0000 | 1001 | 1111 |
| Decimal | 16 | 159 |
| ASCII | © |  |

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

Programming hint: The name for this variable in code will be IP_TCP_DestinationPort_HTTP.

IP > TCP PDU > Sequence Number for the selected HTTP PDU

Field Name:  Sequence Number

Purpose and Definition:
TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Field Key:  Not applicable

Data value (decimal): 988014608

Data values in other bases:

| Hexadecimal | 3 | A | E | 3 | E | 8 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1010 | 1110 | 0011 | 1110 | 1000 | 0001 | 0000 |
| Decimal | 58 | 227 | 232 | 16 |
| ASCII | : |  |  | © |

Programming hint: The name for this variable in code will be IP_TCP_SequenceNumber_HTTP.

IP > TCP PDU > Acknowledgement Number for the selected HTTP PDU

Field Name: Acknowledgement Number

Purpose and Definition:
This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Field Key:  Not applicable

Data value: 1398299764

Data values in other bases:

| Hexadecimal | 5 | 3 | 5 | 8 | 5 | C | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0011 | 0101 | 0111 | 0101 | 1010 | 0111 | 0100 |
| Decimal | 83 | 88 | 92 | 116 |
| ASCII | S | X | \ | t |

Programming hint: The name for this variable in code will be IP_TCP_AcknowledgmentNumber_HTTP.

IP > TCP PDU > Header Length or Offset for the selected HTTP PDU

Field Name:  Header Length or Offset

Purpose and Definition:
This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header.

Field Key:  Not applicable

Data value (bytes): 32

Data values in other bases:

| Hexadecimal | 8 | 0 |
| --- | --- | --- |
| Binary | 1000 | 0000 |
| Decimal | 128 |
| ASCII |  |

Programming hint: The name for this variable in code will be IP_TCP_IHL_HTTP.

IP > TCP PDU > Control Flags for the selected HTTP PDU

Field Name:  Control Flags

Purpose and Definition:
Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:

- Urgent (URG)

- Acknowledgement (ACK)

- Push (PSH)

- Reset (RST)

- Synchronize (SYN)

- Finish (FIN)

Data value (binary): 01 1000

Data values in other bases:  Not applicable

Programming hint: The name for this variable in code will be IP_TCP_Flags_HTTP.

IP > TCP PDU > Window Size for the selected HTTP PDU

Field Name:  Window Size

Purpose and Definition:
Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:  Not applicable

Data value (decimal): 7504

Data values in other bases:

| Hexadecimal | 1 | D | 5 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 1101 | 0101 | 0000 |
| Decimal | 29 | 80 |
| ASCII | © | P |

Programming hint: The name for this variable in code will be IP_TCP_WindowSize_HTTP.

IP > TCP PDU > Urgent Pointer for the selected HTTP PDU

Field Name: Urgent Pointer

Purpose and Definition:
If the Urgent flag is set to on, this value indicates where the urgent data is located.

Information Key:  Not applicable

Data value:  Not applicable

Data values in other bases:  Not applicable

Programming hint: The name for this variable in code will be IP_TCP_UrgentPointer_HTTP.

IP > TCP PDU > Checksum for the selected HTTP PDU

Field Name:  Checksum

Purpose and Definition:
Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Field Key:  Not applicable

Data value (hexadecimal): F0 F6

Data values in other bases:

| Hexadecimal | F | 0 | F | 6 |
| --- | --- | --- | --- | --- |
| Binary | 1111 | 0000 | 1111 | 0110 |
| Decimal | 240 | 246 |
| ASCII |  |  |

Programming hint: The name for this variable in code will be IP_TCP_Checksum_HTTP.

IP > TCP PDU > Options and Padding for the selected HTTP PDU

Field Name: Options and Padding

Purpose and Definition:
Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits.

Field Key:  Not applicable

Data value (hexadecimal): 08 0A 39 22 DB 5B 06 2F 44 96

Data values in other bases:

| Hexadecimal | 0 | 8 | 0 | A | 3 | 9 | 2 | 2 | D | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 1000 | 0000 | 1010 | 0011 | 1001 | 0010 | 0010 | 1101 | 1011 |
| Decimal | 8 | 10 | 57 | 34 | 219 |
| ASCII | © | © | 9 | “ |  |

| Hexadecimal | 5 | B | 0 | 6 | 2 | F | 4 | 4 | 9 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 1011 | 0000 | 0110 | 0010 | 1111 | 0100 | 0100 | 1001 | 0110 |
| Decimal | 91 | 6 | 47 | 68 | 150 |
| ASCII | [ | © | / | F |  |

Programming hint: The name for this variable in code will be IP_TCP_Options_HTTP.

2.2.25 HTTP PDU for the selected HTTP PDU

IP > TCP > HTTP PDU > Content Type for the selected HTTP PDU

Field Name: Content Type

Purpose and Definition: The Content-Type entity-header field indicates the media type of the Entity-Body sent to the recipient.

Field Key:  Not applicable

Data value (ASCII): text/html; charset=iso – 8859-1\r\n

Data values in other bases:

| Hexadecimal | 4 | 3 | 6 | F | 6 | E | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0011 | 0110 | 1111 | 0110 | 1110 | 0111 | 0100 |
| Decimal | 67 | 111 | 110 | 116 |
| ASCII | C | o | n | t |

| Hexadecimal | 6 | 5 | 6 | E | 7 | 4 | 2 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 1110 | 0111 | 0100 | 0010 | 1101 |
| Decimal | 101 | 110 | 116 | 45 |
| ASCII | e | n | t | - |

| Hexadecimal | 5 | 4 | 7 | 9 | 7 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0100 | 0111 | 1001 | 0111 | 0000 | 0110 | 0101 |
| Decimal | 84 | 121 | 112 | 101 |
| ASCII | T | y | p | e |

| Hexadecimal | 3 | A | 2 | 0 | 7 | 4 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1010 | 0010 | 0000 | 0111 | 0100 | 0110 | 0101 |
| Decimal | 58 | 32 | 116 | 101 |
| ASCII | : |  | t | e |

| Hexadecimal | 7 | 8 | 7 | 4 | 2 | F | 6 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 1000 | 0111 | 0100 | 0010 | 1111 | 0110 | 1000 |
| Decimal | 120 | 116 | 47 | 104 |
| ASCII | x | t | / | h |

| Hexadecimal | 7 | 4 | 6 | D | 6 | C | 3 | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0100 | 0110 | 1101 | 0110 | 1100 | 0011 | 1011 |
| Decimal | 116 | 109 | 108 | 59 |
| ASCII | t | m | l | ; |

| Hexadecimal | 2 | 0 | 6 | 3 | 6 | 8 | 6 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 0011 | 0110 | 1000 | 0110 | 0001 |
| Decimal | 32 | 99 | 104 | 97 |
| ASCII |  | c | h | a |

| Hexadecimal | 7 | 2 | 7 | 3 | 6 | 5 | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0111 | 0011 | 0110 | 0101 | 0111 | 0100 |
| Decimal | 114 | 115 | 101 | 116 |
| ASCII | r | s | e | t |

| Hexadecimal | 3 | D | 6 | 9 | 7 | 3 | 6 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1101 | 0110 | 1001 | 0111 | 0011 | 0110 | 1111 |
| Decimal | 61 | 105 | 115 | 111 |
| ASCII | = | i | s | o |

| Hexadecimal | 2 | D | 3 | 8 | 3 | 8 | 3 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1101 | 0011 | 1000 | 0011 | 1000 | 0011 | 0101 |
| Decimal | 45 | 56 | 56 | 53 |
| ASCII | - | 8 | 8 | 5 |

| Hexadecimal | 3 | 9 | 2 | D | 3 | 1 | 0 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1001 | 0010 | 1101 | 0011 | 0001 | 0000 | 1101 |
| Decimal | 57 | 45 | 49 | 13 |
| ASCII | 9 | - | 1 | \r |

| Hexadecimal | 0 | A |
| --- | --- | --- |
| Binary | 0000 | 1010 |
| Decimal | 10 |
| ASCII | \n |

Programmer’s Hint: The name for this variable in code will be IP_TCP_HTTP_Content-Type_HTTP.

IP > TCP > HTTP PDU > Date for the selected HTTP PDU

Field Name: Date

Purpose and Definition: This field contains the date and time on which the web page was accessed.

Field Key:  Not applicable

Data value (ASCII): Date: Tue, 03 Feb 2004 23:08:10 GMT\r\n

Data values in other bases:

| Hexadecimal | 4 | 6 | 6 | 1 | 7 | 4 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0110 | 0110 | 0001 | 0111 | 0100 | 0110 | 0101 |
| Decimal | 70 | 97 | 116 | 101 |
| ASCII | D | a | t | e |

| Hexadecimal | 3 | A | 2 | 0 | 5 | 4 | 7 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1010 | 0010 | 0000 | 0101 | 0100 | 0111 | 0101 |
| Decimal | 58 | 32 | 84 | 117 |
| ASCII | : |  | T | u |

| Hexadecimal | 6 | 5 | 2 | C | 2 | 0 | 3 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0010 | 1100 | 0010 | 0000 | 0011 | 0000 |
| Decimal | 101 | 44 | 32 | 48 |
| ASCII | e | , |  | 0 |

| Hexadecimal | 3 | 3 | 2 | 0 | 4 | 6 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0011 | 0010 | 0000 | 0100 | 0110 | 0110 | 0101 |
| Decimal |  |  |  |  |
| ASCII | 3 |  | F | e |

| Hexadecimal | 6 | 2 | 2 | 0 | 3 | 2 | 3 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0010 | 0010 | 0000 | 0011 | 0010 | 0011 | 0000 |
| Decimal | 98 | 32 | 50 | 48 |
| ASCII | b |  | 2 | 0 |

| Hexadecimal | 3 | 0 | 3 | 4 | 3 | 2 | 3 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0011 | 0100 | 0011 | 0010 | 0011 | 0011 |
| Decimal | 48 | 52 | 50 | 51 |
| ASCII | 0 | 4 | 2 | 3 |

| Hexadecimal | 3 | A | 3 | 0 | 3 | 8 | 3 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1010 | 0011 | 0000 | 0011 | 1000 | 0011 | 1010 |
| Decimal | 58 | 48 | 56 | 58 |
| ASCII | : | 0 | 8 | : |

| Hexadecimal | 3 | 1 | 3 | 0 | 2 | 0 | 4 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0001 | 0011 | 0000 | 0010 | 0000 | 0100 | 0111 |
| Decimal | 49 | 48 | 32 | 71 |
| ASCII | 1 | 0 |  | G |

| Hexadecimal | 4 | D | 5 | 4 | 0 | D | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1101 | 0101 | 0100 | 0000 | 1101 | 0000 | 1010 |
| Decimal | 77 | 84 | 13 | 10 |
| ASCII | M | T | \r | \n |

Programmer’s Hint: The name for this variable in code will be IP_TCP_HTTP_Date_HTTP.

IP > TCP > HTTP PDU > HTTP for the selected HTTP PDU

Field Name: HTTP

Purpose and Definition: This field displays the category of the page that is being displayed.

Field Key:  Not applicable

Data value (ASCII): HTTP/1.1 404 Not Found\r\n

Data values in other bases:

| Hexadecimal | 4 | 8 | 5 | 4 | 5 | 4 | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1000 | 0101 | 0100 | 0101 | 0100 | 0101 | 0000 |
| Decimal | 72 | 84 | 84 | 80 |
| ASCII | H | T | T | P |

| Hexadecimal | 2 | F | 3 | 1 | 2 | E | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0011 | 0001 | 0010 | 1110 | 0011 | 0001 |
| Decimal | 47 | 49 | 46 | 49 |
| ASCII | / | 1 | . | 1 |

| Hexadecimal | 2 | 0 | 3 | 4 | 3 | 0 | 3 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0011 | 0100 | 0011 | 0000 | 0011 | 0100 |
| Decimal | 32 | 52 | 48 | 52 |
| ASCII |  | 4 | 0 | 4 |

| Hexadecimal | 2 | 0 | 4 | E | 6 | F | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0100 | 1110 | 0110 | 1111 | 0111 | 0100 |
| Decimal | 32 | 78 | 111 | 116 |
| ASCII |  | N | o | t |

| Hexadecimal | 2 | 0 | 4 | 6 | 6 | F | 7 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0100 | 0110 | 0110 | 1111 | 0111 | 0101 |
| Decimal | 32 | 70 | 111 | 117 |
| ASCII |  | F | o | u |

| Hexadecimal | 6 | E | 6 | 4 | 0 | D | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1110 | 0110 | 0100 | 0000 | 1101 | 0000 | 1010 |
| Decimal | 110 | 100 | 13 | 10 |
| ASCII | n | d | \r | \n |

Programmer’s Hint: The name for this variable in code will be IP_TCP_HTTP_HTTP_HTTP.

IP > TCP > HTTP PDU > Server for the selected HTTP PDU

Field Name: Server

Purpose and Definition: The Server response-header field contains information about the software used by the origin server to handle the request.

Field Key:  Not applicable

Data value (ASCII): Server: Apache/1.3.24 (Unix) PHP/4.2.1\r\n

Data values in other bases:

| Hexadecimal | 5 | 3 | 6 | 5 | 7 | 2 | 7 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0011 | 0110 | 0101 | 0111 | 0010 | 0111 | 0110 |
| Decimal | 83 | 101 | 114 | 118 |
| ASCII | S | e | r | v |

| Hexadecimal | 6 | 5 | 7 | 2 | 3 | A | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0111 | 0010 | 0011 | 1010 | 0010 | 0000 |
| Decimal | 101 | 114 | 58 | 32 |
| ASCII | e | r | : |  |

| Hexadecimal | 4 | 1 | 7 | 0 | 6 | 1 | 6 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0001 | 0111 | 0000 | 0110 | 0001 | 0110 | 0011 |
| Decimal | 65 | 112 | 97 | 99 |
| ASCII | A | p | a | c |

| Hexadecimal | 6 | 8 | 6 | 5 | 2 | F | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1000 | 0110 | 0101 | 0010 | 1111 | 0011 | 0001 |
| Decimal | 104 | 101 | 47 | 49 |
| ASCII | h | e | / | 1 |

| Hexadecimal | 2 | E | 3 | 3 | 2 | E | 3 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0011 | 0011 | 0010 | 1110 | 0011 | 0010 |
| Decimal | 46 | 51 | 46 | 50 |
| ASCII | . | 3 | . | 2 |

| Hexadecimal | 3 | 4 | 2 | 0 | 2 | 8 | 5 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0100 | 0010 | 0000 | 0010 | 1000 | 0101 | 0101 |
| Decimal | 52 | 32 | 40 | 85 |
| ASCII | 4 |  | ( | U |

| Hexadecimal | 6 | E | 6 | 9 | 7 | 8 | 2 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1110 | 0110 | 1001 | 0111 | 1000 | 0010 | 1001 |
| Decimal | 110 | 105 | 120 | 41 |
| ASCII | n | i | x | ) |

| Hexadecimal | 2 | 0 | 5 | 0 | 4 | 8 | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0101 | 0000 | 0100 | 1000 | 0101 | 0000 |
| Decimal | 32 | 80 | 72 | 80 |
| ASCII |  | P | H | P |

| Hexadecimal | 2 | 5 | 3 | 4 | 2 | E | 3 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0101 | 0011 | 0100 | 0010 | 1110 | 0011 | 0010 |
| Decimal | 37 | 52 | 46 | 50 |
| ASCII | / | 4 | . | 2 |

| Hexadecimal | 2 | E | 3 | 1 | 0 | D | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0011 | 0001 | 0000 | 1101 | 0000 | 1010 |
| Decimal | 46 | 49 | 13 | 10 |
| ASCII | . | 1 | \r | \n |

Programmer’s Hint: The name for this variable in code will be IP_TCP_HTTP_Server_HTTP.

IP > TCP > HTTP PDU > Data for the selected HTTP PDU

Field Name: Data

Purpose and Definition: This field stores the information that is actually contained in the HTTP Protocol.

Field Key:  Not applicable

Data value (ASCII): <!DOCTYPE HTML PUBLIC “-//IETF//DTD HTML 2.0//EN”>\n

<HTML><HEAD>\n

<TITLE>404 Not Found</TITLE>\n

</HEAD><BODY>\n

<H1>Not Found</H1>\n

The requested URL /~csis410/2003/bluetech/Requirements Speicfication Document Final-files/image002.gif was not found on this server.<p>\n

<HR>\n

<ADDRESS>Apache/1.3.24 Server at ares.cs.siena.edu Port 80</ADDRESS>\n

</BODY></HTML>\n

Data values in other bases:

| Hexadecimal | 3 | C | 2 | 1 | 4 | 4 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0010 | 0001 | 0100 | 0100 | 0100 | 0101 |
| Decimal | 60 | 33 | 68 | 69 |
| ASCII | < | ! | D | O |

| Hexadecimal | 4 | 3 | 5 | 4 | 5 | 9 | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0011 | 0101 | 0100 | 0101 | 1001 | 0101 | 0000 |
| Decimal | 67 | 84 | 89 | 80 |
| ASCII | C | T | Y | P |

| Hexadecimal | 4 | 5 | 2 | 0 | 4 | 8 | 5 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0101 | 0010 | 0000 | 0100 | 1000 | 0101 | 0100 |
| Decimal | 69 | 32 | 72 | 84 |
| ASCII | E |  | H | T |

| Hexadecimal | 4 | D | 4 | C | 2 | 0 | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1101 | 0110 | 1100 | 0010 | 0000 | 0101 | 0000 |
| Decimal | 77 | 76 | 32 | 80 |
| ASCII | M | L |  | P |

| Hexadecimal | 5 | 5 | 4 | 2 | 4 | C | 4 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0101 | 0100 | 0010 | 0100 | 1100 | 0100 | 1001 |
| Decimal | 85 | 66 | 76 | 73 |
| ASCII | U | B | L | I |
| Hexadecimal | 4 | 3 | 2 | 0 | 2 | 2 | 2 | D |
| Binary | 0100 | 0011 | 0010 | 0000 | 0010 | 0010 | 0010 | 1101 |
| Decimal | 67 | 32 | 34 | 45 |
| ASCII | C |  | “ | - |

| Hexadecimal | 2 | F | 2 | F | 4 | 9 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0010 | 1111 | 0100 | 1001 | 0100 | 0101 |
| Decimal | 47 | 47 | 73 | 69 |
| ASCII | / | / | I | E |

| Hexadecimal | 5 | 4 | 4 | 6 | 2 | F | 2 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0100 | 0100 | 0110 | 0010 | 1111 | 0010 | 1111 |
| Decimal | 84 | 70 | 47 | 47 |
| ASCII | T | F | / | / |

| Hexadecimal | 4 | 4 | 5 | 4 | 4 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0100 | 0101 | 0100 | 0100 | 0100 | 0010 | 0000 |
| Decimal | 68 | 84 | 68 | 32 |
| ASCII | D | T | D |  |

| Hexadecimal | 4 | 8 | 5 | 4 | 4 | D | 4 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1000 | 0101 | 0100 | 0100 | 1101 | 0100 | 1100 |
| Decimal | 72 | 84 | 77 | 76 |
| ASCII | H | T | M | L |

| Hexadecimal | 2 | 0 | 3 | 2 | 2 | E | 3 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0011 | 0010 | 0010 | 1110 | 0011 | 0000 |
| Decimal | 32 | 50 | 46 | 48 |
| ASCII |  | 2 | . | 0 |

| Hexadecimal | 2 | F | 2 | F | 4 | 5 | 4 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0010 | 1111 | 0100 | 0101 | 0100 | 1110 |
| Decimal | 47 | 47 | 69 | 78 |
| ASCII | / | / | E | N |

| Hexadecimal | 2 | 2 | 3 | E | 0 | A | 3 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0010 | 0011 | 1110 | 0000 | 1010 | 0011 | 1100 |
| Decimal | 34 | 62 | 10 | 60 |
| ASCII | “ | > | \n | < |

| Hexadecimal | 4 | 8 | 5 | 4 | 4 | D | 4 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1000 | 0101 | 0100 | 0100 | 1101 | 0100 | 1100 |
| Decimal | 72 | 84 | 77 | 76 |
| ASCII | H | T | M | L |

| Hexadecimal | 3 | E | 3 | C | 4 | 8 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1110 | 0011 | 1100 | 0100 | 1000 | 0100 | 0101 |
| Decimal | 62 | 60 | 72 | 69 |
| ASCII | > | < | H | E |

| Hexadecimal | 4 | 1 | 4 | 4 | 3 | E | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0001 | 0100 | 0100 | 0011 | 1110 | 0000 | 1010 |
| Decimal | 65 | 68 | 62 | 10 |
| ASCII | A | D | > | \n |

| Hexadecimal | 3 | C | 5 | 4 | 4 | 9 | 5 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0101 | 0100 | 0100 | 1001 | 0101 | 0100 |
| Decimal | 60 | 84 | 73 | 84 |
| ASCII | < | T | I | T |

| Hexadecimal | 4 | C | 4 | 5 | 3 | E | 3 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1100 | 0100 | 0101 | 0011 | 1110 | 0011 | 0100 |
| Decimal | 76 | 69 | 62 | 52 |
| ASCII | L | E | > | 4 |

| Hexadecimal | 3 | 0 | 3 | 4 | 2 | 0 | 4 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0011 | 0100 | 0010 | 0000 | 0100 | 1110 |
| Decimal | 48 | 52 | 32 | 78 |
| ASCII | 0 | 4 |  | N |

| Hexadecimal | 6 | F | 7 | 4 | 2 | 0 | 4 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0111 | 0100 | 0010 | 0000 | 0100 | 0110 |
| Decimal | 111 | 116 | 32 | 70 |
| ASCII | o | t |  | F |

| Hexadecimal | 6 | F | 7 | 5 | 6 | E | 6 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0111 | 0101 | 0110 | 1110 | 0110 | 0100 |
| Decimal | 111 | 117 | 110 | 100 |
| ASCII | o | u | n | d |

| Hexadecimal | 3 | C | 2 | F | 5 | 4 | 4 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0010 | 1111 | 0101 | 0100 | 0100 | 1001 |
| Decimal | 60 | 47 | 84 | 73 |
| ASCII | < | / | T | I |

| Hexadecimal | 5 | 4 | 4 | C | 4 | 5 | 3 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0100 | 0100 | 1100 | 0100 | 0101 | 0011 | 1110 |
| Decimal | 84 | 76 | 69 | 62 |
| ASCII | T | L | E | > |

| Hexadecimal | 0 | A | 3 | C | 2 | F | 4 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 1010 | 0011 | 1100 | 0010 | 1111 | 0100 | 1000 |
| Decimal | 10 | 60 | 47 | 72 |
| ASCII | \n | < | / | H |

| Hexadecimal | 4 | 5 | 4 | 1 | 4 | 4 | 3 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0101 | 0100 | 0001 | 0100 | 0100 | 0011 | 1110 |
| Decimal | 69 | 65 | 68 | 62 |
| ASCII | E | A | D | > |

| Hexadecimal | 3 | C | 4 | 2 | 4 | F | 4 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0100 | 0010 | 0100 | 1111 | 0100 | 0100 |
| Decimal | 60 | 66 | 79 | 68 |
| ASCII | < | B | O | D |

| Hexadecimal | 5 | 9 | 3 | E | 0 | A | 3 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 1001 | 0011 | 1110 | 0000 | 1010 | 0011 | 1100 |
| Decimal | 89 | 62 | 10 | 60 |
| ASCII | Y | > | \n | < |

| Hexadecimal | 4 | 8 | 3 | 1 | 3 | E | 4 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1000 | 0011 | 0001 | 0011 | 1110 | 0100 | 1110 |
| Decimal | 72 | 49 | 62 | 78 |
| ASCII | H | 1 | > | N |

| Hexadecimal | 6 | F | 7 | 4 | 2 | 0 | 4 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0111 | 0100 | 0010 | 0000 | 0100 | 0110 |
| Decimal | 111 | 116 | 32 | 70 |
| ASCII | o | t |  | F |

| Hexadecimal | 6 | F | 7 | 5 | 6 | E | 6 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1111 | 0111 | 0101 | 0110 | 1110 | 0110 | 0100 |
| Decimal | 111 | 117 | 110 | 100 |
| ASCII | o | u | n | d |

| Hexadecimal | 3 | C | 2 | F | 4 | 8 | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0010 | 1111 | 0100 | 1000 | 0011 | 0001 |
| Decimal | 60 | 47 | 72 | 49 |
| ASCII | < | / | H | 1 |

| Hexadecimal | 3 | E | 0 | A | 5 | 4 | 6 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1110 | 0000 | 1010 | 0101 | 0100 | 0110 | 1000 |
| Decimal | 62 | 10 | 84 | 104 |
| ASCII | > | \n | T | h |

| Hexadecimal | 6 | 5 | 2 | 0 | 7 | 2 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0010 | 0000 | 0111 | 0010 | 0110 | 0101 |
| Decimal | 101 | 32 | 114 | 101 |
| ASCII | e |  | r | e |

| Hexadecimal | 7 | 1 | 7 | 5 | 6 | 5 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0001 | 0111 | 0101 | 0110 | 0101 | 0111 | 0011 |
| Decimal | 113 | 117 | 101 | 115 |
| ASCII | q | u | e | s |

| Hexadecimal | 7 | 4 | 6 | 5 | 6 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0100 | 0110 | 0101 | 0110 | 0100 | 0010 | 0000 |
| Decimal | 116 | 101 | 100 | 32 |
| ASCII | t | e | d |  |

| Hexadecimal | 5 | 5 | 5 | 2 | 4 | C | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0101 | 0101 | 0010 | 0100 | 1100 | 0010 | 0000 |
| Decimal | 85 | 82 | 76 | 32 |
| ASCII | U | R | L |  |

| Hexadecimal | 2 | F | 7 | E | 6 | 3 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0111 | 1110 | 0110 | 0011 | 0111 | 0011 |
| Decimal | 47 | 126 | 99 | 115 |
| ASCII | / | ~ | c | s |

| Hexadecimal | 6 | 9 | 7 | 3 | 3 | 4 | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0111 | 0011 | 0011 | 0100 | 0011 | 0001 |
| Decimal | 105 | 115 | 52 | 49 |
| ASCII | i | s | 4 | 1 |

| Hexadecimal | 3 | 0 | 2 | F | 3 | 2 | 3 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0010 | 1111 | 0011 | 0010 | 0011 | 0000 |
| Decimal | 48 | 47 | 50 | 48 |
| ASCII | 0 | / | 2 | 0 |

| Hexadecimal | 3 | 0 | 3 | 3 | 2 | F | 6 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0011 | 0011 | 0010 | 1111 | 0110 | 0010 |
| Decimal | 48 | 51 | 47 | 98 |
| ASCII | 0 | 3 | / | b |

| Hexadecimal | 6 | C | 7 | 5 | 6 | 5 | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1100 | 0111 | 0101 | 0110 | 0101 | 0111 | 0100 |
| Decimal | 108 | 117 | 101 | 116 |
| ASCII | l | u | e | t |

| Hexadecimal | 6 | 5 | 6 | 3 | 6 | 8 | 2 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 0011 | 0110 | 1000 | 0010 | 1111 |
| Decimal | 101 | 99 | 104 | 47 |
| ASCII | e | c | h | / |

| Hexadecimal | 5 | 2 | 6 | 5 | 7 | 1 | 7 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0010 | 0110 | 0101 | 0111 | 0001 | 0111 | 0101 |
| Decimal | 82 | 101 | 113 | 117 |
| ASCII | R | e | q | u |

| Hexadecimal | 6 | 9 | 7 | 2 | 6 | 5 | 6 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0111 | 0010 | 0110 | 0101 | 0110 | 1101 |
| Decimal | 105 | 114 | 101 | 109 |
| ASCII | i | r | e | m |

| Hexadecimal | 6 | 5 | 6 | E | 7 | 4 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 1110 | 0111 | 0100 | 0111 | 0011 |
| Decimal | 101 | 110 | 116 | 115 |
| ASCII | e | n | t | s |

| Hexadecimal | 2 | 0 | 5 | 3 | 7 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0101 | 0011 | 0111 | 0000 | 0110 | 0101 |
| Decimal | 32 | 83 | 112 | 101 |
| ASCII |  | S | p | e |

| Hexadecimal | 6 | 3 | 6 | 9 | 6 | 6 | 6 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0011 | 0110 | 1001 | 0110 | 0110 | 0110 | 1001 |
| Decimal | 99 | 105 | 102 | 105 |
| ASCII | c | i | f | i |

| Hexadecimal | 6 | 3 | 6 | 1 | 7 | 4 | 6 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0011 | 0110 | 0001 | 0111 | 0100 | 0110 | 1001 |
| Decimal | 99 | 97 | 116 | 105 |
| ASCII | c | a | t | i |

| Hexadecimal | 6 | F | 6 | E | 2 | 0 | 4 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0110 | 1110 | 0010 | 0000 | 0100 | 0100 |
| Decimal | 111 | 110 | 32 | 68 |
| ASCII | o | n |  | D |

| Hexadecimal | 6 | F | 6 | 3 | 7 | 5 | 6 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0110 | 0011 | 0111 | 0101 | 0110 | 1101 |
| Decimal | 111 | 99 | 117 | 109 |
| ASCII | o | c | u | m |

| Hexadecimal | 6 | 5 | 6 | E | 7 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 1110 | 0111 | 0100 | 0010 | 0000 |
| Decimal | 101 | 110 | 116 | 32 |
| ASCII | e | n | t |  |

| Hexadecimal | 4 | 6 | 6 | 9 | 6 | E | 6 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0110 | 0110 | 1001 | 0110 | 1110 | 0110 | 0001 |
| Decimal | 70 | 105 | 110 | 97 |
| ASCII | F | i | n | a |

| Hexadecimal | 6 | C | 5 | F | 6 | 6 | 6 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1100 | 0101 | 1111 | 0110 | 0110 | 0110 | 1001 |
| Decimal | 108 | 95 | 102 | 105 |
| ASCII | l | - | f | i |

| Hexadecimal | 6 | C | 6 | 5 | 7 | 3 | 2 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1100 | 0110 | 0101 | 0111 | 0011 | 0010 | 1111 |
| Decimal | 63 | 101 | 115 | 47 |
| ASCII | l | e | s | / |

| Hexadecimal | 6 | 9 | 6 | D | 6 | 1 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0110 | 1101 | 0110 | 0001 | 0110 | 0111 |
| Decimal | 105 | 109 | 97 | 103 |
| ASCII | i | m | a | g |

| Hexadecimal | 6 | 5 | 3 | 0 | 3 | 0 | 3 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0011 | 0000 | 0011 | 0000 | 0011 | 0010 |
| Decimal | 101 | 48 | 48 | 50 |
| ASCII | e | 0 | 0 | 2 |

| Hexadecimal | 2 | E | 6 | 7 | 6 | 9 | 6 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0110 | 0111 | 0110 | 1001 | 0110 | 0110 |
| Decimal | 46 | 103 | 105 | 102 |
| ASCII | . | g | i | f |

| Hexadecimal | 2 | 0 | 7 | 7 | 6 | 1 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0001 | 0000 | 0111 | 0111 | 0110 | 0001 | 0111 | 0011 |
| Decimal | 32 | 119 | 97 | 115 |
| ASCII |  | w | a | s |

| Hexadecimal | 2 | 0 | 6 | E | 6 | F | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 1110 | 0110 | 1111 | 0111 | 0100 |
| Decimal | 32 | 110 | 111 | 116 |
| ASCII |  | n | o | t |

| Hexadecimal | 2 | 0 | 6 | 6 | 6 | F | 7 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 0110 | 0110 | 1111 | 0111 | 0101 |
| Decimal | 32 | 102 | 111 | 117 |
| ASCII |  | f | o | u |

| Hexadecimal | 6 | E | 6 | 4 | 2 | 0 | 6 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1110 | 0110 | 0100 | 0010 | 0000 | 0110 | 1111 |
| Decimal | 110 | 100 | 32 | 111 |
| ASCII | n | d |  | o |

| Hexadecimal | 6 | E | 2 | 0 | 7 | 4 | 6 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1110 | 0010 | 0000 | 0111 | 0100 | 0110 | 1000 |
| Decimal | 110 | 32 | 116 | 104 |
| ASCII | n |  | t | h |

| Hexadecimal | 6 | 9 | 7 | 3 | 2 | 0 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0111 | 0011 | 0010 | 0000 | 0111 | 0011 |
| Decimal | 105 | 115 | 32 | 115 |
| ASCII | i | s |  | s |

| Hexadecimal | 6 | 5 | 7 | 2 | 7 | 6 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0111 | 0010 | 0111 | 0110 | 0110 | 0101 |
| Decimal | 101 | 114 | 118 | 101 |
| ASCII | e | r | v | e |

| Hexadecimal | 7 | 2 | 2 | E | 3 | C | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0010 | 1110 | 0011 | 1100 | 0101 | 0000 |
| Decimal | 114 | 46 | 60 | 80 |
| ASCII | r | . | < | p |

| Hexadecimal | 3 | E | 0 | A | 3 | C | 4 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1110 | 0000 | 1010 | 0011 | 1100 | 0100 | 1000 |
| Decimal |  |  |  |  |
| ASCII | > | \n | < | H |

| Hexadecimal | 5 | 2 | 3 | E | 0 | 4 | 3 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0010 | 0011 | 1110 | 0000 | 0100 | 0011 | 1100 |
| Decimal | 82 | 62 | 10 | 60 |
| ASCII | R | > | \n | < |

| Hexadecimal | 4 | 1 | 4 | 4 | 4 | 4 | 5 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0001 | 0100 | 0100 | 0100 | 0100 | 0101 | 0010 |
| Decimal | 65 | 68 | 68 | 82 |
| ASCII | A | D | D | R |

| Hexadecimal | 4 | 5 | 5 | 3 | 5 | 3 | 3 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0101 | 0101 | 0011 | 0101 | 0011 | 0011 | 1110 |
| Decimal | 69 | 83 | 83 | 62 |
| ASCII | E | S | S | > |

| Hexadecimal | 4 | 1 | 7 | 0 | 6 | 1 | 6 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0001 | 0111 | 0000 | 0110 | 0001 | 0110 | 0011 |
| Decimal | 65 | 112 | 97 | 99 |
| ASCII | A | p | a | c |

| Hexadecimal | 6 | 8 | 6 | 5 | 2 | F | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1000 | 0110 | 0101 | 0010 | 1111 | 0011 | 0001 |
| Decimal | 104 | 101 | 47 | 49 |
| ASCII | h | e | / | 1 |

| Hexadecimal | 2 | E | 3 | 3 | 2 | E | 3 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0011 | 0011 | 0010 | 1110 | 0011 | 0010 |
| Decimal | 46 | 51 | 46 | 50 |
| ASCII | . | 3 | . | 2 |

| Hexadecimal | 3 | 4 | 2 | 0 | 5 | 3 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0100 | 0010 | 0000 | 0101 | 0011 | 0110 | 0101 |
| Decimal | 52 | 32 | 83 | 101 |
| ASCII | 4 |  | S | e |

| Hexadecimal | 7 | 2 | 7 | 6 | 6 | 5 | 7 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0111 | 0110 | 0110 | 0101 | 0111 | 0010 |
| Decimal |  |  |  |  |
| ASCII | r | v | e | r |

| Hexadecimal | 2 | 0 | 6 | 1 | 7 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 0001 | 0111 | 0100 | 0010 | 0000 |
| Decimal | 32 | 97 | 116 | 323 |
| ASCII |  | a | t |  |

| Hexadecimal | 3 | 1 | 7 | 2 | 6 | 5 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0001 | 0111 | 0010 | 0110 | 0101 | 0111 | 0011 |
| Decimal | 97 | 114 | 101 | 115 |
| ASCII | a | r | e | s |

| Hexadecimal | 2 | E | 6 | 3 | 7 | 3 | 2 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0110 | 0011 | 0111 | 0011 | 0010 | 1110 |
| Decimal | 46 | 99 | 115 | 46 |
| ASCII | . | c | s | . |

| Hexadecimal | 7 | 3 | 6 | 9 | 6 | 5 | 6 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0011 | 0110 | 1001 | 0110 | 0101 | 0110 | 1110 |
| Decimal | 115 | 105 | 101 | 110 |
| ASCII | s | i | e | n |

| Hexadecimal | 6 | 1 | 2 | E | 6 | 5 | 6 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0001 | 0010 | 1110 | 0110 | 0101 | 0110 | 0100 |
| Decimal | 97 | 46 | 101 | 100 |
| ASCII | a | . | e | d |

| Hexadecimal | 7 | 5 | 2 | 0 | 5 | 0 | 6 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0101 | 0010 | 0000 | 0101 | 0000 | 0110 | 1111 |
| Decimal | 117 | 32 | 80 | 111 |
| ASCII | u |  | P | o |

| Hexadecimal | 7 | 2 | 7 | 4 | 2 | 0 | 3 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0111 | 0100 | 0010 | 0000 | 0011 | 1000 |
| Decimal | 114 | 116 | 32 | 56 |
| ASCII | r | t |  | 8 |

| Hexadecimal | 3 | 0 | 3 | C | 2 | F | 4 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0010 | 1100 | 0010 | 1111 | 0100 | 0001 |
| Decimal | 48 | 60 | 47 | 65 |
| ASCII | 0 | < | / | A |

| Hexadecimal | 4 | 4 | 4 | 4 | 5 | 2 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0100 | 0100 | 0100 | 0101 | 0010 | 0100 | 0101 |
| Decimal | 68 | 68 | 82 | 69 |
| ASCII | D | D | R | E |

| Hexadecimal | 5 | 3 | 5 | 3 | 3 | E | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0011 | 0101 | 0011 | 0011 | 1110 | 0000 | 1010 |
| Decimal | 83 | 83 | 62 | 10 |
| ASCII | S | S | > | \n |

| Hexadecimal | 3 | C | 2 | F | 4 | 2 | 4 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0010 | 1111 | 0100 | 0010 | 0100 | 1111 |
| Decimal | 60 | 47 | 66 | 79 |
| ASCII | < | / | B | O |

| Hexadecimal | 4 | 4 | 5 | 9 | 3 | E | 3 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0100 | 0101 | 1001 | 0011 | 1110 | 0011 | 1100 |
| Decimal | 68 | 89 | 62 | 60 |
| ASCII | D | Y | > | < |

| Hexadecimal | 2 | F | 4 | 8 | 5 | 4 | 4 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0100 | 1000 | 0101 | 0100 | 0100 | 1101 |
| Decimal | 47 | 72 | 84 | 77 |
| ASCII | / | H | T | M |

| Hexadecimal | 4 | C | 3 | E | 0 | A |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1100 | 0011 | 1110 | 0000 | 1010 |
| Decimal | 76 | 62 | 10 |
| ASCII | L | > | \n |

Programmer’s Hint: The name for this variable in code will be IP_TCP_HTTP_Data_HTTP.

- Testing Requirements

3.1 Testing Overview

We will be assigning someone from outside of our company to test our software.  This will eliminate biases and create a fair environment to ensure that all requirements are met.

We will be conducting these tests for the detailed design portion of development, which is the basis for the final development of the software.

We will be implementing gray box testing in the detailed design portion of our development.  Gray box testing is a testing procedure done with some knowledge of how the internals work.

Attributes Tested:

The result from a right/left click of the mouse on the:

- Individual field of the packets

- Hierarchical tree

- Options

3.2 Test Cases

- Did the computer connect to the web-based client?

  - Does each screen load up promptly when navigating through the client?

  - Is scrolling to a minimum?

- At the main menu:

  - Do the buttons bring you to correct/next logical screen/PDU?

  - Does changing the radians show affect on all PDU’s?

  - Is the hierarchical tree dynamic?

  - Is the “Choose a Protocol” hierarchical tree displayed when the user clicks “Choose a Protocol?”

  - Does a message box appear when user selects “IPv6” stating that it is not currently available?

- Graphical User Interface (GUI):

  - Is the GUI clearly visible on 1024x768 projectors?

    - Is it visible from the farthest corners in the room?

  - Are all colors easily distinguishable?

  - Are information boxes placed so that the current PDU is not covered?

  - When a field is clicked, is the information box the same color as the field?

  - Does each protocol have a link to its RFC?

  - Testing Sheets

    - Functional Requirements

Functional Requirements

Date:

Tester:

Screen: 	Pass 		Fail

| Requirement | Actual Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| Contains information for various protocols. |  |  |  |  |

| Requirement | Actual Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| Produces GUI that colorfully and clearly displays contents of the specified protocol. |  |  |  |  |

| Requirement | Actual Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| Displays clearly on a 1024x768 pixel screen. |  |  |  |  |

| Requirement | Actual Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| Menus on top of screen should be visible on every page to allow user to change protocol, or switch between layers. |  |  |  |  |

| Requirement | Actual Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| Ability to view either an independent field or an entire protocol in a different radix |  |  |  |  |

Functional Requirements

| Requirement | Actual Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| Produces information box for each field of a protocol which displays Purpose of Field, Options for Pattern, Bit Pattern Form, and Minimum/Maximum Length |  |  |  |  |

| Requirement | Actual Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| Displays RFC link for entire protocol or specific field when available. |  |  |  |  |

    - Ethernet Testing Sheet

Screen: Ethernet

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: “Choose a Protocol” Button

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Tree with all possible protocols is displayed |  |  |  |

## Field Name: IPv4 Button

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | By default, IPv4 will be displayed |  |  |  |

## Field Name: IPv6 Button

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Message box will be displayed saying that IPv6 is currently not available |  |  |  |

## Field Name: Preamble Sof Sync Data Field

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Preamble information box is displayed in a magenta box |  |  |  |

## Field Name: Datalink Header

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Datalink information field is displayed in a green box |  |  |  |

Field Name: Frame Check Sequence (FCS)

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | FCS information field is displayed in a yellow box |  |  |  |

Screen: Ethernet

## Field Name: IP PDU

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | IP PDU information field is displayed in a cyan box |  |  |  |

## Field Name: “Different Protocol is Selected”

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Dynamic Road Map will change to show hierarchy of available protocols |  |  |  |

    - IP Testing Sheet

Screen: IP PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Version

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Version information field pops up in a pink box |  |  |  |

## Field Name: Internet Header Length

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Internet Header Length information field pops up in a cyan box |  |  |  |

## Field Name: Type of Service

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Type of Service information field pops up in a yellow box |  |  |  |

## Field Name: Total Length

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Total Length information field pops up in a green box |  |  |  |

Field Name: Identification

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Identification information field pops up in an orange box |  |  |  |

Screen: IP PDU

## Field Name: Flags

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Flags information field pops up in a cyan box |  |  |  |

## Field Name: Fragment Offset

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Fragment Offset information field pops up in a magenta box |  |  |  |

## Field Name: Time to Live

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Time to Live information field pops up in a cyan box |  |  |  |

## Field Name: Protocol

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Protocol information field pops up in a pink box |  |  |  |

## Field Name: Header Checksum

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Header Checksum information field pops up in a yellow box |  |  |  |

## Field Name: Source IP Address

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Source IP Address information field pops up in a green box |  |  |  |

Screen: IP PDU

## Field Name: Destination IP Address

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Destination IP Address information field pops up in an orange box |  |  |  |

## Field Name: Options

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Options information field pops up in a cyan box |  |  |  |

## Field Name: Data

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Data information field pops up in a magenta box |  |  |  |

    - TCP Testing Sheet

Screen: TCP PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Source Port

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Source Port information field pops up in a pink box |  |  |  |

## Field Name: Destination Port

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Destination Port information field pops up in a cyan box |  |  |  |

## Field Name: Sequence Number

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Sequence Number information field pops up in a yellow box |  |  |  |

## Field Name: Acknowledgement Number

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Acknowledgment Number information field pops up in a green box |  |  |  |

Field Name: Length

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Length information field pops up in a orange box |  |  |  |

Field Name: Reserved

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Reserved information field pops up in a magenta box |  |  |  |

Screen: TCP PDU

Field Name: URG

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | URG information field pops up in a orange box |  |  |  |

Field Name: ACK

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | ACK information field pops up in a pink box |  |  |  |

Field Name: PSH

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | PSH information field pops up in a cyan box |  |  |  |

Field Name: RST

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | RST information field pops up in a magenta box |  |  |  |

Field Name: SYN

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | SYN information field pops up in a green box |  |  |  |

Field Name: FIN

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | FIN information field pops up in a yellow box |  |  |  |

Field Name: Window Size

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Window Size information field pops up in pink box |  |  |  |

Screen: TCP PDU

Field Name: Checksum

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Checksum information field pops up in a green box |  |  |  |

Field Name: Urgent Pointer

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Urgent Pointer information field pops up in a yellow box |  |  |  |

Field Name: Options

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Options information field pops up in a magenta box |  |  |  |

Field Name: Data

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | FTP PDU pops up |  |  |  |

### FTP Testing Sheet

Screen: FTP PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Destination Address

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Destination Address information field pops up in the appropriate colored box |  |  |  |

## Field Name: Source Address

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Source Address information field pops up in the appropriate colored box |  |  |  |

Field Name: Pass

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Pass information field pops up in the appropriate colored box |  |  |  |

### ICMP Testing Sheet

Screen: ICMP PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Type

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Type information field pops up in an appropriately colored box |  |  |  |

## Field Name: Code

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Code information field pops up in an appropriately colored box |  |  |  |

## Field Name: Checksum

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Checksum information field pops up in an appropriately colored box |  |  |  |

## Field Name: Identifier

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Identifier information field pops up in an appropriately colored box |  |  |  |

Field Name: Sequence

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Sequence information field pops up in an appropriately colored box |  |  |  |

Screen: ICMP PDU

Date:

Tester:

Screen: 	Pass 		Fail

## Field Name: Data

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Data information field pops up in an appropriately colored box |  |  |  |

### SMTP Testing Sheet

Screen: SMTP PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Command

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Command information field pops up in an appropriately colored box |  |  |  |

## Field Name: Message

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Message information field pops up in an appropriately colored box |  |  |  |

### UDP Testing Sheet

Screen: UDP PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Source Port

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Source Port information field pops up in the appropriately colored box |  |  |  |

## Field Name: Destination Port

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Destination Port information field pops up in the appropriately colored box |  |  |  |

## Field Name: Length

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Length information field pops up in the appropriately colored box |  |  |  |

## Field Name: Checksum

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Checksum information field pops up in the appropriately colored box |  |  |  |

Field Name: Data

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Data information field pops up in the appropriately colored box |  |  |  |

### SNMP Testing Sheet

Screen: SNMP PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Version

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Version information field pops up in the appropriate colored box |  |  |  |

## Field Name: Community

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Community information field pops up in the appropriate colored box |  |  |  |

## Field Name: PDU Type

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | PDU information field pops up in the appropriate colored box |  |  |  |

## Field Name: Request ID

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Request ID information field pops up in the appropriate colored box |  |  |  |

Field Name: Error Status

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Error status information field pops up in the appropriate colored box |  |  |  |

Screen: SNMP PDU

## Field Name: Object Id

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Object information field pops up in the appropriate colored box |  |  |  |

## Field Name: Value Integer

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Value information field pops up in the appropriate colored box |  |  |  |

## Field Name: Value ID

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Value ID information field pops up in the appropriate colored box |  |  |  |

Field Name: Object ID

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Object information field pops up in the appropriate colored box |  |  |  |

### TELNET Testing Sheet

Screen: TELNET PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Data

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Data information field pops up in the appropriately colored box |  |  |  |

### SSH Testing Sheet

Screen: SSH PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Data

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Data information field pops up in the appropriately colored box |  |  |  |

### ARP Testing Sheet

Screen: ARP PDU

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Hardware Address Type

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Hardware Address Type information field pops up in the appropriately colored box |  |  |  |

## Field Name: Protocol Address Type

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Protocol Address Type information field pops up in the appropriately colored box |  |  |  |

Field Name: Hardware Address Length

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Hardware Address Length information field pops up in the appropriately colored box |  |  |  |

Field Name: Protocol Address Length

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Protocol Address Length information field pops up in the appropriately colored box |  |  |  |

Field Name: Operation

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Operation information field pops up in the appropriately colored box |  |  |  |

Screen: ARP PDU

Field Name: Sender Hardware Address

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Sender Hardware Address information field pops up in the appropriately colored box |  |  |  |

## Field Name: Protocol Address Type

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Protocol Address Type information field pops up in the appropriately colored box |  |  |  |

Field Name: Target Hardware Address

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Target Hardware Address information field pops up in the appropriately colored box |  |  |  |

Field Name: Target Protocol Address

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Target Protocol Address information field pops up in the appropriately colored box |  |  |  |

### PING Testing Sheet

Screen: PING

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Destination

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Destination information field pops up in the appropriately colored box |  |  |  |

## Field Name: Source

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Source information field pops up in the appropriately colored box |  |  |  |

## Field Name: Fragment

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Fragment offset information field pops up in the appropriately colored box |  |  |  |

## Field Name: Time to Live

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Time to Live information field pops up in the appropriately colored box |  |  |  |

Field Name: Protocol

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Protocol information field pops up in the appropriately colored box |  |  |  |

Screen: PING

## Field Name: Header Checksum

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Header Checksum information field pops up in the appropriately colored box |  |  |  |

Field Name: Source

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Source information field pops up in the appropriately colored box |  |  |  |

Field Name: Destination

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Destination information field pops up in the appropriately colored box |  |  |  |

## Field Name: Checksum

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Checksum information field pops up in the appropriately colored box |  |  |  |

Field Name: Identifier

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Identifier information field pops up in the appropriately colored box |  |  |  |

Screen: PING

Field Name: Sequence Number

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Sequence number information field pops up in the appropriately colored box |  |  |  |

### HTTP Testing Sheet

Screen: HTTP

Date:

Tester:

Screen: 	Pass 		Fail

Field Name: Fragment offset

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Fragment offset information field pops up in the appropriate colored box |  |  |  |

## Field Name: Time to Live

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Time to Live field pops up in the appropriate colored box |  |  |  |

## Field Name: Protocol

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Protocol information field pops up in the appropriate colored box |  |  |  |

## Field Name: Header Checksum

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Header Checksum information field pops up in the appropriate colored box |  |  |  |

Field Name: Source

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Source field pops up in the appropriate colored box |  |  |  |

Screen: HTTP

## Field Name: Destination

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Destination information field pops up in the appropriate colored box |  |  |  |

Field Name: Header Length

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Header Length field pops up in the appropriate colored box |  |  |  |

Field Name: Window Size

| Attempted | Expected Result | Comments | Pass | Fail |
| --- | --- | --- | --- | --- |
| 1. Right Click | Nothing pops up |  |  |  |
| 2. Left Click | Window Size information field pops up in the appropriate colored box |  |  |  |

### 4.0 Detailed Design Specification

# 4.1	Packaging and Deployment Specifications

Mirage Incorporated will install its Packet Descriptor application and all necessary files on the Siena Computer Science network, Oraserv, in a password protected area, enabling only Siena students to access the program.  An installation executable will be created and will be able to be run by the end user.  The user will then be able to load all the necessary files into a user-configurable directory on the local hard drive and create a shortcut on the start menu for the application.

A CD-ROM, which will include the application, all documents, and all presentations, will be given to our client, Mr. Swarner, for back-up.

- Appendix

  - Gantt Chart (Year)

5.2 	Glossary

ASCII:

American Standard Code for Information Interchange: a code for representing English characters as numbers, with each letter assigned a number from 0 to 127.

Attribute:

A named value or relationship that exists for some or all instances of some entity and is directly associated with that instance.

Binary:

Pertaining to a number system that has just two unique digits, 0 and 1.  Computers operate on a binary number system.

Code:

The symbolic arrangement of data or instructions in a computer program or the set of such instructions.

Data Flow Diagram:

A graphical notation used to describe how data flows between processes in a system.  They are a representation of the functional decomposition of a system.

Decimal:

Refers to numbers in base 10—the numbers we use in everyday life.

Dynamic Combo Menu:

Menu showing all actions possible at the current moment.

Frame:

A feature that divides a browser’s window into separate segments that can be scrolled independently of each other; a single step in a sequence of programmed instructions

GUI:

Graphical User Interface: A user interface based on graphics (icons, pictures, and menus) instead of text; uses a mouse as well as a keyboard as an input device.

Gantt Chart:

A chart that depicts progress in relation to time, often used in planning and tracking a project

Gray Box Testing: Testing procedure done with some knowledge of the internals.

HTML:

Hypertext Transfer Markup Language: A markup language used to structure text and multimedia documents and to set up hypertext links between documents, used extensively on the World Wide Web.

Hexadecimal:

Refers to the base-16 number system which consists of 16 unique symbols: the numbers 0 to 9 and the letters A to F.

Hypertext:

A computer-based text retrieval system that enables a user to access particular locations in web pages or other electronic documents by clicking on links within specific web pages or documents.

Internet:

An interconnected system of networks that connects computers around the world via the TCP/IP protocol.

Linear Sequential Model:

Sometimes called the classic life cycle or the waterfall model, this model suggests a systematic, sequential approach to software development that begins at the system level and progresses through analysis, design, coding, testing, and support.

Linux:

A trademark for an open-source version of the UNIX operating system.

Network:

A group of two or more computer systems linked together.

Open-Source:

A method and philosophy for software licensing and distribution designed to encourage use and improvement of software written by volunteers by ensuring that anyone can copy the source code.

PHP:

PHP Hypertext Preprocessor (server-side scripting language)

Packet:

A short block of data transmitted in a packet switching network.

PDU:

Protocol Data Unit: A packet of data passed across a network.

Protocol:

A set of formal rules describing how to transmit data, especially across a network.

Prototype:

An original type, form, or instance serving as a basis or standard for later stages.

RFC:

Request for Comments: One of a long-establish series of numbered Internet informational documents and standards widely followed by commercial software and freeware in the Internet and Unix communities.

Software:

The code executed by a computer, as opposed to the physical device which they run on.

TCP/IP:

Transmission Control Protocol/Internet Protocol: A suite of protocols for communication between computers, used as a standard for transmitting data over networks and as the basis for standard Internet protocols.

UNIX:

A powerful operating system developed at the ATT Bell Laboratories.

Use Case:

The specification of sequences of actions that a system, subsystem, or class can perform by interacting with outside actors.

Visible Analyst:

Project management software used in Computer-Aided Software Engineering (CASE) to create such illustrations as the data flow diagrams.

# Text boxes

7

6

5

4

3

0             1             2

0

0

R

T

D

Precedence

7

6

5

4

3

0             1             2

0

0

R

T

D

Precedence

0 1 2

Precedence

3

D

4

5

6

7

T

R

0

0

7

6

5

4

3

0             1             2

0

0

R

T

D

Precedence

Precedence

D

T

R

0

0

0             1             2

3

4

5

6

7

7

6

5

4

3

0             1             2

0

0

R

T

D

Precedence

7

6

5

4

3

0             1             2

0

0

R

T

D

Precedence

7

6

5

4

3

0             1             2

0

0

R

T

D

Precedence

7

6

5

4

3

0             1             2

0

0

R

T

D

Precedence