Preliminary Design

Requested by: 		Mr. Ken Swarner

Systems Administrator

Computer Science Department of Siena College

TCP/IP Packet Descriptor

Mirage Incorporated

“We are there…even if you cannot see us”

Mirageinc2003@yahoo.com

Prepared by:			Paul Aiuto

Richard Connell

Lauren Englisbe, Team Leader

Jayme Gresen

Jeffrey Habiniak

December 5, 2003

Preliminary Design

Table of Contents

| 1.0 External Design Specifications | 3 |
| --- | --- |
| 1.1 User Displays | 3-12 |
| 1.2 User Command Summary | 13 |
| 1.3 Detailed Data Flow Diagrams | 14-16 |
| 1.4 Hardware, Software, and Human Interfaces | 17 |
| 2.0 Architectural Design Specification | 18 |
| 2.1 User Commands (AKA “Clickable Buttons”) | 18 |
| 2.2 Functional Descriptions | 19 |
| 2.2.1 IP PDU for the selected FTP PDU | 19-32 |
| 2.2.2 TCP PDU for the selected FTP PDU | 33-43 |
| 2.2.3 FTP PDU for the selected FTP PDU | 44 |
| 2.2.4 IP PDU for the selected ICMP PDU | 45-57 |
| 2.2.5 ICMP PDU for the selected ICMP PDU | 58-64 |
| 3.0 Appendix | 65 |
| 3.1 Glossary | 65-67 |
| 3.2 Gantt Chart | 68-69 |

1.0 External Design Specifications

  - User displays

This will be the first screen the user sees.  It is the introduction screen to our software, and presents our mascot, “The Descript-roar”.

This is the first functional screen the user will see.  It allows the user to see what an Ethernet Packet looks like, and eventually each frame within that packet will be clickable and able to display information about that frame.

The “Choose a Protocol” menu gives the user a graphical representation of how protocols are interrelated, and allows the desired protocol to be selected.

Once a protocol has been selected by the user, this screen will display.  The basis for our protocol suite, the IP PDU is displayed on the left, filled in with the given data for the selected protocol.  The user is able to click on any field in the IP PDU, and an information box will display on the right, describing that field.  In the IP PDU Data field, “TCP PDU” is written – this indicates that the entire TCP PDU is contained within the IP Data field.  If the user clicks on this field, the TCP PDU will be displayed.

The PDUs are tabbed on their lower left corners: this allows the user to navigate between them.  Additionally, there is a key at the top right corner to display what PDUs make up the chosen protocol.  The user may also click on any PDU in this map to navigate.  If at any point, the user wants to choose a different protocol to view, he or she may click on the “Choose a Protocol” button in the top left corner.

The next screen shows the TCP PDU on top of the IP PDU.  This is meant to show that the TCP PDU is contained within the IP PDU.  Additionally, the FTP PDU is contained within the TCP PDU Data field, so clicking on that field will display the FTP PDU.  As with IP, if a TCP field is clicked, the information for that field will be displayed in the information box at the right.

This is the software with all the information displayed for the selected FTP PDU.  The IP PDU gives rise to the TCP PDU, and the TCP Data field has been clicked, which allows us to see the information field for the FTP PDU on the right.

Mirage has provided a number of prototype options, which will be chosen by the client at a later date.

Prototype Model Option 1 (IP PDU):

Prototype Model Option 2 (TCP PDU):

We also have two choices to allow for information display for a given field.

Information Field Option 1:

Information Field Option 2:

This is the user display using our second option for the Information Field:

1.2 User Command Summary

## Main Screen

This is the screen giving the user the option to choose many different packets.

## PDU Hierarchy Tree

Allows the user to see their progression through the many packets, and also able to choose their desired packet.

# IP Version

Allows the user two chooses of two different IP Versions.

# Radix (Base) Selection

Allows the user to select a radix to display.

# Information Box

Allows the user to see the given information for a selected field.

1.3 Detailed Data Flow Diagrams

Level 0 Diagram:

Context Diagram:

Detailed Diagram:

1.4 Hardware, Software and Human Interfaces

The prototype was developed and designed on Macromedia Fireworks, a graphic design program.

The program will be written in HTML using Macromedia MX and perhaps PHP (PHP Hypertext Processor) Version 4.1.2.

The TCP/IP Packet Descriptor program will be hosted as a web site on the Siena College Computer Science Department’s Oraserv Linux server (Red Hat version 7.1), running the Apache web server (version 1.3.19).

Any Netscape Navigator 7.x or greater and Internet Explorer 5.x or greater web browser may access the program.

2.0 Architectural Design Specification

2.1 User Commands (AKA “Clickable Buttons”)

# IP PDU

IP Version

Internet Header Length

Type of Service

Total Length of Ethernet Frame

Identification

Flags

Fragment Offset

Time to Live

Protocol

Header Checksum

Source IP Address

Destination IP Address

Options

Data

# TCP PDU

Source Port Number

Destination Port Number

Sequence Number

Acknowledgement Number

Header Lengths

Reserved

Window Size

TCP Checksum

Urgent Pointer

Options

Data

2.2 Functional Descriptions

2.2.1 IP PDU for the selected FTP PDU

IP PDU > IP Version for the selected FTP PDU

Field Name: IP Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be IP_IPVersion_FTP.

IP PDU > Internet Header Length for the selected FTP PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4-bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |
| Decimal | 5 |

Programming Hint: The name for this variable in code will be IP_IHL_FTP.

IP PDU > Type of Service for the selected FTP PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 10

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |
| Decimal | 16 |

Programming Hint: The name for this variable in code will be IP_TypeOfService_FTP.

IP PDU > Total Length of Ethernet Frame for the selected FTP PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key:  Not applicable

Data values (hexadecimal):  69

Data values in other bases:

| Hexadecimal | 0 | 0 | 6 | 9 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0110 | 1001 |
| Decimal | 0 | 105 |
| ASCII | © | i |

Programming Hint: The name for this variable in code will be IP_TotalLength_FTP.

IP PDU > Identification for the selected FTP PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet.

Field Key:  Not applicable

Data value (hexadecimal): AA 41

Data values in other bases:

| Hexadecimal | A | A | 4 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 1010 | 1010 | 0100 | 0001 |

Programming Hint: The name for this variable in code will be IP_Idenfification_FTP.

IP PDU > Flags for the selected FTP PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_Flags_FTP.

IP PDU > Fragment Offset for the selected FTP PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0 0000 0000 0000

Programming Hint: The name for this variable in code will be IP_FragmentOffset_FTP.

IP PDU > Time to Live for the selected FTP PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_FTP.

IP PDU > Protocol for the selected FTP PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	 10	Telnet						116		74	   WIDEBAND Monitoring

17	 11	XNET						117		75	   WIDEBAND EXPAK

20	 14	Chaos						120-376	78-0178  Unassigned

21	 15	User Datagram				377		0179	    Reserved

Data value (hexadecimal): 06

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |
| Decimal | 6 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming Hint: The name for this variable in code will be IP_Protocol_FTP.

IP PDU > Header Checksum for the selected FTP PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): 0E 85

Data values in other bases:

| Hexadecimal | 0 | E | 8 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 1110 | 1000 | 0101 |

Programming Hint: The name for this variable in code will be IP_HeaderChecksum_FTP.

IP PDU > Source Address for the selected FTP PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value (decimal):  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |
| Decimal | 192 | 168 | 0 | 39 |

Programming Hint: The name for this variable in code will be IP_SourceAddress_FTP.

IP PDU > Destination Address for the selected FTP PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key: Not applicable

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192 | 168 | 0 | 101 |

Programming Hint: The name for this variable in code will be IP_DestinationAddress_FTP.

IP PDU > Options and Padding for the selected FTP PDU

Field Name:  Options and Padding

Purpose and Definition:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Field Key:  Not applicable

Data values:  Not applicable

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_OptionsPadding_FTP.

IP PDU > Data for the selected FTP PDU

Field Name:  Data

Purpose and Definition:  The Data is a variable length field which contains the actual data that is being sent from one host to another.  The data field may start with a Layer 4 header, which will give additional instructions to the application that will be receiving the data; alternately, it may be an ICMP header and not contain any user data at all.

Field Key:  Not applicable

Data values (hexadecimal) :  (TCP) 80 30 00 15 81 A5 16 6C 87 A3 53 5D 80 18 16 D0 11 F4 00 00 01 01 08 0A 1B 25 F3 A1 0b DD 73 58

(FTP) 50 41 53 53 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

Data values in other bases:

Hexadecimal: (TCP) 0 x 80 30 00 15 81 A5 16 6C 87 A3 53 5D 80 18 16 D0 11 F4 00 00 01 01 08 0A 1B 25 F3 A1 0B DD 73 58

(FTP) 50 41 53 53 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

ASCII:  (TCP) ↑ 0 © © ↑ ↑ © ↑ ↑ S ] ↑ © © ↑ © ↑ © © © © © © © % ↑ ↑ © ↑ s X

(FTP) P A S S S © f 1 a 2 k 3 u s e r © ©

Programming Hint: The name for this variable in code will be IP_Data_FTP.

2.2.2 TCP PDU for the selected FTP PDU

IP > TCP PDU > Source Port for the selected FTP PDU

Field Name:  Source Port

Purpose and Definition:

This 16-bit number represents the name of the application that sent the data in the IP packet.

Field Key:  Not applicable

Data value (decimal): 32816

Data values in other bases:

| Hexadecimal | 8 | 0 | 3 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 0000 | 0011 | 0000 |
| Decimal | 128 | 48 |
| ASCII |  | 0 |

Programming Hint: The name for this variable in code will be IP_TCP_SourcePort_FTP.

IP > TCP PDU > Destination Port for the selected FTP PDU

Field Name: Destination Port

Purpose and Definition:
This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

Field Key:

This key indicates assigned port number values:

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (decimal): 21 (indicates FTP)

Data values in other bases:

| Hexadecimal | 0 | 0 | 1 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0101 |
| Decimal | 0 | 21 |
| ASCII | © | © |

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

Programming Hint: The name for this variable in code will be IP_TCP_DestinationPort_FTP.

IP > TCP PDU > Sequence Number for the selected FTP PDU

Field Name:  Sequence Number

Purpose and Definition:
TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Field Key:  Not applicable

Data value (decimal): 2175080044

Data values in other bases:

| Hexadecimal | 8 | 1 | A | 5 | 1 | 6 | 6 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0011 | 1100 | 1010 | 1010 | 0011 | 1100 |
| Decimal | 0 | 60 | 176 | 60 |
| ASCII | © | ‘ |  | ‘ |

Programming Hint: The name for this variable in code will be IP_TCP_SequenceNumber_FTP.

IP > TCP PDU > Acknowledgement Number for the selected FTP PDU

Field Name: Acknowledgement Number

Purpose and Definition:
This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Field Key:  Not applicable

Data value: 2275627869

Data values in other bases:

| Hexadecimal | 8 | 7 | A | 3 | 5 | 3 | 5 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 0111 | 1010 | 0011 | 0101 | 0011 | 0101 | 1101 |
| Decimal | 135 | 163 | 83 | 93 |
| ASCII |  |  | S | ] |

Programming Hint: The name for this variable in code will be IP_TCP_AcknowledgementNumber_FTP.

IP > TCP PDU > Header Length or Offset for the selected FTP PDU

Field Name:  Header Length or Offset

Purpose and Definition:
This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header.

Field Key:  Not applicable

Data value (bytes): 32

Data values in other bases:

| Hexadecimal | 8 | 0 |
| --- | --- | --- |
| Binary | 1000 | 0000 |
| Decimal | 128 |
| ASCII |  |

Programming Hint: The name for this variable in code will be IP_TCP_HeaderLength_FTP.

IP > TCP PDU > Reserved for the selected FTP PDU

Field Name:  Reserved

Purpose and Definition:
These 6 bits are unused and are always set to 0.

Field Key:  Not applicable

Data value (binary): 0000 00

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 |
| Decimal | 0 | 0 | 0 |
| ASCII | © | © | © |

Programming Hint: The name for this variable in code will be IP_TCP_Reserved_FTP.

IP > TCP PDU > Control Flags for the selected FTP PDU

Field Name:  Control Flags

Purpose and Definition:
Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:

- Urgent (URG)

- Acknowledgement (ACK)

- Push (PSH)

- Reset (RST)

- Synchronize (SYN)

- Finish (FIN)

Data value (binary): 01 1000

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_TCP_ControlFlags_FTP.

IP > TCP PDU > Window Size for the selected FTP PDU

Field Name:  Window Size

Purpose and Definition:
Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Field Key:  Not applicable

Data value (decimal): 5840

Data values in other bases:

| Hexadecimal | 1 | 6 | D | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0110 | 1110 | 0000 |
| Decimal | 22 | 224 |
| ASCII | © |  |

Programming Hint: The name for this variable in code will be IP_TCP_WindowSize_FTP.

IP > TCP PDU > Checksum for the selected FTP PDU

Field Name:  Checksum

Purpose and Definition:
Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Field Key:  Not applicable

Data value (hexadecimal): 11 F4

Data values in other bases:

| Hexadecimal | 1 | 1 | F | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0001 | 1111 | 0100 |
| Decimal | 17 | 244 |
| ASCII | © | © |

Programming Hint: The name for this variable in code will be IP_TCP_Checksum_FTP.

IP > TCP PDU > Urgent Pointer for the selected FTP PDU

Field Name: Urgent Pointer

Purpose and Definition:
If the Urgent flag is set to on, this value indicates where the urgent data is located.

Information Key:  Not applicable

Data value:  Not applicable

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_TCP_UrgentPointer_FTP.

IP > TCP PDU > Options and Padding for the selected FTP PDU

Field Name: Options and Padding

Purpose and Definition:
Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits.

Field Key:  Not applicable

Data value (hexadecimal): 01 01 08 0A 1B 25 F3 A1 0B DD 73 58

Data values in other bases:

| Hexadecimal | 0 | 1 | 0 | 1 | 0 | 8 | 0 | A | 1 | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0001 | 0000 | 0001 | 0000 | 1000 | 0000 | 1010 | 0001 | 1011 |
| Decimal | 1 | 1 | 8 | 10 | 27 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 2 | 5 | F | 3 | A | 1 | 0 | B | D | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0101 | 1111 | 0011 | 1010 | 0001 | 0000 | 1011 | 1101 | 1101 |
| Decimal | 37 | 243 | 161 | 11 | 221 |
| ASCII | % |  |  | © |  |

| Hexadecimal | 7 | 3 | 5 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0101 | 0011 | 0101 | 1000 |
| Decimal | 115 | 96 |
| ASCII |  |  |

Programming Hint: The name for this variable in code will be IP_TCP_OptionsPadding_FTP.

2.2.3 FTP PDU for the selected FTP PDU

IP >TCP > FTP PDU for the FTP Packet

RFC Link:  http://www.ietf.org/rfc/rfc0959.txt?number=959

PASS (Password)

The argument field is a Telnet string specifying the user’s password.  This command must be immediately preceded by the user name command, and, for some sites, completes the user’s identification for access control.

What is Contained in the Packet

Request:	PASS

Request Arg:	f1a2k3user

Data Values (hexadecimal): 50 41 53 53 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

Data Values in Other Bases

| ASCII | P | A | S | S | SPC | f | 1 | a | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hexadecimal | 5 0 | 4 1 | 5 3 | 5 3 | 2 0 | 6 6 | 3 1 | 6 1 | 3 2 |
| Binary | 0101 0000 | 0100 0001 | 0101 0011 | 0101 0011 | 0010 0000 | 0110 0110 | 0011 0001 | 0110 0001 | 0011 0010 |
| Decimal | 80 | 65 | 83 | 83 | 32 | 102 | 49 | 97 | 59 |

| ASCII | k | 3 | u | s | e | r | \r | \n |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hexadecimal | 6 B | 3 3 | 7 5 | 7 3 | 6 5 | 7 2 | 0 D | 0 A |
| Binary | 0110 1011 | 0011 0011 | 0111 0101 | 0111 0011 | 0110 0101 | 0111 0010 | 0000 1101 | 0000 1010 |
| Decimal | 107 | 51 | 117 | 115 | 101 | 114 | 13 | 10 |

Programming Hint: The name for this variable in code will be IP_TCP_FTP_PDU_FTP.

2.2.4 IP PDU for the selected ICMP PDU

IP PDU > Version for the selected ICMP PDU

Field Name: Version

Purpose and Definition:  Version is a 4-bit field that indicates the format of the internet header.

Field Key: 	4 = IPv4

6 = IPv6

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |
| Decimal | 4 |

Programming Hint: The name for this variable in code will be IP_Version_ICMP.

IP PDU > Internet Header Length for the selected ICMP PDU

Field Name:  Internet Header Length

Purpose and Definition:  The IHL field is a 4 bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Field Key:  Not applicable

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |
| Decimal | 5 |

Programming Hint: The name for this variable in code will be IP_Version_ICMP.

IP PDU > Type of Service for the selected ICMP PDU

Field Name:  Type of Service

Purpose and Definition:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Field Key:  The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (hexadecimal): 00

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |
| Decimal | 0 |

Programming Hint: The name for this variable in code will be IP_TypeOfService_ICMP.

IP PDU > Total Length of Ethernet Frame for the selected ICMP PDU

Field Name: Total Length of Ethernet Frame

Purpose and Definition: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Field Key: Not applicable

Data values (decimal):  84

Data values in other bases:

| Hexadecimal | 0 | 0 | 5 | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0101 | 0100 |
| Decimal | 0 | 84 |
| ASCII | © | T |

Programming Hint: The name for this variable in code will be IP_TotalLength_ICMP.

IP PDU > Identification for the selected ICMP PDU

Field Name:  Identification

Purpose and Definition:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a datagram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the datagram or any fragment could be alive in the internet

Field Key: Not applicable

Data value (hexadecimal): 00 00

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |

Programming Hint: The name for this variable in code will be IP_Identification_ICMP.

IP PDU > Flags for the selected ICMP PDU

Field Name:  Flags

Purpose and Definition:  Flags is a 3-bit field that indicates directions for fragmentation.

Field Key:

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_Flags_ICMP.

IP PDU > Fragment Offset for the selected ICMP PDU

Field Name:  Fragment Offset

Purpose and Definition:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Field Key:  Not applicable

Data value (decimal): 0

Data values in other bases:

# Binary: 0 0000 0000 0000

Programming Hint: The name for this variable in code will be IP_FragmentOffset_ICMP.

IP PDU > Time to Live for the selected ICMP PDU

Field Name: Time to Live

Purpose and Definition:  Time to Live is an 8-bit field that indicates the maximum time the datagram is allowed to remain in the internet.  If this field contains the value 0, then the datagram must be destroyed.  This field is modified in internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the datagram is allowed to be in the internet.  This field is decreased at each point that the internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum datagram lifetime.

Field Key:  Not applicable

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |
| Decimal | 64 |

Programming Hint: The name for this variable in code will be IP_TimeToLive_ICMP.

IP PDU > Protocol for the selected ICMP PDU

Field Name:  Protocol

Purpose and Definition:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the internet diagram.

Field Key:

# Dec Hex	Protocol					Dec		Hex	  Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	 10	Telnet						116		74	   WIDEBAND Monitoring

17	 11	XNET						117		75	   WIDEBAND EXPAK

20	 14	Chaos						120-376	78-0178  Unassigned

21	 15	User Datagram				377		0179	    Reserved

Data value (hexadecimal): 01

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0001 |
| Decimal | 1 |

RFC Link: http://www.faqs.org/rfcs/rfc790.html

Programming Hint: The name for this variable in code will be IP_Protocol_ICMP.

IP PDU > Header Checksum for the Selected ICMP PDU

Field Name:  Header Checksum

Purpose and Definition:  The Header Checksum is a 16-bit field.  This CRC algorithm is the 16-bit one’s complement sum of all the 16-bit words in the header.  For purposes of computing the checksum, the value of the checksum field is initially zero.  When both header checksums are the same, then the header bits are correct.  If either checksums vary, then a packet will need to be resent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Field Key:  Not applicable

Data value (hexadecimal): B8 CC

Data values in other bases:

| Hexadecimal | B | 8 | C | C |
| --- | --- | --- | --- | --- |
| Binary | 1011 | 1000 | 1100 | 1100 |

Programming Hint: The name for this variable in code will be IP_HeaderChecksum_ICMP.

IP PDU > Source Address for the Selected ICMP PDU

Field Name:  Source Address

Purpose and Definition:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Field Key:  Not applicable

Data value:  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |
| Decimal | 192 | 168 | 0 | 39 |

Programming Hint: The name for this variable in code will be IP_SourceAddress_ICMP.

IP PDU > Destination Address for the selected ICMP PDU

Field Name:  Destination Address

Purpose and Definition:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Field Key:  Not applicable

Data value:  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |
| Decimal | 192. | 168. | 0. | 101 |

Programming Hint: The name for this variable in code will be IP_DestinationAddress_ICMP.

IP PDU > Options and Padding for the selected ICMP PDU

Field Name:  Options and Padding

Purpose and Definition:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Field Key:  Not applicable

Data values:  Not applicable

Data values in other bases:  Not applicable

Programming Hint: The name for this variable in code will be IP_OptionsPadding_ICMP.

2.2.5 ICMP PDU for the selected ICMP PDU

IP > ICMP Header > Type for the selected ICMP PDU

Field Name:  Type

Purpose and Definition:  The type is an 8-bit field that identifies what sort of message the ICMP protocol is sending.

Field Key:

# Dec	 Hex	Message Type		Dec	  Hex	   Message Type

0	00	Echo Reply			16	  10	   Information Reply

1	01	Unassigned			17	  11	   Address Mask Request

2	02	Unassigned			18	  12	   Address Mask Reply

3	03	Destination Unreachable	19	  13	   Reserved (for Security)

4	04	Source Quench		20-29	  14-1D   Reserved (for Robustness Experiment)

5	05	Redirect			30	  1E	   Traceroute

6	06	Alternate Host Address	31	  1F	   Datagram Conversion Error

7	07	Unassigned			32	  20	   Mobile Host Redirect

8	08	Echo				33	  21	   IPv6 Where-Are-You

9	09	Router Advertisement		34	  22	   IPv6 I-Am-Here

10	0A	Router Solicitation		35	  23	   Mobile Registration Request

11	0B	Time Exceeded		36	  24	   Mobile Registration Reply

12	0C	Parameter Problem		37	  25	   Domain Name Request

13	0D	Timestamp			38	  26	   Domain Name Reply

14	0E	Timestamp Reply		39	  27	   SKIP

15	0F	Information Request		40	  28	   Photuris

41-255	  29-FF Reserved

Data value: 8 (Echo (ping) Request)

Data values in other bases:

| Hexadecimal | 0 | 8 |
| --- | --- | --- |
| Binary | 0000 | 1000 |
| Decimal | 8 |

RFC Link: http://www.iana.org/assignments/icmp-parameters

Programming Hint: The name for this variable in code will be IP_ICMP_Type_ICMP.

IP > ICMP Header > Code for the selected ICMP PDU

Field Name:  Code

Purpose and Definition: Code is an 8-bit field that provides further information about the associated type field.

Field Key:

Type     Name					Type     Name

0             Echo Reply (used by “PING”)			   7            Unassigned

0     No Code			    	   8            Echo (used by "PING")

1             Unassigned 					    0     No Code

2             Unassigned				   9            Router Advertisement

3             Destination Unreachable 			                       0    No Code

0     Net Unreachable			  10           Router Selection

1     Host Unreachable				     0    No Code

2     Protocol Unreachable			  11           Time Exceeded

3     Port Unreachable				     0    Time to Live exceeded in Transit

- Fragmentation needed and 			     1    Fragment Reassembly Time Exceeded

Don't Fragment was Set			  12            Parameter Problem

5     Source Route Failed				     0    Pointer indicates the error

6     Destination Network Unknown			     1    Missing a Required Option

7     Destination Host Unknown			     2    Bad Length

8     Source Host Isolated			  13           Timestamp

- Communication with Destination		  	     0    No Code

Network is Administratively Prohibited	  14           Timestamp Reply

- Communication with Destination		  	     0    No Code

Host is Administratively Prohibited		  15           Information Request

- Destination Network Unreachable		  	     0    No Code

for Type of Service                                               16           Information Reply

- Destination Host Unreachable for 		  	     0    No Code

Type of Service			  17           Address Mask Request

4            Source Quench                           			  	     0    No Code

0     No Code				  18           Address Mask Reply

5            Redirect                                 			  	    0     No Code

0    Redirect Datagram for the Network		  19           Reserved (for Security)

1    Redirect Datagram for the Host		  20-29   Reserved (for Robustness Experiment)

2    Redirect Datagram for the Type of 		  30        Traceroute

Service and Network			  31        Datagram Conversion Error

- Redirect Datagram for the Type of		  32        Mobile Host Redirect

Service and Host			  33        IPv6 Where-Are-You

6            Alternate Host Address 			  34        IPv6 I-Am-Here

0    Alternate Address for Host		  35        Mobile Registration Request

36        Mobile Registration Reply

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |
| Decimal | 0 |
| ASCII | © |

Programming Hint: The name for this variable in code will be IP_ICMP_Header_ICMP.

IP > ICMP Header > Checksum for the selected ICMP PDU

Field Name:  Checksum

Purpose and Definition:  The checksum is the 16-bit one’s complement of the one’s complement sum of the ICMP message, starting with the ICMP type.  For computing the checksum, the checksum field should initially be zero.

Field Key:  Not applicable

Data value (hexadecimal): C9 15

Data values in other bases:

| Hexadecimal | C | 9 | 1 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 1100 | 1001 | 0001 | 0101 |
| Decimal | 201 | 21 |
| ASCII |  | © |

Programming Hint: The name for this variable in code will be IP_ICMP_Checksum_ICMP.

IP > ICMP Header > Identifier for the selected ICMP PDU

Field Name:  Identifier

Purpose and Definition:  The identifier is a 16-bit field that is used in matching echoes and replies for when the code field is zero.

Field Key:  Not applicable

Data value (hexadecimal): 70 60

Data values in other bases:

| Hexadecimal | 7 | 0 | 6 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 0000 | 0110 | 0000 |
| Decimal | 112 | 96 |
| ASCII | P | ‘ |

Programming Hint: The name for this variable in code will be IP_ICMP_Identifier_ICMP.

IP > ICMP Header > Sequence for the selected ICMP PDU

Field Name:  Sequence

Purpose and Definition:  The sequence is a 16-bit field that is used in matching echoes and replies for when the code field is zero.

Field Key:  Not applicable

Data value (hexadecimal): 70 60

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |
| Decimal | 0 | 0 |
| ASCII | © | © |

Programming Hint: The name for this variable in code will be IP_ICMP_Sequence_ICMP.

IP > ICMP Header > Data for the selected ICMP PDU

Field Name:  Data

Purpose and Definition:  The data is a variable-length field that contains the actual information that is sent in the ping packet.

Field Key:  Not applicable

Data value (hexadecimal): 42 B1 89 3F 00 00 00 00 2C C6 07 00 00 00 00 00 10 11 12 13 14 15 16 17 18 19 1A 1B 1C 1D 1E 1F 20 21 22 23 24 25 26 27 28 29 2A 2B 2C 2D 2E 2F 30 31 32 33 34 35 36 37

Data values in other bases:

| Hexadecimal | 4 | 2 | B | 1 | 8 | 9 | 3 | F | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0010 | 1011 | 0001 | 1000 | 1001 | 0011 | 1111 | 0000 | 0000 |
| Decimal | 66 | 177 | 137 | 63 | 0 |
| ASCII | B |  |  | ? | © |

| Hexadecimal | 0 | 0 | 0 | 0 | 0 | 0 | 2 | C | C | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0010 | 1100 | 1100 | 0110 |
| Decimal | 0 | 0 | 0 | 44 | 198 |
| ASCII | © | © | © | , |  |

| Hexadecimal | 0 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0111 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 |
| Decimal | 7 | 0 | 0 | 0 | 0 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 2 | 1 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0000 | 0001 | 0001 | 0001 | 0010 | 0001 | 0011 |
| Decimal | 0 | 16 | 17 | 18 | 19 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 1 | 4 | 1 | 5 | 1 | 6 | 1 | 7 | 1 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0001 | 0100 | 0001 | 0101 | 0001 | 0110 | 0001 | 0111 | 0001 | 1000 |
| Decimal | 20 | 21 | 22 | 23 | 24 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 1 | 9 | 1 | A | 1 | B | 1 | C | 1 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0001 | 1001 | 0001 | 1010 | 0001 | 1011 | 0001 | 1100 | 0001 | 1101 |
| Decimal | 25 | 26 | 27 | 28 | 29 |
| ASCII | © | © | © | © | © |

| Hexadecimal | 1 | E | 1 | F | 2 | 0 | 2 | 1 | 2 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0001 | 1110 | 0001 | 1111 | 0010 | 0000 | 0010 | 0001 | 0010 | 0010 |
| Decimal | 30 | 31 | 32 | 33 | 34 |
| ASCII | © | © | SPACE | ! | “ |

| Hexadecimal | 2 | 3 | 2 | 4 | 2 | 5 | 2 | 6 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0011 | 0010 | 0100 | 0010 | 0101 | 0010 | 0110 | 0010 | 0111 |
| Decimal | 35 | 36 | 37 | 38 | 39 |
| ASCII | # | $ | % | & | ‘ |

| Hexadecimal | 2 | 8 | 2 | 9 | 2 | A | 2 | B | 2 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1000 | 0010 | 1001 | 0010 | 1010 | 0010 | 1011 | 0010 | 1100 |
| Decimal | 40 | 41 | 42 | 43 | 44 |
| ASCII | ( | ) | * | + | , |

| Hexadecimal | 2 | D | 2 | E | 2 | F | 3 | 0 | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1101 | 0010 | 1110 | 00010 | 1111 | 0011 | 0000 | 0011 | 0001 |
| Decimal | 45 | 46 | 47 | 48 | 49 |
| ASCII | - | . | / | 0 | 1 |

| Hexadecimal | 3 | 2 | 3 | 3 | 3 | 4 | 3 | 5 | 3 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0010 | 0011 | 0011 | 0011 | 0100 | 0011 | 0101 | 0011 | 0110 |
| Decimal | 50 | 51 | 52 | 53 | 54 |
| ASCII | 2 | 3 | 4 | 5 | 6 |

| Hexadecimal | 3 | 7 |
| --- | --- | --- |
| Binary | 0011 | 0111 |
| Decimal | 55 |
| ASCII | 7 |

Programming Hint: The name for this variable in code will be IP_ICMP_Data_ICMP.

3.0 Appendix

3.1 Glossary

ASCII:

American Standard Code for Information Interchange: a code for representing English characters as numbers, with each letter assigned a number from 0 to 127.

Attribute:

A named value or relationship that exists for some or all instances of some entity and is directly associated with that instance.

Binary:

Pertaining to a number system that has just two unique digits, 0 and 1.  Computers operate on a binary number system.

Code:

The symbolic arrangement of data or instructions in a computer program or the set of such instructions.

Data Flow Diagram:

A graphical notation used to describe how data flows between processes in a system.  They are a representation of the functional decomposition of a system.

Decimal:

Refers to numbers in base 10—the numbers we use in everyday life.

Dynamic Combo Menu:

Menu showing all actions possible at the current moment.

Frame:

A feature that divides a browser’s window into separate segments that can be scrolled independently of each other; a single step in a sequence of programmed instructions

GUI:

Graphical User Interface: A user interface based on graphics (icons, pictures, and menus) instead of text; uses a mouse as well as a keyboard as an input device.

Gantt Chart:

A chart that depicts progress in relation to time, often used in planning and tracking a project

HTML:

Hypertext Transfer Markup Language: A markup language used to structure text and multimedia documents and to set up hypertext links between documents, used extensively on the World Wide Web.

Hexadecimal:

Refers to the base-16 number system which consists of 16 unique symbols: the numbers 0 to 9 and the letters A to F.

Hypertext:

A computer-based text retrieval system that enables a user to access particular locations in web pages or other electronic documents by clicking on links within specific web pages or documents.

Internet:

An interconnected system of networks that connects computers around the world via the TCP/IP protocol.

Linear Sequential Model:

Sometimes called the classic life cycle or the waterfall model, this model suggests a systematic, sequential approach to software development that begins at the system level and progresses through analysis, design, coding, testing, and support.

Linux:

A trademark for an open-source version of the UNIX operating system.

Network:

A group of two or more computer systems linked together.

Open-Source:

A method and philosophy for software licensing and distribution designed to encourage use and improvement of software written by volunteers by ensuring that anyone can copy the source code.

PHP:

PHP Hypertext Preprocessor (server-side scripting language)

Packet:

A short block of data transmitted in a packet switching network.

PDU:

Protocol Data Unit: A packet of data passed across a network.

Protocol:

A set of formal rules describing how to transmit data, especially across a network.

Prototype:

An original type, form, or instance serving as a basis or standard for later stages.

RFC:

Request for Comments: One of a long-establish series of numbered Internet informational documents and standards widely followed by commercial software and freeware in the Internet and Unix communities.

Software:

The code executed by a computer, as opposed to the physical device which they run on.

TCP/IP:

Transmission Control Protocol/Internet Protocol: A suite of protocols for communication between computers, used as a standard for transmitting data over networks and as the basis for standard Internet protocols.

UNIX:

A powerful operating system developed at the ATT Bell Laboratories.

Use Case:

The specification of sequences of actions that a system, subsystem, or class can perform by interacting with outside actors.

Visible Analyst:

Project management software used in Computer-Aided Software Engineering (CASE) to create such illustrations as the data flow diagrams.

3.2 Gantt Charts

Fall Gantt Chart:

Yearlong Gantt Chart:

# Text boxes

7

6

5

4

3

0             1             2

0

0

R

T

D

Precedence

7

6

5

4

3

0             1             2

0

0

R

T

D

Precedence