##### Detailed Design

Requested by:	Ken Swarner

System Administrator

Siena College

Computer Science Department

##### TCP/IP Packet Descriptor

##### Paradigm Solutions

Prepared by:  	Jonathan Baker, Team Leader

Ryan Fischer

Mike Sebast

Justin Waterman

Jim DeSario

Mark Mossman

#### February 28, 2005

Detailed Design

Table of Contents

Section 1: 	External Design Specifications	4

Section 1.1: 	User Displays	4

Section 1.2: 	Detailed Data Flow Diagrams	18

Section 1.3: 	Hardware, Software, and Human Interfaces	23

Section 2: 	Architectural Design Specification	24

Section 2.1: 	User Commands	24

Section 2.2: 	Functional Descriptions	26

Section 2.2.0: 	Ethernet PDU for the selected FTP PDU	26

Section 2.2.1: 	 IP PDU for the selected FTP PDU	32

Section 2.2.2: 	 TCP PDU for the selected FTP PDU	45

Section 2.2.3: 	 FTP PDU for the selected FTP PDU	56

Section 2.2.4: 	 IP PDU for the selected ICMP PDU	58

Section 2.2.5: 	 ICMP PDU for the selected ICMP PDU	71

Section 2.2.6: 	 IP PDU for the selected SMTP PDU	79

Section 2.2.7: 	 TCP PDU for the selected SMTP PDU	92

Section 2.2.8: 	 SMTP PDU for the selected SMTP PDU	103

Section 2.2.9: 	 IP PDU for the selected HTTP PDU	106

Section 2.2.10: 	 TCP PDU for the selected HTTP PDU	120

Section 2.2.11: 	 HTTP PDU for the selected HTTP PDU	131

Section 2.2.12: 	 IP PDU for the selected SSH PDU	147

Section 2.2.13: 	 TCP PDU for the selected SSH PDU	159

Section 2.2.14: 	 IP PDU for the selected TELNET PDU	168

Section 2.2.15: 	 TCP PDU for the selected TELNET PDU	181

Section 2.2.16:         	TELNET PDU for the selected TELNET PDU 	192

Section 2.2.17: 	 ARP PDU for the selected ARP PDU	193

Section 2.2.18: 	 IP PDU for the selected UPD PDU	206

Section 3:	Data Storage		 225

Section 3.1:	Naming Convention	225

Section 3.2:	Physical Location of Data	225

Section 4:	Testing Requirements		226

Section 4.1:	Testing Specifications	227

Section 4.2:	Testing Forms	230

Section 5: 	Appendix	238

Section 5.1: 	Glossary	238

Section 5.2: 	Gantt Chart	240

1.0 External Design Specifications

  - User displays

In order to effectively portray the user displays, the following pages contain a pictorial representation of a user navigating through the HTTP protocol selection.  After each picture there is a brief summary of what the user would have selected in order to make each screen appear.

This is the first screen that the user will see when he logs onto the program.  This screen consists of a protocol tree in the middle, with an accompanying Ethernet stack to the right of it, measuring where each protocol lies in the tree.  Additionally, we have an Ethernet frame at the top of the screen that displays information about the destination, source, and other information about it.  Any button when selected will cause the box at the bottom to display topic information about what was selected.  Also there is a history page link in the bottom right corner, which upon clicking will bring the user to a history page with previous teams web pages.  The history page link is a uniform feature throughout the screens.

This is the history page that the user will be sent to if the icon is selected.  The user can click on any previous teams link to view their homepages, to return to the previous screen the user clicks on the back button.

In the middle of the screen is a protocol tree, which the user may select any of the non-shaded out protocols to display a list of data sessions.  In this example, the HTTP protocol was selected, and a drop-down menu of data sessions has appeared.  The user then scrolls to the particular data field that he is interested in, and then clicks on it to take him or her to the Packet Selection screen.

The user can scroll down the list using the scroll bar.  This screen shows the user had scrolled down to view other data sessions.

When the user moves the mouse over a data session, the session becomes highlighted.  The data session then becomes un-highlighted when the mouse moves off of the data session.  This screen shows the mouse highlighting a particular data session.  The user would click the highlighted data session to advance to the Packet Selection screen.

This is a Packet Selection Screen as the user first sees it.  Its title at the top reflects the protocol that was selected.  From before, the HTTP protocol was selected.  The box in the middle of the screen displays the different packets of the selected protocol as well as other relevant information about the packet.  The screen is initialized to highlight the topmost packet, which is the default packet.  Above this, we have repeated the data session name for the data session that was selected from the Protocol Selector screen.  There are two buttons below this packet box:  a View Packet Button, which takes you to the Information Display Screen and display the highlighted packet; and a Choose Protocol Button, which when clicked returns you to the Protocol Selection Screen.  Additionally the user can display the contents of a packet by double clicking the packet on this screen.

If there are more packets in the data session than the box is capable of displaying, the scroll bar on the right allows the user to scroll through the different packets available in the data session.  This is an example of the user scrolling to see more packets.  The user can highlight a particular packet by clicking on its row.  This action will un-highlight the previously highlighted packet.  Clicking on a currently highlighted packet does nothing.  This screen demonstrates the highlighting of a packet other than the default packet.

This is the Information Display Screen.  This screen displays the contents of the packet that was selected in the Packet Selector Screen.  The two buttons on the upper left, the Choose Packet Button and the Choose Protocol Button, bring the user to the Packet Selector Screen and the Protocol Selection Screen, respectively.  There are tabs that would allow the user to traverse the protocol tree, less the Ethernet root.  Since, in this example the user had selected an HTTP packet; the tabs at the bottom of the screen are IP, TCP, and HTTP.  Everything on this screen except for the packet fields is geographically static, that is they will not change in size or location on this screen.  The user first sees the highest level of protocol, in this case HTTP.  This is the screen as the user first sees it.  The protocol stack in the upper right corner allows the user to navigate through the different protocols within the protocol hierarchy.  At the top of the screen there is an Ethernet Frame that is now filled with data.

Clicking on any of the fields’ causes the program to display both information about the field and the data contained in that field in the Information Box, located on the left of the screen.  This is an example of the user clicking on the Type of Service field.

This is an example of the user selecting the TCP protocol, as the user first sees it.  The information box displays the selected packet’s TCP protocol information.

Clicking on a different field clears out the information box and displays the information of the newly selected field.  This is an example of the user selecting Source Port Number field.

The user went to the HTTP protocol, the information box displays information about the HTTP protocol.

The user selected the HTTP PDU field.  The information box displays the information within that field.

1.2 Detailed Data Flow Diagrams

Key:

□   — Source/Sink

○  — Process

═  — Data Stores

→ — Data Flow

1.3 Hardware, Software and Human Interfaces

The prototype was developed and designed using Macromedia Fireworks and Adobe Photoshop graphic design programs.

The program will be written in HTML and PHP using the Macromedia Studio MX Suite of web design tools. Other Linux based code editing tools may be used.

The TCP/IP Packet Descriptor program will be hosted as a web site on the Siena College Computer Science Department’s Oraserv Linux server (Red Hat version 7.1), running the Apache web server (version 1.3.19) and PHP (version 4.1.2).

The program will be compatible with any Netscape Navigator 7.x or greater, Internet Explorer 5.x or greater, Firefox 1.x or greater, and Mozilla 1.7.x or greater web browsers.

2.0 Architectural Design Specification

2.1 User Commands

Active Protocols (those that the user can select) –

File Transfer Protocol (FTP)

Simple Mail Transfer Protocol (SMTP)

Hyper Text Transfer Protocol (HTTP)

Terminal Emulation Protocol (TELNET)

Address Resolution Protocol (ARP)

Secure Shell (SSH)

Internet Control Message Protocol (ICMP)

User Datagram Protocol (UDP)

Inactive Protocols (those that show up in the protocol hierarchy, but cannot be chosen for viewing) –

Simple Network Management Protocol (SNMP)

Secure Control Protocol (SCP)

Dynamic Host Configuration Protocol (DHCP)

Domain Name Service (DNS)

Resource Reservation Protocol (RSVP)

Lightweight Directory Access Protocol (LDAP)

Network Time Protocol (NTP)

Choose Protocol- The “Choose Protocol” function will display a hierarchical tree of available protocols.  Each node of the tree will be a link to display that particular protocol.

Protocol Fields- Each field will be a link.  When selected it will be highlighted and the Information of that field will be shown in an information box to the left of the PDU.

Team Logos – Each logo will be a link that, when selected, will take the user to that team’s website.

View Packet – This command is given from the Packet Selector screen by pressing the View Packet button. Here, it will bring up the Information Display screen, displaying the highlighted packet.

Choose Protocol – This button in on both the Packet Selector Screen and the Information Display screen.  This command will take the user back to the Protocol Selection screen.

Choose Packet – This command is executed when the user presses the Choose Packet button on the Information Display screen.  This allows the user to select a different packet from within the current data session.

Packet Select – On the Packet Selector screen, there will be a display of all the packets within the current data session.  The user can select the row that they wish to view by clicking on the row that contains that packet.  Note that this does not bring up the Information Display screen, but rather indicates which packet will be displayed when the user selects the View Packet button.

Data Session Select – After the user clicks on their desired protocol, a drop down menu will appear displaying all the data sessions that have been stored in a folder to be specified later by our client, Mr. Swarner.  The user then clicks on the data session that they would like to view.  The act of selecting takes them to the Packet Selector screen.

Request for Comments Link – Each PDU will have a link to a web site with extensive information about the selected protocol.

2.2 Functional Descriptions

2.2.0 Ethernet PDU for the selected FTP PDU

Hex Dump:

00    01    03    1e    e2    24    00    00

f8     1f     00    85   08    00    45    10

00    45    AA   41   40    00    40    06

0e     85    c0     a8   00    27    c0    a8

00     65    80    30   00    15    81    a5

16     6c    87    a3    53    5d    80   18

16     d0    11    f4    00    00    01   01

08     0a    1b    25    f3     a1    0b   dd

73     58    50    41   53     53    20   66

31     61    32    6b   33     75    73   65

72     0d    0a

Ethernet PDU > Preamble for the selected FTP PDU

Field Name: Preamble

Description:  Repeating bit sequence (10101010…) used to determine clock synchronization between transmitting and receiving stations

Data value (hexadecimal):  AAAAAAAAAAAAAA

Data values in other bases: Not applicable

Start Bit: Pre-Packet

Length: 56

Ethernet PDU > Start of Frame (Sof) for the selected FTP PDU

Field Name: Start of Frame (Sof)

Description:  Marks the beginning of the Ethernet Frame

Data value (decimal):  171

Data values in other bases:

| Hexadecimal | A | B |
| --- | --- | --- |
| Binary | 1010 | 1011 |

Start Bit: Pre-Packet

Length: 8

Ethernet PDU > Destination MAC Address for the selected FTP PDU

Field Name: Destination MAC Address

Description:  48 bit destination node address, specifying the station(s) for which the frame is intended.  It may be an individual or multicast (including broadcast) address.

The LSB of 48-bit Ethernet addresses will be 0 if the frame is single cast (meant for a specific node) or 1 if it is multicast (broadcast to multiple nodes). Individual nodes on a network determine whether they need to participate in a multicast, and either receive or ignore the frame

Data value (hexadecimal):  00 : 01 : 03 : 1E : E2 : 24

Data values in other bases: Not applicable

Start Bit: 0

Length: 48

Ethernet PDU > Source MAC Address for the selected FTP PDU

Field Name: Source MAC Address

Description:  48 bit source node address, specifying the station sending the frame.  The Source Address field is not interpreted by the CSMA/CD MAC sublayer

Data value (hexadecimal):  00 : 00 : F8 : 1F : 00 : 85

Data values in other bases: Not applicable

Start Bit: 48

Length: 48

Ethernet PDU > Length for the selected FTP PDU

Field Name: Length

Description:  The Length field is a 2-octet field whose value indicates the number of LLC data octets in the data field.  If the value is less than the minimum required for proper operation of the protocol, a PAD field (a sequence of octets) will be added at the end of the data field but prior to the FCS field.  The length field is transmitted and received with the high order octet first.

Data value (decimal):  2048

Data values in other bases:

| Hexadecimal | 0 | 8 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 1000 | 0000 | 0000 |

Start Bit: 96

Length: 16

Ethernet PDU > Cyclic Redundancy Check (CRC) for the selected FTP PDU

Field Name: Cyclic Redundancy Check (CRC)

Description:  Calculation to determine if any bit errors occurred to the packet during transmission

Data value (hexadecimal):  FFFF

Data values in other bases: Not applicable

Start Bit: Post-packet

Length: 32

2.2.1 IP PDU for the selected FTP PDU

IP PDU > IP Version for the selected FTP PDU

Field Name: IP Version

Description:  IP Version is a 4-bit field that indicates the format of the Internet header

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |

Start Bit: 0

Length: 4

IP PDU > Header Length for the selected FTP PDU

Field Name:  Header Length

Description:  The Header Length field is a 4-bit field indicating the length of the Internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5 (20 bytes) and the maximum value is 15 (60 bytes).

Data value (decimal):  5

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |

Start Bit: 4

Length: 4

IP PDU > Type of Service for the selected FTP PDU

Field Name:  Type of Service

Description:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a data gram through a particular network.

The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D) 0 = Normal Delay		1 = Low Delay

Bit 4: (T) 0 = Normal Throughput	1 = High Throughput

Bit 5: (R) 0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Inter-network Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overridden		000 = Routine

Data value (decimal): 16

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |

Start Bit: 8

Length: 8

IP PDU > Total Length for the selected FTP PDU

Field Name: Total Length

Description: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including Internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Data values (decimal):  69

Data values in other bases:

| Hexadecimal | 0 | 0 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0100 | 0101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 69 in hexadecimal

Start Bit: 16

Length: 16

IP PDU > Identification for the selected FTP PDU

Field Name:  Identification

Description:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a data gram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the data gram or any fragment could be alive in the Internet.

Data value (decimal): 43585

Data values in other bases:

| Hexadecimal | A | A | 4 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 1010 | 1010 | 0100 | 0001 |

Start Bit: 32

Length: 16

IP PDU > Flags for the selected FTP PDU

Field Name:  Flags

Description:  Flags is a 3-bit field that indicates directions for fragmentation.

Bit 0: reserved, must be 0

Bit 1: (DF) 0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Start Bit: 48

Length: 3

IP PDU > Fragment Offset for the selected FTP PDU

Field Name:  Fragment Offset

Description:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |

Start Bit: 51

Length: 13

IP PDU > Time to Live for the selected FTP PDU

Field Name: Time to Live

Description:  Time to Live is an 8-bit field that indicates the maximum time the data ram is allowed to remain in the Internet.  If this field contains the value 0, then the data gram must be destroyed.  This field is modified in Internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the data gram is allowed to be in the Internet.  This field is decreased at each point that the Internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum data gram lifetime.

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |

Start Bit: 64

Length: 8

IP PDU > Protocol for the selected FTP PDU

Field Name:  Protocol

Description:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the Internet diagram.

# Dec 	Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	05	ST						100		64	   SATNET and                  
 										   Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet 
 										   Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET 
 										   Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core 
                      									   Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET 
 											   Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	  10	Telnet						116		74	   WIDEBAND 
 										   Monitoring

17	  11	XNET						117		75	   WIDEBAND      
  										    EXPAK

20	  14	Chaos						120-376	78-0178  Unassigned

21	  15	User Data gram				377		0179	    Reserved

Data value (decimal): 6

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |

Start Bit: 72

Length: 8

RFC Link: http://www.faqs.org/rfcs/rfc790.html

.

IP PDU > Header Checksum for the selected FTP PDU

Field Name:  Header Checksum

Description:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Data value (decimal): 3717

Data values in other bases:

| Hexadecimal | 0 | E | 8 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 1110 | 1000 | 0101 |

Start Bit: 80

Length: 16

IP PDU > Source IP Address for the selected FTP PDU

Field Name:  Source IP Address

Description:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Data value (decimal):  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |

Start Bit: 96

Length: 32

IP PDU > Destination IP Address for the selected FTP PDU

Field Name:  Destination IP Address

Description:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |

Start Bit: 128

Length: 32

IP PDU > Options for the selected FTP PDU

Field Name:  Options

Description:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Some example options are:

0 End of Options list 		68 Timestamp

1 No operation (pad) 		131 Loose source route

7 Record route 		137 Strict source route

Data values:  Not applicable

Data values in other bases:  Not applicable

Start Bit: 160

Length: Variable (0-40 bytes)

2.2.2 TCP PDU for the selected FTP PDU

IP > TCP PDU > Source Port Number for the selected FTP PDU

Field Name:  Source Port Number

Description: A 16-bit address assigned by the sending computer that represents the name of the application that sent the data in the IP packet.

Common TCP Well-Known Server Ports (Decimal):

7 echo 		 	 110	pop3

19 chargen 			 111	sunrpc

20 ftp-data 		 	119	nntp

21 ftp-control 	 		139	netbios-ssn

22 ssh 			 	143	imap

23 telnet 		 	179	bgp

25 smtp 		 	 389	ldap

53 domain 		 	443	https (ssl)

79 finger 			 445	microsoft-ds

80 http 			1080	socks

Data value (decimal): 32816

Data values in other bases:

| Hexadecimal | 8 | 0 | 3 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 0000 | 0011 | 0000 |

Start Bit: 0

Length: 16

IP > TCP PDU > Destination Port Number for the selected FTP PDU

Field Name: Destination Port Number

Description: This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

Common TCP Well-Known Server Ports (Decimal):

7 echo 		 	 110	pop3

19 chargen 			 111	sunrpc

20 ftp-data 			 119	nntp

21 ftp-control 	 		139	netbios-ssn

22 ssh 				 143	imap

23 telnet 			 179	bgp

25 smtp 		 	 389	ldap

53 domain 			 443	https (ssl)

79 finger 			 445	microsoft-ds

80 http 			1080	socks

This key indicates assigned port number values:

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (decimal): 21 (indicates FTP)

Data values in other bases:

| Hexadecimal | 0 | 0 | 1 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0101 |

Start Bit: 16

Length: 16

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

IP > TCP PDU > Sequence Number for the selected FTP PDU

Field Name:  Sequence Number

Description: TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Data value (decimal): 2175080044

Data values in other bases:

| Hexadecimal | 8 | 1 | A | 5 | 1 | 6 | 6 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 0001 | 1010 | 0101 | 0001 | 0110 | 0110 | 1100 |

Start Bit: 32

Length: 32

IP > TCP PDU > Acknowledgement Number for the selected FTP PDU

Field Name: Acknowledgement Number

Description: This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Data value (decimal): 2275627869

Data values in other bases:

| Hexadecimal | 8 | 7 | A | 3 | 5 | 3 | 5 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 0111 | 1010 | 0011 | 0101 | 0011 | 0101 | 1101 |

Start Bit: 64

Length: 32

IP > TCP PDU > Length for the selected FTP PDU

Field Name: Length

Description: This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header. The minimum value of a correct header is 5 (20 bytes) and the maximum value is 15 (60 bytes).

Data value (decimal): 8

Data values in other bases:

| Hexadecimal | 0 | 8 |
| --- | --- | --- |
| Binary | 0000 | 1000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 128 in decimal

Start Bit: 96

Length: 4

IP > TCP PDU > Reserved for the selected FTP PDU

Field Name:  Reserved

Description: 
These 6 bits are unused and are always set to 0.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 |

Start Bit: 100

Length: 6

IP > TCP PDU > Flags for the selected FTP PDU

Field Name:  Flags

Description: Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Flags: U A P R S F

U (1 = Urgent pointer valid)

A (1 = Acknowledgement field value valid)

P (1 = Push data)

R (1 = Reset connection)

S (1 = Synchronize sequence numbers)

F (1 = no more data; Finish connection)}

Data value (binary): 01 1000

Data values in other bases:  Not applicable

Start Bit: 106

Length: 6

IP > TCP PDU > Window Size for the selected FTP PDU

Field Name:  Window Size

Description: Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Data value (decimal): 5840

Data values in other bases:

| Hexadecimal | 1 | 6 | D | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0110 | 1101 | 000 |

Start Bit: 112

Length: 16

IP > TCP PDU > TCP Checksum for the selected FTP PDU

Field Name: TCP Checksum

Description: Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Data value (decimal): 4596

Data values in other bases:

| Hexadecimal | 1 | 1 | F | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0001 | 1111 | 0100 |

Start Bit: 128

Length: 16

IP > TCP PDU > Urgent Pointer for the selected FTP PDU

Field Name: Urgent Pointer

Description:  If the Urgent flag is set to on, this value indicates where the urgent data is located.

Data value (decimal):  0

Data values in other bases:  Not applicable

Start Bit: 144

Length: 16

IP > TCP PDU > Options for the selected FTP PDU

Field Name: Options

Description:  Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits. If present, may be used in negotiating a connection.

The Options field must fit the 32-bit boundary and is padded with 0s if it does not

Some example options (Decimal):

0 End of Options list 		3 Window scale

1 No operation (pad) 		4 Selective ACK ok

2 Maximum segment size 	8 Timestamp

Data value (hexadecimal): 01 01 08 0A 1B 25 F3 A1 0B DD 73 58

Data values in other bases: Not applicable

Start Bit: 160

Length: Variable

2.2.3 FTP PDU for the selected FTP PDU

IP >FTP > Request/Response for the selected FTP PDU

Description: Request: PASS (Password)

The argument field is a Telnet string specifying the user’s password.  This command must be immediately preceded by the user name command, and, for some sites, completes the user’s identification for access control,

Data Values (hexadecimal): 50 41 53 53

Data Values in Other Bases:

| ASCII | P | A | S | S |
| --- | --- | --- | --- | --- |
| Binary | 0101 0000 | 0100 0001 | 0101 0011 | 0101 0011 |

Start Bit: 144

Length: 16

RFC Link: http://www.ietf.org/rfc/rfc0959.txt?number=959

IP >FTP > Data for the selected FTP PDU

Description: Payload for the FTP data gram

Request Arg:	        f1a2k3user

Data Value (hexadecimal): 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

Data Values in Other Bases:

| ASCII | SPC | f | 1 | a | 2 | k | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 0000 | 0110 0110 | 0011 0001 | 0110 0001 | 0011 0010 | 0110 1011 | 0011 0011 |

| ASCII | u | s | e | r | \r | \n |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 0101 | 0111 0011 | 0110 0101 | 0111 0010 | 0000 1101 | 0000 1010 |

Start Bit: 144

Length: 16

2.2.4 IP PDU for the selected ICMP PDU

IP PDU > IP Version for the selected ICMP PDU

Field Name: IP Version

Description:  Version is a 4-bit field that indicates the format of the Internet header.

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |

Start Bit: 0

Length: 5

IP PDU > Header Length for the selected ICMP PDU

Field Name: Header Length

Description:  The IHL field is a 4 bit field indicating the length of the Internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5 (20 bytes) and the maximum value is 15 (60 bytes).

Data value (decimal):  5

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |

Start Bit: 4

Length: 4

IP PDU > Type of Service for the selected ICMP PDU

Field Name:  Type of Service

Description:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a data gram through a particular network.

The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D) 0 = Normal Delay		1 = Low Delay

Bit 4: (T) 0 = Normal Throughput		1 = High Throughput

Bit 5: (R) 0 = Normal Reliability		1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP		001 = Priority

100 = Flash Overridden		000 = Routine

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |

Start Bit: 8

Length: 8

IP PDU > Total Length for the selected ICMP PDU

Field Name: Total Length

Description: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including Internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Data values (decimal):  84

Data values in other bases:

| Hexadecimal | 0 | 0 | 5 | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0101 | 0100 |

Start Bit: 16

Length: 16

IP PDU > Identification for the selected ICMP PDU

Field Name:  Identification

Description:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a data gram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the data gram or any fragment could be alive in the Internet

Data value (decimal): 21929

Data values in other bases:

| Hexadecimal | 5 | 5 | A | 9 |
| --- | --- | --- | --- | --- |
| Binary | 0101 | 0101 | 1010 | 1001 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary data value was 0000 0000 0000 0000

Start Bit: 32

Length: 16

IP PDU > Flags for the selected ICMP PDU

Field Name:  Flags

Description:  Flags is a 3-bit field that indicates directions for fragmentation.

Bit 0: reserved, must be 0

Bit 1: (DF) 0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 000

Data values in other bases:  Not applicable

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary data value was 010

Start Bit: 48

Length: 3

IP PDU > Fragment Offset for the selected ICMP PDU

Field Name:  Fragment Offset

Description:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |

Start Bit: 51

Length: 13

IP PDU > Time to Live for the selected ICMP PDU

Field Name: Time to Live

Description:  Time to Live is an 8-bit field that indicates the maximum time the data gram is allowed to remain in the Internet.  If this field contains the value 0, then the data gram must be destroyed.  This field is modified in Internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the data gram is allowed to be in the Internet.  This field is decreased at each point that the Internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum data gram lifetime.

Data value (decimal): 255

Data values in other bases:

| Hexadecimal | F | F |
| --- | --- | --- |
| Binary | 1111 | 1111 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 64 in decimal

Start Bit: 64

Length: 8

IP PDU > Protocol for the selected ICMP PDU

Field Name:  Protocol

Description:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the Internet diagram.

# Dec Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	05	ST						100		64	   SATNET and                  
 										   Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet 
 										   Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET 
 										   Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core 
                      									   Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET 
 											   Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	  10	Telnet						116		74	   WIDEBAND 
 										   Monitoring

17	  11	XNET						117		75	   WIDEBAND      
  										    EXPAK

20	  14	Chaos						120-376	78-0178  Unassigned

21	  15	User Data gram				377		0179	    Reserved

Data value (decimal): 1

Data values in other bases:

| Hexadecimal | 0 | 1 |
| --- | --- | --- |
| Binary | 0000 | 0001 |

Start Bit: 72

Length: 8

RFC Link: http://www.faqs.org/rfcs/rfc790.html

IP PDU > Header Checksum for the Selected ICMP PDU

Field Name:  Header Checksum

Description:  The Header Checksum is a 16-bit field.  This CRC algorithm is the 16-bit one’s complement sum of all the 16-bit words in the header.  For purposes of computing the checksum, the value of the checksum field is initially zero.  When both header checksums are the same, then the header bits are correct.  If either checksums vary, then a packet will need to be resent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Data value (decimal): 58402

Data values in other bases:

| Hexadecimal | E | 4 | 2 | 2 |
| --- | --- | --- | --- | --- |
| Binary | 1110 | 0100 | 0010 | 0010 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was B8 CC in hexadecimal

Start Bit: 80

Length: 16

IP PDU > Source IP Address for the Selected ICMP PDU

Field Name:  Source IP Address

Description:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Data value:  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 192.168.0.39

Start Bit: 96

Length: 32

IP PDU > Destination IP Address for the selected ICMP PDU

Field Name:  Destination IP Address

Description:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Data value:  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 192.168.0.101

Start Bit: 128

Length: 32

IP PDU > Options for the selected ICMP PDU

Field Name:  Options

Description:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data

octets.

Some example options are:

0 End of Options list 		68 Timestamp

1 No operation (pad) 		131 Loose source route

7 Record route 		137 Strict source route

Data values:  Not applicable

Data values in other bases:  Not applicable

Start Bit: 160

Length: Variable (0-40 bytes)

2.2.5 ICMP PDU for the selected ICMP PDU

IP > ICMP Header > Type for the selected ICMP PDU

Field Name:  Type

Description:  The type is an 8-bit field that identifies what sort of message the ICMP protocol is sending.

ICMP message types are:

0 Echo Reply
3 Destination Unreachable
4 Source Quench
5 Redirect
8 Echo
11 Time Exceeded
12 Parameter Problem
13 Timestamp
14 Timestamp Reply
15 Information Request
16 Information Reply

# Dec	Hex	Message Type		Dec	  Hex	   Message Type

0	00	Echo Reply		16	  10	  Information Reply

1	01	Unassigned		17	  11	  Address Mask Request

2	02	Unassigned		18	  12	  Address Mask Reply

3	03	Destination Unreachable	19	  13	  Reserved (for Security)

4          04	Source Quench		20-29	  14-1D     Reserved (for Robustness 
                                                				  Experiment)

5	05	Redirect			30	  1E	   Traceroute

6	06	Alternate Host Address	31	  1F	   Data gram Conversion Error

7	07	Unassigned		32	  20	   Mobile Host Redirect

8	08	Echo			33	  21	   IPv6 Where-Are-You

9	09	Router Advertisement	34	  22	   IPv6 I-Am-Here

10	0A	Router Solicitation		35	  23	   Mobile Registration Request

11	0B	Time Exceeded		36	  24	   Mobile Registration Reply

12	0C	Parameter Problem	37	  25	   Domain Name Request

13	0D	Timestamp		38	  26	   Domain Name Reply

14	0E	Timestamp Reply		39	  27	   SKIP

15	0F	Information Request	40	  28	   Photuris

41-255	  29-FF      Reserved

Data value: 0

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 8 in decimal

Start Bit: 0

Length: 8

RFC Link: http://www.iana.org/assignments/icmp-parameters

IP > ICMP Header > Code for the selected ICMP PDU

Field Name:  Code

Description: Code is an 8-bit field that provides further information about the associated type field. Based on what type the ICMP PDU is, the code can have a number of meanings.

For example, with ICMP type 3 (Destination Unreachable) is as follows:
0 = net unreachable;
1 = host unreachable;
2 = protocol unreachable;
3 = port unreachable;
4 = fragmentation needed and DF set;
5 = source route failed.

Type     Name					Type     Name

0             Echo Reply (used by “PING”)			  7            Unassigned

0     No Code			    	 	  8            Echo (used by "PING")

1             Unassigned 					    0     No Code

2             Unassigned				 	  9            Router Advertisement

3             Destination Unreachable 			                       0    No Code

0     Net Unreachable				 10           Router Selection

1     Host Unreachable				     0    No Code

2     Protocol Unreachable				 11           Time Exceeded

3     Port Unreachable				     0    Time to Live exceeded in Transit

- Fragmentation needed and 			     1    Fragment Reassembly Time Exceeded

Don't Fragment was Set				 12            Parameter Problem

5     Source Route Failed				     0    Pointer indicates the error

6     Destination Network Unknown			     1    Missing a Required Option

7     Destination Host Unknown			     2    Bad Length

8     Source Host Isolated				 13           Timestamp

- Communication with Destination		  	     0    No Code

Network is Administratively Prohibited		 14           Timestamp Reply

- Communication with Destination		  	     0    No Code

Host is Administratively Prohibited		 	 15           Information Request

- Destination Network Unreachable		  	     0    No Code

for Type of Service                                             	 16           Information Reply

- Destination Host Unreachable for 		  	     0    No Code

Type of Service			 	 17           Address Mask Request

4            Source Quench                           			  	     0    No Code

0     No Code				  	 18           Address Mask Reply

5            Redirect                                 			  	    0     No Code

0    Redirect Data gram for the Network			 19           Reserved (for Security)

1    Redirect Data gram for the Host			 20-29   Reserved (for Robustness 
           							               Experiment)

2    Redirect Data gram for the Type of 			 30        Trace route

Service and Network				 31        Data gram Conversion Error

- Redirect Data gram for the Type of		  	 32        Mobile Host Redirect

Service and Host			 	 33        IPv6 Where-Are-You

6            Alternate Host Address 			  	 34        IPv6 I-Am-Here

0    Alternate Address for Host		  	 35        Mobile Registration Request

36        Mobile Registration Reply

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |

Start Bit: 8

Length: 8

IP > ICMP Header > ICMP Checksum for the selected ICMP PDU

Field Name:  ICMP Checksum

Description:  The checksum is the 16-bit one’s complement of the one’s complement sum of the ICMP message, starting with the ICMP type.  For computing the checksum, the checksum field should initially be zero.

Data value (decimal): 17173

Data values in other bases:

| Hexadecimal | 4 | 3 | 1 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0100 | 0011 | 0001 | 0101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was C9 15 in hexadecimal

Start Bit: 16

Length: 16

IP > ICMP Header > Identifier for the selected ICMP PDU

Field Name:  Identifier

Description:  The identifier is a 16-bit field that is used in matching echoes and replies for when the code field is zero.

Data value (decimal): 28768

Data values in other bases:

| Hexadecimal | 7 | 0 | 6 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 0000 | 0110 | 0000 |

Start Bit: 32

Length: 16

IP > ICMP Header > Sequence Number for the selected ICMP PDU

Field Name:  Sequence Number

Description:  The sequence is a 16-bit field that is used in matching echoes and replies for when the code field is zero.

Data value (decimal): 256

Data values in other bases:

| Hexadecimal | 0 | 1 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 000 | 0001 | 0000 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 70 60 in hexadecimal

Start Bit: 48

Length: 16

IP > ICMP Header > Data for the selected ICMP PDU

Field Name:  Data

Description:  The data is a variable-length field that contains the actual information that is sent in the ping packet.

Data value (hexadecimal): 43 B1 89 3F 00 00 00 00 B8 C6 07 00 00 00 00 00 10 11 12 13 14 15 16 17 18 19 1A 1B 1C 1D 1E 1F 20 21 22 23 24 25 26 27 28 29 2A 2B 2C 2D 2E 2F 30 31 32 33 34 35 36 37

Data values in other bases: Not applicable

Start Bit: 64

Length: Variable

2.2.6 IP PDU for the selected SMTP PDU

IP PDU > IP Version for the selected SMTP PDU

Field Name: IP Version

Description:  Version is a 4-bit field that indicates the format of the Internet header

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |

Start Bit: 0

Length: 4

IP PDU > Header Length for the selected SMTP PDU

Field Name: Header Length

Description:  The IHL field is a 4-bit field indicating the length of the Internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5 (20 bytes) and the maximum value is 15 (60 bytes).

Data value:  5

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |

Start Bit: 4

Length: 4

IP PDU > Type of Service for the selected SMTP PDU

Field Name:  Type of Service

Description:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a data gram through a particular network.

The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D) 0 = Normal Delay			1 = Low Delay

Bit 4: (T) 0 = Normal Throughput		1 = High Throughput

Bit 5: (R) 0 = Normal Reliability		1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP		001 = Priority

100 = Flash Overridden		000 = Routine

Data value (decimal): 16

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 0 in decimal

Start Bit: 8

Length: 8

IP PDU > Total Length for the selected SMTP PDU

Field Name: Total Length

Description: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including Internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets

Data values (decimal):  70

Data values in other bases:

| Hexadecimal | 0 | 0 | 4 | 6 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0010 | 0100 | 0110 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 02 12 in hexadecimal

Start Bit: 16

Length: 16

IP PDU > Identification for the selected SMTP PDU

Field Name:  Identification

Description:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a data gram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the data gram or any fragment could be alive in the Internet.

Data value (decimal): 46047

Data values in other bases:

| Hexadecimal | B | 3 | D | F |
| --- | --- | --- | --- | --- |
| Binary | 1011 | 0011 | 1101 | 1111 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 61 28 in hexadecimal

Start Bit: 32

Length: 16

IP PDU > Flags for the selected SMTP PDU

Field Name:  Flags

Description:  Flags is a 3-bit field that indicates directions for fragmentation.

Bit 0: reserved, must be 0

Bit 1: (DF) 0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Start Bit: 48

Length: 3

IP PDU > Fragment Offset for the selected SMTP PDU

Field Name:  Fragment Offset

Description:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |

Start Bit: 51

Length: 13

IP PDU > Time to Live for the selected SMTP PDU

Field Name: Time to Live

Description:  Time to Live is an 8-bit field that indicates the maximum time the data gram is allowed to remain in the Internet.  If this field contains the value 0, then the data gram must be destroyed.  This field is modified in Internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the data gram is allowed to be in the Internet.  This field is decreased at each point that the Internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum data gram lifetime.

Data value (decimal): 128

Data values in other bases:

| Hexadecimal | 8 | 0 |
| --- | --- | --- |
| Binary | 1000 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 64 in decimal

Start Bit: 64

Length: 8

IP PDU > Protocol for the selected SMTP PDU

Field Name:  Protocol

Description:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the Internet diagram.

# Dec 	Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5            05	ST						100		64	   SATNET and                  
 										   Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet 
 										   Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET 
 										   Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core 
                      									   Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET 
 											   Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	  10	Telnet						116		74	   WIDEBAND 
 										   Monitoring

17	  11	XNET						117		75	   WIDEBAND      
  										    EXPAK

20	  14	Chaos						120-376	78-0178  Unassigned

21	  15	User Data gram				377		0179	    Reserved

Data value (decimal): 6

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |

Start Bit: 72

Length: 8

RFC Link: http://www.faqs.org/rfcs/rfc790.html

IP PDU > Header Checksum for the selected SMTP PDU

Field Name:  Header Checksum

Description:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Data value (decimal): 24840

Data values in other bases:

| Hexadecimal | 6 | 1 | 0 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0110 | 0001 | 0000 | 1000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was F1 F3 in hexadecimal

Start Bit: 80

Length: 16

IP PDU > Source IP Address for the selected SMTP PDU

Field Name:  Source IP Address

Description:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Data value (decimal):  192.168.100.20

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 6 | 4 | 1 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0110 | 0100 | 0001 | 0100 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 192.168.0.101 in decimal

Start Bit: 96

Length: 32

IP PDU > Destination IP Address for the selected SMTP PDU

Field Name:  Destination IP Address

Description:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 192.168.100.20 in decimal

Start Bit: 128

Length: 32

IP PDU > Options for the selected SMTP PDU

Field Name:  Options

Description:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Some example options are:

0 End of Options list 		68 Timestamp

1 No operation (pad) 		131 Loose source route

7 Record route 		137 Strict source route

Data values:  Not applicable

Data values in other bases:  Not applicable

Start Bit: 160

Length: Variable (0-40 bytes)

2.2.7 TCP PDU for the selected SMTP PDU

IP > TCP PDU > Source Port Number for the selected SMTP PDU

Field Name:  Source Port Number

Description: A 16-bit address assigned by the sending computer, to the application program sending data as TCP data grams.

Common TCP Well-Known Server Ports (Decimal):
07 echo		 110 pop3
19 chargen 	 111 sunrpc
20 ftp-data 	 119 nntp
21 ftp-control 	 139 netbios-ssn
22 ssh 	 	 143 imap
23 telnet 		 179 bgp
25 smtp 		 389 idap
53 domain 	 443 https(ssl)
79 finger 	 445 microsoft-ds
80 http 		 1080 socks

Data value (decimal): 32816

Data values in other bases:

| Hexadecimal | 8 | 0 | 3 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 0000 | 0011 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 3651 in decimal

Start Bit: 0

Length: 16

IP > TCP PDU > Destination Port Number for the selected SMTP PDU

Field Name: Destination Port Number

Description: A 16-bit address assigned by the receiving computer, to the destination application program for this message.

Common TCP Well-Known Server Ports (Decimal):
07 echo		 110 pop3
19 chargen 	 111 sunrpc
20 ftp-data 	 119 nntp
21 ftp-control 	 139 netbios-ssn
22 ssh 	 	 143 imap
23 telnet 		 179 bgp
25 smtp 		 389 idap
53 domain 	 443 https (ssl)
79 finger 	 445 microsoft-ds
80 http 		 1080 socks

Data value (decimal): 21 (indicates SMTP)

Data values in other bases:

| Hexadecimal | 0 | 0 | 1 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 25 in decimal

Start Bit: 16

Length: 16

IP > TCP PDU > Sequence Number for the selected SMTP PDU

Field Name:  Sequence Number

Description: TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Data value (decimal): 2175080044

Data values in other bases:

| Hexadecimal | 8 | 1 | A | 5 | 1 | 6 | 6 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 0001 | 1010 | 0101 | 0001 | 0110 | 0110 | 1100 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 2069207327 in decimal

Start Bit: 32

Length: 32

IP > TCP PDU > Acknowledgement Number for the selected SMTP PDU

Field Name: Acknowledgement Number

Description: This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Data value (decimal): 2275627869

Data values in other bases:

| Hexadecimal | 8 | 7 | A | 3 | 5 | 3 | 5 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 0111 | 1010 | 0011 | 0101 | 0011 | 0101 | 1101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 3827794966 in decimal

Start Bit: 64

Length: 32

IP > TCP PDU > Length for the selected SMTP PDU

Field Name: Length

Description: The Header Length field is a 4-bit field indicating the length of the TCP header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5 (20 bytes) and the maximum value is 15 (60 bytes).

Data value (decimal): 8

Data values in other bases:

| Hexadecimal | 0 | 8 |
| --- | --- | --- |
| Binary | 0000 | 1000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 128 in decimal

Start Bit: 96

Length: 4

IP > TCP PDU > Reserved for the selected SMTP PDU

Field Name:  Reserved

Description: These 6 bits are unused and are always set to 0.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 | 0000 | 0000 |

Start Bit: 100

Length: 6

IP > TCP PDU > Control Flags for the selected SMTP PDU

Field Name:  Control Flags

Description: Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Flags: U A P R S F

U (1 = Urgent pointer valid)

A (1 = Acknowledgement field value valid)

P (1 = Push data)

R (1 = Reset connection)

S (1 = Synchronize sequence numbers)

F (1 = no more data; Finish connection)

Data value (binary): 01 1000

Data values in other bases:  Not applicable

Start Bit: 106

Length: 6

IP > TCP PDU > Window Size for the selected SMTP PDU

Field Name:  Window Size

Description: Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Data value (decimal): 5840

Data values in other bases:

| Hexadecimal | 1 | 6 | D | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0110 | 1101 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 32120 in decimal

Start Bit: 112

Length: 16

IP > TCP PDU > TCP Checksum for the selected SMTP PDU

Field Name: TCP Checksum

Description: Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Data value (decimal): 4596

Data values in other bases:

| Hexadecimal | 1 | 1 | F | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0001 | 1111 | 0100 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 72 B5 in hexadecimal

Start Bit: 128

Length: 16

IP > TCP PDU > Urgent Pointer for the selected SMTP PDU

Field Name: Urgent Pointer

Description: If the Urgent flag is set to on, this value indicates where the urgent data is located.

Data value:  Not applicable

Data values in other bases:  Not applicable

Start Bit: 144

Length: 16

IP > TCP PDU > Options for the selected SMTP PDU

Field Name: Options

Description: Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. If present may be used in negotiating a connection. The options field must fit the 32 bit boundary and is padded with 0's if it does not. 

Some example options (In decimal):
0 - End of options list
1 - No operation (pad)
2 - Maximum segment size
3 - Window scale
4 - Selective Acknowledgement OK
8 - Timestamp

Data value (hexadecimal): 01 01 08 0A 1B 25 F3 A1 0B DD 73 58

Data values in other bases: Not applicable

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 01 01 08 0A 07 AE F6 75 00 21 66 A4 in hexadecimal

Start Bit: 160

Length: Variable

2.2.8 SMTP PDU for the selected SMTP PDU

IP > SMTP Header > Data for the selected SMTP PDU

Field Name:  Data

Description:  ASCII messages sent between SMTP hosts.

| Command | Description |
| --- | --- |
| DATA | Begins message composition. |
| EXPN <string> | Returns names on the specified mail list. |
| HELO <domain> | Returns identity of mail server. |
| HELP <command> | Returns information on the specified command. |
| MAIL FROM <host> | Initiates a mail session from host. |
| NOOP | Causes no action, except acknowledgement from server. |
| QUIT | Terminates the mail session. |
| RCPT TO <user> | Designates who receives mail. |
| RSET | Resets mail connection. |
| SAML FROM <host> | Sends mail to user terminal and mailbox. |
| SEND FROM <host> | Sends mail to user terminal. |
| SOML FROM <host> | Sends mail to user terminal or mailbox. |
| TURN | Switches role of receiver and sender. |
| VRFY <user> | Verifies the identity of a user. |

Data value: Content_TEXT\Plain;name=”mimetest.txt”

Data values in other bases:

| Hexadecimal | 4 | 3 | 6 | F | 6 | E | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0011 | 0110 | 1111 | 0110 | 1110 | 0111 | 0100 |

| Hexadecimal | 6 | 5 | 6 | E | 7 | 4 | 2 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 1110 | 0111 | 0100 | 0010 | 1101 |

| Hexadecimal | 5 | 4 | 4 | 5 | 5 | 8 | 5 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0100 | 0100 | 0101 | 0101 | 1000 | 0101 | 0100 |

| Hexadecimal | 2 | F | 5 | 0 | 6 | C | 6 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0101 | 0000 | 0110 | 1100 | 0110 | 0001 |

| Hexadecimal | 6 | 9 | 6 | E | 3 | B | 6 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0110 | 1110 | 0011 | 1011 | 0110 | 1001 |

| Hexadecimal | 6 | 1 | 6 | D | 6 | 5 | 3 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0001 | 0110 | 1101 | 0110 | 0101 | 0011 | 1101 |

| Hexadecimal | 2 | 0 | 6 | 3 | 6 | 8 | 6 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 0011 | 0110 | 1000 | 0110 | 0001 |

| Hexadecimal | 2 | 2 | 7 | 4 | 6 | 5 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0010 | 0111 | 0100 | 0110 | 0101 | 0111 | 0011 |

| Hexadecimal | 7 | 4 | 2 | E | 7 | 4 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0100 | 0010 | 1110 | 0111 | 0100 | 0111 | 1000 |

| Hexadecimal | 7 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 0100 | 0010 | 0000 |

Start Bit: 0

Length: 152

RFC Link: http://www.ietf.org/rfc/rfc0821.txt?number=821

IP > SMTP Header > Message for the selected SMTP PDU

Field Name:  Message

Description:  Response messages consist of a response code followed by explanatory text

| Response Code | Explanatory Text |
| --- | --- |
| 211 | (Response to system status or help request). |
| 214 | (Response to help request). |
| 220 | Mail service ready. |
| 221 | Mail service closing connection. |
| 250 | Mail transfer completed. |
| 251 | User not local, forward to <path>. |
| 354 | Start mail message, end with <CRLF><CRLF>. |
| 421 | Mail service unavailable. |
| 450 | Mailbox unavailable. |
| 451 | Local error in processing command. |
| 452 | Insufficient system storage. |
| 500 | Unknown command. |
| 501 | Bad parameter. |
| 502 | Command not implemented. |
| 503 | Bad command sequence. |
| 504 | Parameter not implemented. |
| 550 | Mailbox not found. |
| 551 | User not local, try <path>. |
| 552 | Storage allocation exceeded. |
| 553 | Mailbox name not allowed. |
| 554 | Mail transaction failed. |

Data value: Not applicable.

Start Bit: 152

Length: Variable

2.2.9 IP PDU for the selected HTTP PDU

IP PDU > IP Version for the selected HTTP PDU

Field Name: IP Version

Description:  Version is a 4-bit field that indicates the format of the Internet header.

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |

Start Bit: 0

Length: 4

IP PDU> Header Length for the selected HTTP PDU

Field Name:  Header Length

Description:  The IHL field is a 4-bit field indicating the length of the Internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |

Start Bit: 4

Length: 4

IP PDU > Type of Service for the selected HTTP PDU

Field Name:  Type of Service

Description:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a data gram through a particular network.

The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D) 0 = Normal Delay		1 = Low Delay

Bit 4: (T) 0 = Normal Throughput	1 = High Throughput

Bit 5: (R) 0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (decimal): 16

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 0 in decimal.

Start Bit: 8

Length: 8

IP PDU > Total Length for the selected HTTP PDU

Field Name: Total Length

Description: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including Internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Data values (decimal):  69

Data values in other bases:

| Hexadecimal | 0 | 0 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0100 | 0101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 570 in decimal.

Start Bit: 16

Length: 16

IP PDU > Identification for the selected HTTP PDU

Field Name:  Identification

Description:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a data gram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the data gram or any fragment could be alive in the Internet.

Data value (decimal): 43585

Data values in other bases:

| Hexadecimal | A | A | 4 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 1010 | 1010 | 0100 | 0001 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 15365 in decimal.

Start Bit: 32

Length: 16

IP PDU > Flags for the selected HTTP PDU

Field Name:  Flags

Description:  Flags is a 3-bit field that indicates directions for fragmentation.

Bit 0: reserved, must be 0

Bit 1: (DF) 0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Start Bit: 48

Length: 3

IP PDU > Fragment Offset for the selected HTTP PDU

Field Name:  Fragment Offset

Description:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |

Start Bit: 51

Length: 13

IP PDU > Time to Live for the selected HTTP PDU

Field Name: Time to Live

Description:  Time to Live is an 8-bit field that indicates the maximum time the data gram is allowed to remain in the Internet.  If this field contains the value 0, then the data gram must be destroyed.  This field is modified in Internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the data gram is allowed to be in the Internet.  This field is decreased at each point that the Internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum data gram lifetime.

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |

Start Bit: 64

Length: 8

IP PDU > Protocol for the selected HTTP PDU

Field Name:  Protocol

Description:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the Internet diagram.

# Dec 	Hex	Protocol					Dec		Hex	Protocol

0 	  0	Reserved					22		16	Multiplexing

1 	  1	ICMP						23		17	DCN

2	  2	Unassigned					24		18	TAC Monitoring

3 	  3	Gateway-to-Gateway				25-76		19-4C	Unassigned

4 	  4	CMCC Gateway Monitoring Message	77		4D	Any local network

5	  5	ST						100		64	SATNET and             
                                         							Backroom EXPAK

6	  6	TCP						101		65	MIT Subnet Support

7	  7	UCL						102-104	66-68	Unassigned

10	  A	Unassigned					105		69	SATNET Monitoring

11	  B	Secure						106		6A	Unassigned

12	  C	BBN RCC Monitoring			107		6B	Internet Packet Core  
          											Utility

13	  D	NVP						110-113	6E-71	Unassigned

14	  E	PUP						114		72	Backroom SATNET 
             										Monitoring

15	  F	Pluribus					115		73	Unassigned

16	10	Telnet						116		74	WIDEBAND 
                                                                                                                        Monitoring

17	11	XNET						117		75	WIDEBAND 
  												EXPAK

20	14	Chaos						120-376	78-178  Unassigned

21	15	User Datagram				377		179	  Reserved

Data value (decimal): 6

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |

Start Bit: 72

Length: 8

RFC Link: http://www.faqs.org/rfcs/rfc790.html

IP PDU > Header Checksum for the selected HTTP PDU

Field Name:  Header Checksum

Description:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Data value (decimal): 3717

Data values in other bases:

| Hexadecimal | 0 | E | 8 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 1110 | 1000 | 0101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 31319 in decimal.

Start Bit: 80

Length: 16

IP PDU > Source IP Address for the selected HTTP PDU

Field Name:  Source IP Address

Description:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Data value (decimal):  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 192.168.0.012 in decimal.

Start Bit: 96

Length: 32

IP PDU > Destination IP Address for the selected HTTP PDU

Field Name:  Destination IP Address

Description:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |

Start Bit: 128

Length: 32

IP PDU > Options for the selected HTTP PDU

Field Name:  Options

Description:  The options may or may not appear in Ethernet packets.  They must be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Data values:  Not applicable

Data values in other bases:  Not applicable

Start Bit: 160

Length: 0-40

IP PDU > Data for the selected HTTP PDU

Field Name:  Data

Description:  The Data is a variable length field, which contains the actual data that is being sent from one host to another.  The data field may start with a Layer 4 header, which will give additional instructions to the application that will be receiving the data; alternately, it may be an ICMP header and not contain any user data at all.

Data values (hexadecimal):  (TCP) 80 30 00 15 81 A5 16 6C 87 A3 53 5D 80 18 16 D0 11 F4 00 00 01 01 08 0A 1B 25 F3 A1 0b DD 73 58

(FTP) 50 41 53 53 20 66 31 61 32 6B 33 75 73 65 72 0D 0A

Data values in other bases:  Not applicable

2.2.10 TCP PDU for the selected HTTP PDU

IP > TCP PDU > Source Port Number for the selected HTTP PDU

Field Name:  Source Port Number

Description: This 16-bit number represents the name of the application that sent the data in the IP packet.

Data value (decimal): 32816

Data values in other bases:

| Hexadecimal | 8 | 0 | 3 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 0000 | 0011 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 50 in decimal.

Start Bit: 0

Length: 16

IP > TCP PDU > Destination Port Number for the selected HTTP PDU

Field Name: Destination Port Number

Description: This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

This key indicates assigned port number values:

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (decimal): 21

Data values in other bases:

| Hexadecimal | 0 | 0 | 1 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 4255 in decimal.

Start Bit: 16

Length: 16

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

IP > TCP PDU > Sequence Number for the selected HTTP PDU

Field Name:  Sequence Number

Description: TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Data value (decimal): 2175080044

Data values in other bases:

| Hexadecimal | 8 | 1 | A | 5 | 1 | 6 | 6 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 0001 | 1010 | 0101 | 0001 | 0110 | 0110 | 1100 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 988014608 in decimal.

Start Bit: 32

Length: 32

IP > TCP PDU > Acknowledgement Number for the selected HTTP PDU

Field Name: Acknowledgement Number

Description: This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Data value (decimal): 2275627869

Data values in other bases:

| Hexadecimal | 8 | 7 | A | 3 | 5 | 3 | 5 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1000 | 0111 | 1010 | 0011 | 0101 | 0011 | 0101 | 1101 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 1398299764 in decimal.

Start Bit: 64

Length: 32

IP > TCP PDU > Length for the selected HTTP PDU

Field Name: Length

Description: This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header.

Data value (decimal): 8

Data values in other bases:

| Hexadecimal | 0 | 8 |
| --- | --- | --- |
| Binary | 0000 | 1000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 128 in decimal.

Start Bit: 96

Length: 4

IP > TCP PDU > Reserved for the selected HTTP PDU

Field Name:  Reserved

Description: 4 bits; set to 0
ECN bits (used when ECN employed; else 00)
CWR (1=sender has cut congestion window in half
ECN-Echo (1=receiver has cut congestion window in half

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |

Start Bit: 100

Length: 6 Bits

IP > TCP PDU > Control Flags for the selected HTTP PDU

Field Name:  Control Flags

Description: Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

- Urgent (URG)

- Acknowledgement (ACK)

- Push (PSH)

- Reset (RST)

- Synchronize (SYN)

- Finish (FIN)

Data value (binary): 01 1000

Data values in other bases:  Not applicable

Start Bit: 106

Length: 6

IP > TCP PDU > Window Size for the selected HTTP PDU

Field Name:  Window Size

Description: Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Data value (decimal): 5840

Data values in other bases:

| Hexadecimal | 1 | 6 | D | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0110 | 1101 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 7504 in decimal.

Start Bit: 112

Length: 16

IP > TCP PDU > Urgent Pointer for the selected HTTP PDU

Field Name: Urgent Pointer

Description: If the Urgent flag is set to on, this value indicates where the urgent data is located.

Information Key:  Not applicable

Data value:  Not applicable

Data values in other bases:  Not applicable

IP > TCP PDU > TCP Checksum for the selected HTTP PDU

Field Name:  TCP Checksum

Description: Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Data value (decimal): 4596

Data values in other bases:

| Hexadecimal | 1 | 1 | F | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0001 | 0001 | 1111 | 0100 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 61686 in decimal.

Start Bit: 128

Length: 16

IP > TCP PDU > Options for the selected HTTP PDU

Field Name: Options

Description: Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits.

Data value (hexadecimal): 01 01 0A 1B 25 F3 A1 0B DD 73 58

Data values in other bases: Not applicable

Start Bit: 160

Length: Variable

2.2.11 HTTP PDU for the selected HTTP PDU

IP > TCP > HTTP PDU > Content Type for the selected HTTP PDU

Field Name: Content Type

Description: The Content-Type entity-header field indicates the media type of the Entity-Body sent to the recipient.

Data value (ASCII): text/html; charset=iso – 8859-1\r\n

Data values in other bases:

| Hexadecimal | 4 | 3 | 6 | F | 6 | E | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0011 | 0110 | 1111 | 0110 | 1110 | 0111 | 0100 |
| ASCII | C | o | n | t |

| Hexadecimal | 6 | 5 | 6 | E | 7 | 4 | 2 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 1110 | 0111 | 0100 | 0010 | 1101 |
| ASCII | e | n | t | - |

| Hexadecimal | 5 | 4 | 7 | 9 | 7 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0100 | 0111 | 1001 | 0111 | 0000 | 0110 | 0101 |
| ASCII | T | y | p | e |

| Hexadecimal | 3 | A | 2 | 0 | 7 | 4 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1010 | 0010 | 0000 | 0111 | 0100 | 0110 | 0101 |
| ASCII | : |  | t | e |

| Hexadecimal | 7 | 8 | 7 | 4 | 2 | F | 6 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 1000 | 0111 | 0100 | 0010 | 1111 | 0110 | 1000 |
| ASCII | x | t | / | h |

| Hexadecimal | 7 | 4 | 6 | D | 6 | C | 3 | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0100 | 0110 | 1101 | 0110 | 1100 | 0011 | 1011 |
| ASCII | t | m | l | ; |

| Hexadecimal | 2 | 0 | 6 | 3 | 6 | 8 | 6 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 0011 | 0110 | 1000 | 0110 | 0001 |
| ASCII |  | c | h | a |

| Hexadecimal | 7 | 2 | 7 | 3 | 6 | 5 | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0111 | 0011 | 0110 | 0101 | 0111 | 0100 |
| ASCII | r | s | e | t |

| Hexadecimal | 3 | D | 6 | 9 | 7 | 3 | 6 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1101 | 0110 | 1001 | 0111 | 0011 | 0110 | 1111 |
| ASCII | = | i | s | o |

| Hexadecimal | 2 | D | 3 | 8 | 3 | 8 | 3 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1101 | 0011 | 1000 | 0011 | 1000 | 0011 | 0101 |
| ASCII | - | 8 | 8 | 5 |

| Hexadecimal | 3 | 9 | 2 | D | 3 | 1 | 0 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1001 | 0010 | 1101 | 0011 | 0001 | 0000 | 1101 |
| ASCII | 9 | - | 1 | \r |

| Hexadecimal | 0 | A |
| --- | --- | --- |
| Binary | 0000 | 1010 |
| ASCII | \n |

Start Bit: 0

Length: 460

IP > TCP > HTTP PDU > Date for the selected HTTP PDU

Field Name: Date

Description: This field contains the date and time on which the web page was accessed.

Data value (ASCII): Date: Tue, 03 Feb 2004 23:08:10 GMT\r\n

Data values in other bases:

| Hexadecimal | 4 | 6 | 6 | 1 | 7 | 4 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0110 | 0110 | 0001 | 0111 | 0100 | 0110 | 0101 |
| ASCII | D | a | t | e |

| Hexadecimal | 3 | A | 2 | 0 | 5 | 4 | 7 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1010 | 0010 | 0000 | 0101 | 0100 | 0111 | 0101 |
| ASCII | : |  | T | u |

| Hexadecimal | 6 | 5 | 2 | C | 2 | 0 | 3 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0010 | 1100 | 0010 | 0000 | 0011 | 0000 |
| ASCII | e | , |  | 0 |

| Hexadecimal | 3 | 3 | 2 | 0 | 4 | 6 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0011 | 0010 | 0000 | 0100 | 0110 | 0110 | 0101 |
| ASCII | 3 |  | F | e |

| Hexadecimal | 6 | 2 | 2 | 0 | 3 | 2 | 3 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0010 | 0010 | 0000 | 0011 | 0010 | 0011 | 0000 |
| ASCII | b |  | 2 | 0 |

| Hexadecimal | 3 | 0 | 3 | 4 | 3 | 2 | 3 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0011 | 0100 | 0011 | 0010 | 0011 | 0011 |
| ASCII | 0 | 4 | 2 | 3 |

| Hexadecimal | 3 | A | 3 | 0 | 3 | 8 | 3 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1010 | 0011 | 0000 | 0011 | 1000 | 0011 | 1010 |
| ASCII | : | 0 | 8 | : |

| Hexadecimal | 3 | 1 | 3 | 0 | 2 | 0 | 4 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0001 | 0011 | 0000 | 0010 | 0000 | 0100 | 0111 |
| ASCII | 1 | 0 |  | G |

| Hexadecimal | 4 | D | 5 | 4 | 0 | D | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1101 | 0101 | 0100 | 0000 | 1101 | 0000 | 1010 |
| ASCII | M | T | \r | \n |

Start Bit: 0

Length: 296

IP > TCP > HTTP PDU > HTTP for the selected HTTP PDU

Field Name: HTTP

Description: This field displays the category of the page that is being displayed.

Data value (ASCII): HTTP/1.1 404 Not Found\r\n

Data values in other bases:

| Hexadecimal | 4 | 8 | 5 | 4 | 5 | 4 | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1000 | 0101 | 0100 | 0101 | 0100 | 0101 | 0000 |
| ASCII | H | T | T | P |

| Hexadecimal | 2 | F | 3 | 1 | 2 | E | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0011 | 0001 | 0010 | 1110 | 0011 | 0001 |
| ASCII | / | 1 | . | 1 |

| Hexadecimal | 2 | 0 | 3 | 4 | 3 | 0 | 3 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0011 | 0100 | 0011 | 0000 | 0011 | 0100 |
| ASCII |  | 4 | 0 | 4 |

| Hexadecimal | 2 | 0 | 4 | E | 6 | F | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0100 | 1110 | 0110 | 1111 | 0111 | 0100 |
| ASCII |  | N | o | t |

| Hexadecimal | 2 | 0 | 4 | 6 | 6 | F | 7 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0100 | 0110 | 0110 | 1111 | 0111 | 0101 |
| ASCII |  | F | o | u |

| Hexadecimal | 6 | E | 6 | 4 | 0 | D | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1110 | 0110 | 0100 | 0000 | 1101 | 0000 | 1010 |
| ASCII | n | d | \r | \n |

Start Bit: 0

Length: 40 octets

IP > TCP > HTTP PDU > Server for the selected HTTP PDU

Field Name: Server

Description: The Server response-header field contains information about the software used by the origin server to handle the request.

Field Key:  Not applicable

Data value (ASCII): Server: Apache/1.3.24 (Unix) PHP/4.2.1\r\n

Data values in other bases:

| Hexadecimal | 5 | 3 | 6 | 5 | 7 | 2 | 7 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0011 | 0110 | 0101 | 0111 | 0010 | 0111 | 0110 |
| ASCII | S | e | r | v |

| Hexadecimal | 6 | 5 | 7 | 2 | 3 | A | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0111 | 0010 | 0011 | 1010 | 0010 | 0000 |
| ASCII | e | r | : |  |

| Hexadecimal | 4 | 1 | 7 | 0 | 6 | 1 | 6 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0001 | 0111 | 0000 | 0110 | 0001 | 0110 | 0011 |
| ASCII | A | p | a | c |

| Hexadecimal | 6 | 8 | 6 | 5 | 2 | F | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1000 | 0110 | 0101 | 0010 | 1111 | 0011 | 0001 |
| ASCII | h | e | / | 1 |

| Hexadecimal | 2 | E | 3 | 3 | 2 | E | 3 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0011 | 0011 | 0010 | 1110 | 0011 | 0010 |
| ASCII | . | 3 | . | 2 |

| Hexadecimal | 3 | 4 | 2 | 0 | 2 | 8 | 5 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0100 | 0010 | 0000 | 0010 | 1000 | 0101 | 0101 |
| ASCII | 4 |  | ( | U |

| Hexadecimal | 6 | E | 6 | 9 | 7 | 8 | 2 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1110 | 0110 | 1001 | 0111 | 1000 | 0010 | 1001 |
| ASCII | n | i | x | ) |

| Hexadecimal | 2 | 0 | 5 | 0 | 4 | 8 | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0101 | 0000 | 0100 | 1000 | 0101 | 0000 |
| ASCII |  | P | H | P |

| Hexadecimal | 2 | 5 | 3 | 4 | 2 | E | 3 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0101 | 0011 | 0100 | 0010 | 1110 | 0011 | 0010 |
| ASCII | / | 4 | . | 2 |

| Hexadecimal | 2 | E | 3 | 1 | 0 | D | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0011 | 0001 | 0000 | 1101 | 0000 | 1010 |
| ASCII | . | 1 | \r | \n |

Start Bit: 0

Length: 312

IP > TCP > HTTP PDU > Data for the selected HTTP PDU

Field Name: Data

Description: This field stores the information that is actually contained in the HTTP Protocol.

Data value (ASCII): <!DOCTYPE HTML PUBLIC “-//IETF//DTD HTML 2.0//EN”>\n

<HTML><HEAD>\n

<TITLE>404 Not Found</TITLE>\n

</HEAD><BODY>\n

<H1>Not Found</H1>\n

The requested URL /~csis410/2003/bluetech/Requirements Specification Document Final-files/image002.gif was not found on this server.<p>\n

<HR>\n

<ADDRESS>Apache/1.3.24 Server at ares.cs.siena.edu Port 80</ADDRESS>\n

</BODY></HTML>\n

Data values in other bases:

| Hexadecimal | 3 | C | 2 | 1 | 4 | 4 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0010 | 0001 | 0100 | 0100 | 0100 | 0101 |
| ASCII | < | ! | D | O |

| Hexadecimal | 4 | 3 | 5 | 4 | 5 | 9 | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0011 | 0101 | 0100 | 0101 | 1001 | 0101 | 0000 |
| ASCII | C | T | Y | P |

| Hexadecimal | 4 | 5 | 2 | 0 | 4 | 8 | 5 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0101 | 0010 | 0000 | 0100 | 1000 | 0101 | 0100 |
| ASCII | E |  | H | T |

| Hexadecimal | 4 | D | 4 | C | 2 | 0 | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1101 | 0110 | 1100 | 0010 | 0000 | 0101 | 0000 |
| ASCII | M | L |  | P |

| Hexadecimal | 5 | 5 | 4 | 2 | 4 | C | 4 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0101 | 0100 | 0010 | 0100 | 1100 | 0100 | 1001 |
| ASCII | U | B | L | I |

| Hexadecimal | 4 | 3 | 2 | 0 | 2 | 2 | 2 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0011 | 0010 | 0000 | 0010 | 0010 | 0010 | 1101 |
| ASCII | C |  | “ | - |

| Hexadecimal | 2 | F | 2 | F | 4 | 9 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0010 | 1111 | 0100 | 1001 | 0100 | 0101 |
| ASCII | / | / | I | E |

| Hexadecimal | 5 | 4 | 4 | 6 | 2 | F | 2 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0100 | 0100 | 0110 | 0010 | 1111 | 0010 | 1111 |
| ASCII | T | F | / | / |

| Hexadecimal | 4 | 4 | 5 | 4 | 4 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0100 | 0101 | 0100 | 0100 | 0100 | 0010 | 0000 |
| ASCII | D | T | D |  |

| Hexadecimal | 4 | 8 | 5 | 4 | 4 | D | 4 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1000 | 0101 | 0100 | 0100 | 1101 | 0100 | 1100 |
| ASCII | H | T | M | L |

| Hexadecimal | 2 | 0 | 3 | 2 | 2 | E | 3 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0011 | 0010 | 0010 | 1110 | 0011 | 0000 |
| ASCII |  | 2 | . | 0 |

| Hexadecimal | 2 | F | 2 | F | 4 | 5 | 4 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0010 | 1111 | 0100 | 0101 | 0100 | 1110 |
| ASCII | / | / | E | N |

| Hexadecimal | 2 | 2 | 3 | E | 0 | A | 3 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0010 | 0011 | 1110 | 0000 | 1010 | 0011 | 1100 |
| ASCII | “ | > | \n | < |

| Hexadecimal | 4 | 8 | 5 | 4 | 4 | D | 4 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1000 | 0101 | 0100 | 0100 | 1101 | 0100 | 1100 |
| ASCII | H | T | M | L |

| Hexadecimal | 3 | E | 3 | C | 4 | 8 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1110 | 0011 | 1100 | 0100 | 1000 | 0100 | 0101 |
| ASCII | > | < | H | E |

| Hexadecimal | 4 | 1 | 4 | 4 | 3 | E | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0001 | 0100 | 0100 | 0011 | 1110 | 0000 | 1010 |
| ASCII | A | D | > | \n |

| Hexadecimal | 3 | C | 5 | 4 | 4 | 9 | 5 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0101 | 0100 | 0100 | 1001 | 0101 | 0100 |
| ASCII | < | T | I | T |

| Hexadecimal | 4 | C | 4 | 5 | 3 | E | 3 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1100 | 0100 | 0101 | 0011 | 1110 | 0011 | 0100 |
| ASCII | L | E | > | 4 |

| Hexadecimal | 3 | 0 | 3 | 4 | 2 | 0 | 4 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0011 | 0100 | 0010 | 0000 | 0100 | 1110 |
| ASCII | 0 | 4 |  | N |

| Hexadecimal | 6 | F | 7 | 4 | 2 | 0 | 4 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0111 | 0100 | 0010 | 0000 | 0100 | 0110 |
| ASCII | o | t |  | F |

| Hexadecimal | 6 | F | 7 | 5 | 6 | E | 6 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0111 | 0101 | 0110 | 1110 | 0110 | 0100 |
| ASCII | o | u | n | d |

| Hexadecimal | 3 | C | 2 | F | 5 | 4 | 4 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0010 | 1111 | 0101 | 0100 | 0100 | 1001 |
| ASCII | < | / | T | I |

| Hexadecimal | 5 | 4 | 4 | C | 4 | 5 | 3 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0100 | 0100 | 1100 | 0100 | 0101 | 0011 | 1110 |
| ASCII | T | L | E | > |

| Hexadecimal | 0 | A | 3 | C | 2 | F | 4 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 1010 | 0011 | 1100 | 0010 | 1111 | 0100 | 1000 |
| ASCII | \n | < | / | H |

| Hexadecimal | 4 | 5 | 4 | 1 | 4 | 4 | 3 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0101 | 0100 | 0001 | 0100 | 0100 | 0011 | 1110 |
| ASCII | E | A | D | > |

| Hexadecimal | 3 | C | 4 | 2 | 4 | F | 4 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0100 | 0010 | 0100 | 1111 | 0100 | 0100 |
| ASCII | < | B | O | D |

| Hexadecimal | 5 | 9 | 3 | E | 0 | A | 3 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 1001 | 0011 | 1110 | 0000 | 1010 | 0011 | 1100 |
| ASCII | Y | > | \n | < |

| Hexadecimal | 4 | 8 | 3 | 1 | 3 | E | 4 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1000 | 0011 | 0001 | 0011 | 1110 | 0100 | 1110 |
| ASCII | H | 1 | > | N |

| Hexadecimal | 6 | F | 7 | 4 | 2 | 0 | 4 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0111 | 0100 | 0010 | 0000 | 0100 | 0110 |
| ASCII | o | t |  | F |

| Hexadecimal | 6 | F | 7 | 5 | 6 | E | 6 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1111 | 0111 | 0101 | 0110 | 1110 | 0110 | 0100 |
| ASCII | o | u | n | d |

| Hexadecimal | 3 | C | 2 | F | 4 | 8 | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0010 | 1111 | 0100 | 1000 | 0011 | 0001 |
| ASCII | < | / | H | 1 |

| Hexadecimal | 3 | E | 0 | A | 5 | 4 | 6 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1110 | 0000 | 1010 | 0101 | 0100 | 0110 | 1000 |
| ASCII | > | \n | T | h |

| Hexadecimal | 6 | 5 | 2 | 0 | 7 | 2 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0010 | 0000 | 0111 | 0010 | 0110 | 0101 |
| ASCII | e |  | r | e |

| Hexadecimal | 7 | 1 | 7 | 5 | 6 | 5 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0001 | 0111 | 0101 | 0110 | 0101 | 0111 | 0011 |
| ASCII | q | u | e | s |

| Hexadecimal | 7 | 4 | 6 | 5 | 6 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0100 | 0110 | 0101 | 0110 | 0100 | 0010 | 0000 |
| ASCII | t | e | d |  |

| Hexadecimal | 5 | 5 | 5 | 2 | 4 | C | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0101 | 0101 | 0010 | 0100 | 1100 | 0010 | 0000 |
| ASCII | U | R | L |  |

| Hexadecimal | 2 | F | 7 | E | 6 | 3 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0111 | 1110 | 0110 | 0011 | 0111 | 0011 |
| ASCII | / | ~ | c | s |

| Hexadecimal | 6 | 9 | 7 | 3 | 3 | 4 | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0111 | 0011 | 0011 | 0100 | 0011 | 0001 |
| ASCII | i | s | 4 | 1 |

| Hexadecimal | 3 | 0 | 2 | F | 3 | 2 | 3 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0010 | 1111 | 0011 | 0010 | 0011 | 0000 |
| ASCII | 0 | / | 2 | 0 |

| Hexadecimal | 3 | 0 | 3 | 3 | 2 | F | 6 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0011 | 0011 | 0010 | 1111 | 0110 | 0010 |
| ASCII | 0 | 3 | / | b |

| Hexadecimal | 6 | C | 7 | 5 | 6 | 5 | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1100 | 0111 | 0101 | 0110 | 0101 | 0111 | 0100 |
| ASCII | l | u | e | t |

| Hexadecimal | 6 | 5 | 6 | 3 | 6 | 8 | 2 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 0011 | 0110 | 1000 | 0010 | 1111 |
| ASCII | e | c | h | / |

| Hexadecimal | 5 | 2 | 6 | 5 | 7 | 1 | 7 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0010 | 0110 | 0101 | 0111 | 0001 | 0111 | 0101 |
| ASCII | R | e | q | u |

| Hexadecimal | 6 | 9 | 7 | 2 | 6 | 5 | 6 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0111 | 0010 | 0110 | 0101 | 0110 | 1101 |
| ASCII | i | r | e | m |

| Hexadecimal | 6 | 5 | 6 | E | 7 | 4 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 1110 | 0111 | 0100 | 0111 | 0011 |
| ASCII | e | n | t | s |

| Hexadecimal | 2 | 0 | 5 | 3 | 7 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0101 | 0011 | 0111 | 0000 | 0110 | 0101 |
| ASCII |  | S | p | e |

| Hexadecimal | 6 | 3 | 6 | 9 | 6 | 6 | 6 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0011 | 0110 | 1001 | 0110 | 0110 | 0110 | 1001 |
| ASCII | c | i | f | i |

| Hexadecimal | 6 | 3 | 6 | 1 | 7 | 4 | 6 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0011 | 0110 | 0001 | 0111 | 0100 | 0110 | 1001 |
| ASCII | c | a | t | i |

| Hexadecimal | 6 | F | 6 | E | 2 | 0 | 4 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0110 | 1110 | 0010 | 0000 | 0100 | 0100 |
| ASCII | o | n |  | D |

| Hexadecimal | 6 | F | 6 | 3 | 7 | 5 | 6 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1111 | 0110 | 0011 | 0111 | 0101 | 0110 | 1101 |
| ASCII | o | c | u | m |

| Hexadecimal | 6 | 5 | 6 | E | 7 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0110 | 1110 | 0111 | 0100 | 0010 | 0000 |
| ASCII | e | n | t |  |

| Hexadecimal | 4 | 6 | 6 | 9 | 6 | E | 6 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0110 | 0110 | 1001 | 0110 | 1110 | 0110 | 0001 |
| ASCII | F | i | n | a |

| Hexadecimal | 6 | C | 5 | F | 6 | 6 | 6 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1100 | 0101 | 1111 | 0110 | 0110 | 0110 | 1001 |
| ASCII | l | - | f | i |

| Hexadecimal | 6 | C | 6 | 5 | 7 | 3 | 2 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1100 | 0110 | 0101 | 0111 | 0011 | 0010 | 1111 |
| ASCII | l | e | s | / |

| Hexadecimal | 6 | 9 | 6 | D | 6 | 1 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0110 | 1101 | 0110 | 0001 | 0110 | 0111 |
| ASCII | i | m | a | g |

| Hexadecimal | 6 | 5 | 3 | 0 | 3 | 0 | 3 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0011 | 0000 | 0011 | 0000 | 0011 | 0010 |
| ASCII | e | 0 | 0 | 2 |

| Hexadecimal | 2 | E | 6 | 7 | 6 | 9 | 6 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0110 | 0111 | 0110 | 1001 | 0110 | 0110 |
| ASCII | . | g | i | f |

| Hexadecimal | 2 | 0 | 7 | 7 | 6 | 1 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0001 | 0000 | 0111 | 0111 | 0110 | 0001 | 0111 | 0011 |
| ASCII |  | w | a | s |

| Hexadecimal | 2 | 0 | 6 | E | 6 | F | 7 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 1110 | 0110 | 1111 | 0111 | 0100 |
| ASCII |  | n | o | t |

| Hexadecimal | 2 | 0 | 6 | 6 | 6 | F | 7 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 0110 | 0110 | 1111 | 0111 | 0101 |
| ASCII |  | f | o | u |

| Hexadecimal | 6 | E | 6 | 4 | 2 | 0 | 6 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1110 | 0110 | 0100 | 0010 | 0000 | 0110 | 1111 |
| ASCII | n | d |  | o |

| Hexadecimal | 6 | E | 2 | 0 | 7 | 4 | 6 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1110 | 0010 | 0000 | 0111 | 0100 | 0110 | 1000 |
| ASCII | n |  | t | h |

| Hexadecimal | 6 | 9 | 7 | 3 | 2 | 0 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1001 | 0111 | 0011 | 0010 | 0000 | 0111 | 0011 |
| ASCII | i | s |  | s |

| Hexadecimal | 6 | 5 | 7 | 2 | 7 | 6 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0101 | 0111 | 0010 | 0111 | 0110 | 0110 | 0101 |
| ASCII | e | r | v | e |

| Hexadecimal | 7 | 2 | 2 | E | 3 | C | 5 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0010 | 1110 | 0011 | 1100 | 0101 | 0000 |
| ASCII | r | . | < | p |

| Hexadecimal | 3 | E | 0 | A | 3 | C | 4 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1110 | 0000 | 1010 | 0011 | 1100 | 0100 | 1000 |
| ASCII | > | \n | < | H |

| Hexadecimal | 5 | 2 | 3 | E | 0 | 4 | 3 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0010 | 0011 | 1110 | 0000 | 0100 | 0011 | 1100 |
| ASCII | R | > | \n | < |

| Hexadecimal | 4 | 1 | 4 | 4 | 4 | 4 | 5 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0001 | 0100 | 0100 | 0100 | 0100 | 0101 | 0010 |
| ASCII | A | D | D | R |

| Hexadecimal | 4 | 5 | 5 | 3 | 5 | 3 | 3 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0101 | 0101 | 0011 | 0101 | 0011 | 0011 | 1110 |
| ASCII | E | S | S | > |

| Hexadecimal | 4 | 1 | 7 | 0 | 6 | 1 | 6 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0001 | 0111 | 0000 | 0110 | 0001 | 0110 | 0011 |
| ASCII | A | p | a | c |

| Hexadecimal | 6 | 8 | 6 | 5 | 2 | F | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 1000 | 0110 | 0101 | 0010 | 1111 | 0011 | 0001 |
| ASCII | h | e | / | 1 |

| Hexadecimal | 2 | E | 3 | 3 | 2 | E | 3 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0011 | 0011 | 0010 | 1110 | 0011 | 0010 |
| ASCII | . | 3 | . | 2 |

| Hexadecimal | 3 | 4 | 2 | 0 | 5 | 3 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0100 | 0010 | 0000 | 0101 | 0011 | 0110 | 0101 |
| ASCII | 4 |  | S | e |

| Hexadecimal | 7 | 2 | 7 | 6 | 6 | 5 | 7 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0111 | 0110 | 0110 | 0101 | 0111 | 0010 |
| ASCII | r | v | e | r |

| Hexadecimal | 2 | 0 | 6 | 1 | 7 | 4 | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 0000 | 0110 | 0001 | 0111 | 0100 | 0010 | 0000 |
| ASCII |  | a | t |  |

| Hexadecimal | 3 | 1 | 7 | 2 | 6 | 5 | 7 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0001 | 0111 | 0010 | 0110 | 0101 | 0111 | 0011 |
| ASCII | a | r | e | s |

| Hexadecimal | 2 | E | 6 | 3 | 7 | 3 | 2 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1110 | 0110 | 0011 | 0111 | 0011 | 0010 | 1110 |
| ASCII | . | c | s | . |

| Hexadecimal | 7 | 3 | 6 | 9 | 6 | 5 | 6 | E |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0011 | 0110 | 1001 | 0110 | 0101 | 0110 | 1110 |
| ASCII | s | i | e | n |

| Hexadecimal | 6 | 1 | 2 | E | 6 | 5 | 6 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0110 | 0001 | 0010 | 1110 | 0110 | 0101 | 0110 | 0100 |
| ASCII | a | . | e | d |

| Hexadecimal | 7 | 5 | 2 | 0 | 5 | 0 | 6 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0101 | 0010 | 0000 | 0101 | 0000 | 0110 | 1111 |
| ASCII | u |  | P | o |

| Hexadecimal | 7 | 2 | 7 | 4 | 2 | 0 | 3 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0111 | 0100 | 0010 | 0000 | 0011 | 1000 |
| ASCII | r | t |  | 8 |

| Hexadecimal | 3 | 0 | 3 | C | 2 | F | 4 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 0010 | 1100 | 0010 | 1111 | 0100 | 0001 |
| ASCII | 0 | < | / | A |

| Hexadecimal | 4 | 4 | 4 | 4 | 5 | 2 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0100 | 0100 | 0100 | 0101 | 0010 | 0100 | 0101 |
| ASCII | D | D | R | E |

| Hexadecimal | 5 | 3 | 5 | 3 | 3 | E | 0 | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0011 | 0101 | 0011 | 0011 | 1110 | 0000 | 1010 |
| ASCII | S | S | > | \n |

| Hexadecimal | 3 | C | 2 | F | 4 | 2 | 4 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0011 | 1100 | 0010 | 1111 | 0100 | 0010 | 0100 | 1111 |
| ASCII | < | / | B | O |

| Hexadecimal | 4 | 4 | 5 | 9 | 3 | E | 3 | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 0100 | 0101 | 1001 | 0011 | 1110 | 0011 | 1100 |
| ASCII | D | Y | > | < |

| Hexadecimal | 2 | F | 4 | 8 | 5 | 4 | 4 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0010 | 1111 | 0100 | 1000 | 0101 | 0100 | 0100 | 1101 |
| ASCII | / | H | T | M |

| Hexadecimal | 4 | C | 3 | E | 0 | A |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 0100 | 1100 | 0011 | 1110 | 0000 | 1010 |
| ASCII | L | > | \n |

Start Bit: 0

Length: 351

2.2.12 IP PDU for the selected SSH PDU

IP PDU > IP Version for the selected SSH PDU

Field Name: IP Version

Description:  Version is a 4-bit field that indicates the format of the Internet header.

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |

Start Bit: 0

Length: 4

IP PDU > Header Length for the selected SSH PDU

Field Name:  Header Length

Description:  The IHL field is a 4-bit field indicating the length of the Internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data values in other bases:

| Hexadecimal | 5 |
| --- | --- |
| Binary | 0101 |

Start Bit: 4

Length: 4

IP PDU > Type of Service for the selected SSH PDU

Field Name:  Type of Service

Description:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a data gram through a particular network.

The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D) 0 = Normal Delay		1 = Low Delay

Bit 4: (T) 0 = Normal Throughput	1 = High Throughput

Bit 5: (R) 0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (decimal): 16

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 0 in decimal.

Start Bit: 8

Length: 8

IP PDU > Total Length of Ethernet Frame for the selected SSH PDU

Field Name: Total Length of Ethernet Frame

Description: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including Internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Data values (decimal):  100

Data values in other bases:

| Hexadecimal | 0 | 0 | 6 | 4 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0110 | 0100 |

Start Bit: 16

Length: 16

IP PDU > Identification for the selected SSH PDU

Field Name:  Identification

Description:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a data gram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the data gram or any fragment could be alive in the Internet.

Data value (decimal): 12490

Data values in other bases:

| Hexadecimal | 3 | 0 | C | A |
| --- | --- | --- | --- | --- |
| Binary | 0011 | 0000 | 1100 | 1010 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 12942 in decimal.

Start Bit: 32

Length: 16

IP PDU > Flags for the selected SSH PDU

Field Name:  Flags

Description:  Flags is a 3-bit field that indicates directions for fragmentation.

Bit 0: reserved, must be 0

Bit 1: (DF) 0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 001 in binary.

Start Bit: 4

Length: 4

IP PDU > Fragment Offset for the selected SSH PDU

Field Name:  Fragment Offset

Description:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |

Start Bit: 51

Length: 13

IP PDU > Time to Live for the selected SSH PDU

Field Name: Time to Live

Description: Time to Live is an 8-bit field that indicates the maximum time the data gram is allowed to remain in the Internet.  If this field contains the value 0, then the data gram must be destroyed.  This field is modified in Internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the data gram is allowed to be in the Internet.  This field is decreased at each point that the Internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum data gram lifetime.

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |

Start Bit: 64

Length: 8

IP PDU > Protocol for the selected SSH PDU

Field Name:  Protocol

Description:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the Internet diagram.

# Dec Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and 
                                                                                                                                       Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet 
 											   Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET 
 											   Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core 
 										   Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET 
 											   Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	10	SSH						116		74	   WIDEBAND 
 											   Monitoring

17	11	XNET						117		75	   WIDEBAND 
 											   EXPAK

20	14	Chaos						120-376	78-0178  Unassigned

21	15	User Datagram				377		0179	    Reserved

Data value (decimal): 6

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |

Start Bit: 72

Length: 8

RFC Link: http://www.faqs.org/rfcs/rfc790.html

IP PDU > Header Checksum for the selected SSH PDU

Field Name:  Header Checksum

Description:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Data value (decimal): 34734

Data values in other bases:

| Hexadecimal | 8 | 7 | A | E |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 0111 | 1010 | 1110 |

Start Bit: 80

Length: 16

IP PDU > Source IP Address for the selected SSH PDU

Field Name:  Source IP Address

Description:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |

Start Bit: 96

Length: 32

IP PDU > Destination IP Address for the selected SSH PDU

Field Name:  Destination IP Address

Description:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

Data value (decimal):  192.168.0.102

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0110 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 192.168.0.39 in decimal.

Start Bit: 128

Length: 32

2.2.13 TCP PDU for the selected SSH PDU

IP > TCP PDU > Source Port Number for the selected SSH PDU

Field Name:  Source Port Number

Description: This 16-bit number represents the name of the application that sent the data in the IP packet.

Data value (decimal): 1243

Data values in other bases:

| Hexadecimal | 0 | 4 | D | B |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0100 | 1101 | 1011 |

Start Bit: 0

Length: 16

IP > TCP PDU > Destination Port Number for the selected SSH PDU

Field Name: Destination Port Number

Description:
This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

This key indicates assigned port number values:

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (decimal): 22

Data values in other bases:

| Hexadecimal | 0 | 0 | 1 | 6 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 1243 in decimal.

Start Bit: 16

Length: 16

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

IP > TCP PDU > Sequence Number for the selected SSH PDU

Field Name:  Sequence Number

Description: TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Data value (decimal): 4008673261

Data values in other bases:

| Hexadecimal | E | E | E | F | 7 | F | E | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1110 | 1110 | 1110 | 1111 | 0111 | 1111 | 1110 | 1101 |

Start Bit: 32

Length: 32

IP > TCP PDU > Acknowledgement Number for the selected SSH PDU

Field Name: Acknowledgement Number

Description: This number is used by the receiving computer to acknowledge which packets have successfully arrived. This number will be the sequence number of the next packet the receiver is ready to receive.

Data value (decimal): 3798775616

Data values in other bases:

| Hexadecimal | E | 2 | 6 | C | B | 7 | 4 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1110 | 0010 | 0110 | 1100 | 1011 | 0111 | 0100 | 0000 |

Start Bit: 64

Length: 32

IP > TCP PDU > Length or Offset for the selected SSH PDU

Field Name: Length or Offset

Description: This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header.

Data value (decimal): 8

Data values in other bases:

| Hexadecimal | 0 | 8 |
| --- | --- | --- |
| Binary | 0000 | 1000 |

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 32 in decimal.

Start Bit: 96

Length: 4

IP > TCP PDU > Control Flags for the selected SSH PDU

Field Name:  Control Flags

Description: Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

- Urgent (URG)

- Acknowledgement (ACK)

- Push (PSH)

- Reset (RST)

- Synchronize (SYN)

- Finish (FIN)

Data value (decimal): 24

Data values in other bases:

| Hexadecimal | 1 | 8 |
| --- | --- | --- |
| Binary | 0001 | 1000 |

Start Bit: 106

Length: 6

IP > TCP PDU > Window Size for the selected SSH PDU

Field Name:  Window Size

Description: Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Data value (decimal): 32120

Data values in other bases:

| Hexadecimal | 7 | D | 7 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 1101 | 0111 | 1000 |

Start Bit: 112

Length: 16

IP > TCP PDU > TCP Checksum for the selected SSH PDU

Field Name:  TCP Checksum

Description: Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Data value (decimal): 35786

Data values in other bases:

| Hexadecimal | 8 | B | C | A |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 1011 | 1100 | 1010 |

Start Bit: 128

Length: 16

IP > TCP PDU > Options for the selected SSH PDU

Field Name: Options

Description: Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits.

Data value: 01 01 08 0A 1B 25 F3 A1 0B DD 73 58

- The data value used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s data value was 01 01 08 0A 0B D1 8D EC 1A AC 06 AB in hexidecimal.

Start Bit: 160

Length: Variable

2.2.14 IP PDU for the selected TELNET PDU

IP PDU > IP Version for the selected TELNET PDU

Field Name: IP Version

Description:  Version is a 4-bit field that indicates the format of the Internet header.

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |

Start Bit: 0

Length: 4

IP PDU > Header Length for the selected TELNET PDU

Field Name: Header Length

Description:  The IHL field is a 4-bit field indicating the length of the Internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Data value:  The value contained in our field is 20 bytes.  This is the hexadecimal and decimal value of 5 multiplied by 4 bits.

Data value (decimal): 5

Data values in other bases:

| Hexadecimal | 5 |
| --- | --- |
| Binary | 0101 |

Start Bit: 4

Length: 4

IP PDU > Type of Service for the selected TELNET PDU

Field Name:  Type of Service

Description:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a data gram through a particular network.

The major choice is a three-way tradeoff between low-delay, high-reliability, and high-throughput.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internet work Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Override			000 = Routine

Data value (decimal): 00

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |

Start Bit: 8

Length: 8

IP PDU > Total Length for the selected TELNET PDU

Field Name: Total Length

Description: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including Internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Data values (decimal):  125

Data values in other bases:

| Hexadecimal | 00 | 7D |
| --- | --- | --- |
| Binary | 1111 | 1101 |

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 0011 1110

Start Bit: 16

Length: 16

IP PDU > Identification for the selected TELNET PDU

Field Name:  Identification

Description:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a data gram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the data gram or any fragment could be alive in the Internet.

Data value (decimal): 51102

Data values in other bases:

| Hexadecimal | C | 7 | 9 | E |
| --- | --- | --- | --- | --- |
| Binary | 1100 | 0111 | 1001 | 1110 |

.

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 1100 0111 0101 0111

Start Bit: 32

Length: 16

IP PDU > Flags for the selected TELNET PDU

Field Name:  Flags

Description:  Flags is a 3-bit field that indicates directions for fragmentation.

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 010

Data values in other bases:  Not applicable

Start Bit: 48

Length: 3

IP PDU > Fragment Offset for the selected TELNET PDU

Field Name:  Fragment Offset

Description:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |

Start Bit: 51

Length: 13

IP PDU > Time to Live for the selected TELNET PDU

Field Name: Time to Live

Description:  Time to Live is an 8-bit field that indicates the maximum time the data gram is allowed to remain in the Internet.  If this field contains the value 0, then the data gram must be destroyed.  This field is modified in Internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the data gram is allowed to be in the Internet.  This field is decreased at each point that the Internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum data gram lifetime.

Data value (decimal): 64

Data values in other bases:

| Hexadecimal | 4 | 0 |
| --- | --- | --- |
| Binary | 0100 | 0000 |

Start Bit: 64

Length: 8

IP PDU > Protocol for the selected TELNET PDU

Field Name:  Protocol

Description:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the Internet diagram.

# Dec 	Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and 
 											   Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet 
 											   Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET 
 											   Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core 
 											   Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET 
 											   Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	  10	Telnet						116		74	   WIDEBAND 
 											   Monitoring

17	  11	XNET						117		75	   WIDEBAND 
 											   EXPAK

20	  14	Chaos						120-376	78-0178  Unassigned

21	  15	User Datagram				377		0179	    Reserved

Data value (decimal): 6

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |

Start Bit: 72

Length: 8

RFC Link: http://www.faqs.org/rfcs/rfc790.html

IP PDU > Header Checksum for the selected TELNET PDU

Field Name:  Header Checksum

Description:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Data value (decimal): 61695

Data values in other bases:

| Hexadecimal | F | 0 | F | F |
| --- | --- | --- | --- | --- |
| Binary | 1111 | 0000 | 1111 | 1111 |

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 1111 0001 1000 0101

Start Bit: 80

Length: 16

IP PDU > Source IP Address for the selected TELNET PDU

Field Name:  Source IP Address

Description:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

The source address of the sender of the IP data gram:
NET ID ADDRESS RANGE
000-127 Class A 10.0.0.0-10.225.225
128-191 Class B 172.16.0.0-172.31.255.255
192-223 Class C 192.168.0.0-192.168.255.255
224-239 Class D (multicast)
240-255 Class E (experimental)
HOST ID
0 Network value; broadcast(old)
255 Broadcast

Data value (decimal):  192.168.0.101

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |

Start Bit: 96

Length: 32

IP PDU > Destination IP Address for the selected TELNET PDU

Field Name:  Destination IP Address

Description:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

The IP address of the host where this data gram is being sent:
NET ID ADDRESS RANGE
000-127 Class A 10.0.0.0-10.225.225
128-191 Class B 172.16.0.0-172.31.255.255
192-223 Class C 192.168.0.0-192.168.255.255
224-239 Class D (multicast)
240-255 Class E (experimental)
HOST ID
0 Network value; broadcast(old)
255 Broadcast

Data value (decimal):  192.168.0.39

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 2 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0010 | 0111 |

Start Bit: 128

Length: 32

IP > TCP PDU > Options for the selected TELNET PDU

Field Name: Options

Description: The options may or may not appear in Ethernet packets. Options have to be implemented by all IP modules (host and gateways). What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length. There may be zero or more options. There are two cases for the format of an option.

Case 1: A single octet of option type
Case 2: An option-type octet, an option-length octet, and the actual option-data octets

Data value: Not applicable

Start Bit: 160

Length: Variable (0-40)

2.2.15 TCP PDU for the selected TELNET PDU

IP > TCP PDU > Source Port Number for the selected TELNET PDU

Field Name:  Source Port Number

Description: A 16-bit address assigned by the sending computer, to the application program sending data as TCP data grams.

Data value (ASCII): TELNET (23)

Data values in other bases:

| Hexadecimal | 0 | 0 | 1 | 7 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0001 | 0111 |

Start Bit: 0

Length: 16

IP > TCP PDU > Destination Port Number for the selected TELNET PDU

Field Name: Destination Port Number

Description: This 16-bit number represents the name of the application that is to receive the data contained within the IP packet. This is one of the major differences between a Layer 3 and a Layer 4 header: the Layer 3 header contains the IP address of the computer that is to receive the IP packet; once that packet has been received, the port address in the Layer 4 header ensures that the data contained within that IP packet is passed to the correct application on that computer.

# Dec		      Port Numbers

0             		Reserved

1-32767       	Internet registered ("well-known") protocols

32768-98303   	Reserved, to allow TCPv7-TCPv4 conversion

98304 & up      	Dynamic assignment

Data value (decimal): 32805

Data values in other bases:

| Hexadecimal | 8 | 0 | 2 | 5 |
| --- | --- | --- | --- | --- |
| Binary | 1000 | 0000 | 0010 | 0101 |

Start Bit: 16

Length: 16

Source: http://www.zvon.org/tmRFC/RFC1475/Output/chapter4.html

IP > TCP PDU > Sequence Number for the selected TELNET PDU

Field Name:  Sequence Number

Description: TCP is responsible for ensuring that all IP packets sent are actually received. When an application's data is packaged into IP packets, TCP will give each IP packet a sequence number. Once all the packets have arrived at the receiving computer, TCP uses the number in this 32-bit field to ensure that all of the packets actually arrived and are in the correct sequence.

Data value (decimal): 263530302

Data values in other bases:

| Hexadecimal | 9 | D | 1 | 3 | 8 | 8 | 6 | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1001 | 1101 | 0001 | 0011 | 1000 | 1000 | 0110 | 1101 |

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 1001 1101 0001 0011 1000 1000 0000 1000

Start Bit: 32

Length: 32

IP > TCP PDU > Acknowledgement Number for the selected TELNET PDU

Field Name: Acknowledgement Number

Description: The receiving computer to acknowledge which packets have successfully arrived uses this number. This number will be the sequence number of the next packet the receiver is ready to receive.

Data value: 2526101273

Data values in other bases:

| Hexadecimal | 9 | 6 | 9 | 1 | 3 | F | 1 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1001 | 0110 | 1001 | 0001 | 0011 | 1111 | 0001 | 1001 |

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 1001 0110 1001 0001 0011 1111 0000 0101

Start Bit: 64

Length: 32

IP > TCP PDU > Length for the selected TELNET PDU

Field Name:  Length

Description: This is identical in concept to the header length in an IP packet, except this time it indicates the length of the TCP header.

Data value (decimal): 128

Data values in other bases:

| Hexadecimal | 8 | 0 |
| --- | --- | --- |
| Binary | 1000 | 0000 |

Start Bit: 96

Length: 4

IP > TCP PDU > Reserved for the selected TELNET PDU

Field Name:  Reserved

Description: 4 bits; set to 0
ECN bits (used when ECN employed; else 00)
CWR (1=sender has cut congestion window in half
ECN-Echo (1=receiver has cut congestion window in half

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |

Start Bit: 100

Length: 6

IP > TCP PDU > Control Flags for the selected TELNET PDU

Field Name:  Control Flags

Description: Every TCP packet contains this 6-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

- Urgent (URG)

- Acknowledgement (ACK)

- Push (PSH)

- Reset (RST)

- Synchronize (SYN)

- Finish (FIN)

Data value (decimal): 24

Data values in other bases:

| Hexadecimal | 1 | 8 |
| --- | --- | --- |
| Binary | 0001 | 1000 |

Start Bit: 106

Length: 6

IP > TCP PDU > Window Size for the selected TELNET PDU

Field Name:  Window Size

Description: Every TCP packet contains this 16-bit value that indicates how many octets it can receive at once. When IP packets are received, they are placed in a temporary area of RAM known as a buffer until the receiving computer has a chance to process them; this value represents how big a buffer the receiving host has made available for this temporary storage of IP packets.

Data value (decimal): 32120

Data values in other bases:

| Hexadecimal | 7 | D | 7 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0111 | 1101 | 0111 | 1000 |

Start Bit: 116

Length: 16

IP > TCP PDU > TCP Checksum for the selected TELNET PDU

Field Name:  TCP Checksum

Description: Unlike IP, TCP is responsible for ensuring that the entire IP packet arrived intact. TCP will run a CRC on the entire IP packet (not just the header) and place the resulting checksum in this field. When the IP packet is received, TCP re-runs the CRC on the entire packet to ensure the checksum is the same.

Data value (decimal): 63307

Data values in other bases:

| Hexadecimal | F | 7 | 4 | B |
| --- | --- | --- | --- | --- |
| Binary | 1111 | 0111 | 0100 | 1011 |

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 0101 1001 1000 1001

Start Bit: 128

Length: 16

IP > TCP PDU > Urgent Pointer for the selected TELNET PDU

Field Name: Urgent Pointer

Description: A 16-bit pointer to the last byte within the segment, which is urgent and should be expected in delivery-valid only if URG flag is set.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0000 |

Start Bit: 144

Length: 16

IP > TCP PDU > Options for the selected TELNET PDU

Field Name: Options

Description: Like IP options, this field is optional and represents additional instructions not covered in the other TCP fields. Again, if an option does not fill up a 32-bit word, it will be filled in with padding bits.

Data value (hexadecimal): 01 01 08	0A 0B D1 8D EC 1A AC 06 AB

Data values in other bases:

| Hexadecimal | 0 | 1 | 0 | 1 | 0 | 8 | 0 | A | 0 | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0000 | 0001 | 0000 | 0001 | 0000 | 1000 | 0000 | 1010 | 0000 | 1011 |

| Hexadecimal | D | 1 | 8 | D | E | C | 1 | A | A | C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1101 | 0001 | 1000 | 1101 | 1110 | 1100 | 0001 | 1010 | 1010 | 1100 |

| Hexadecimal | 0 | 6 | A | B |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0110 | 1010 | 1011 |

2.2.16 TELNET PDU for the selected TELNET PDU

IP >TCP > TELNET PDU for the TELNET Packet

Field Name: Telnet PDU

Description: PASS (Password)

The argument field is a Telnet string specifying the user’s password.  This command must be immediately preceded by the user name command, and, for some sites, completes the user’s identification for access control.

What is contained in the Packet:

Request:	PASS

Data Values (hexadecimal): 50 61 73 73 77 6F 72 64 3A 20

Data Values in Other Bases:

| Hexadecimal | 5 | 0 | 6 | 1 | 7 | 3 | 7 | 7 | 6 | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0101 | 0000 | 0110 | 0001 | 0111 | 0011 | 0111 | 0111 | 0110 | 1111 |
| ASCII | P | a | s | w | o |

| Hexadecimal | 7 | 2 | 6 | 4 | 3 | A | 2 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 0111 | 0010 | 0110 | 0100 | 0011 | 1010 | 0010 | 0000 |
| ASCII | r | d | : | © |

RFC Link: http://www.ietf.org/rfc/rfc0959.txt?number=959

2.2.17 ARP PDU for the selected ARP PDU

ARP PDU> Hardware Type > for the selected ARP PDU

Field Name: Hardware Type

Description:  The physical media that communicates on the network.

Data value (decimal):  1

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0001 |

# Start Bit: 0

Length: 16

ARP PDU > Protocol Type > for the selected ARP PDU

Field Name: Protocol Type

Description:  Defines the protocol that the terminals are using to connect with each other.

Data value (decimal): 2048

Data values in other bases:

| Hexadecimal | 0 | 8 | 0 | 0 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 1000 | 0000 | 0000 |

Start Bit: 16

Length: 16

ARP PDU > Hardware size > for the selected ARP PDU

Field Name:  Hardware size

Description: This field determines the type of hardware used.

Data value (decimal): 6

Data values in other bases:

| Hexadecimal | 0 | 6 |
| --- | --- | --- |
| Binary | 0000 | 0110 |

Start Bit: 32

Length: 8

ARP PDU >Protocol size>for the selected ARP PDU

Field Name:  Protocol size

Description: Determines the protocol used in the request or response.   .

Data value (decimal):  2

Data values in other bases:

| Hexadecimal | 0 | 2 |
| --- | --- | --- |
| Binary | 0000 | 0010 |

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 0000 0100

Start Bit: 40

Length: 8

ARP PDU > Opcode Request> for the selected ARP PDU

Field Name: Opcode Request

Description: Determines weather a request or a response is being called upon.

Data value (decimal):  1

Data values in other bases:

| Hexadecimal | 0 | 0 | 0 | 1 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0000 | 0000 | 0001 |

Start Bit: 48

Length: 16

# ARP PDU > Sender Hardware Address > for the selected ARP PDU

Field Name:  Sender Hardware Address

Description: The Physical address or MAC address of the network adapter of the sender’s terminal.

00000C  Cisco

00000E  Fujitsu

00000F  NeXT

000010  Sytek

00001D  Cabletron

000020  DIAB (Data Intdustrier AB)

000022  Visual Technology

00002A  TRW

000032  GPT Limited (reassigned from GEC Computers Ltd)

00005A  S & Koch

00005E  IANA

000065  Network General

00006B  MIPS

000077  MIPS

00007A  Ardent

000089  Cayman Systems  Gatorbox

000093  Proteon

00009F  Ameristar Technology

0000A2  Wellfleet

0000A3  Network Application Technology

0000A6  Network General (internal assignment, not for products)

0000A7  NCD  	X-terminals

0000A9  Network Systems

0000AA  Xerox	Xerox machines

0000B3  CIMLinc

0000B7  Dove            Fastnet

0000BC  Allen-Bradley

0000C0  Western Digital

0000C5  Farallon phone net card

0000C6  HP Intelligent Networks Operation (formerly Eon Systems)

0000C8  Altos

0000C9  Emulex          Terminal Servers

0000D7  Dartmouth College (NED Router)

0000D8  3Com? Novell?   PS/2

0000DD  Gould

0000DE  Unigraph

0000E2  Acer Counterpoint

0000EF  Alantec

0000FD  High Level Hardvare (Orion, UK)

000102  BBN             BBN internal usage (not registered)

0020AF  3COM ???

001700  Kabel

008064  Wyse Technology / Link Technologies

00802B  IMAC ???

00802D  Xylogics, Inc.  Annex terminal servers

00808C  Frontier Software Development

0080C2  IEEE 802.1 Committee

0080D3  Shiva

00AA00  Intel

00DD00  Ungermann-Bass

00DD01  Ungermann-Bass

020701  Racal InterLan

020406  BBN             BBN internal usage (not registered)

026086  Satelcom MegaPac (UK)

02608C  3Com            IBM PC; Imagen; Valid; Cisco

02CF1F  CMC             Masscomp; Silicon Graphics; Prime EXL

080002  3Com (Formerly Bridge)

080003  ACC (Advanced Computer Communications)

080005  Symbolics       Symbolics LISP machines

080008  BBN

080009  Hewlett-Packard

08000A  Nestar Systems

08000B  Unisys

080011  Tektronix, Inc.

080014  Excelan         BBN Butterfly, Masscomp, Silicon Graphics

080017  NSC

08001A  Data General

08001B  Data General

08001E  Apollo

080020  Sun             Sun machines

080022  NBI

080025  CDC

080026  Norsk Data (Nord)

080027  PCS Computer Systems GmbH

080028  TI              Explorer

08002B  DEC

08002E  Metaphor

08002F  Prime Computer  Prime 50-Series LHC300

080036  Intergraph      CAE stations

080037  Fujitsu-Xerox

080038  Bull

080039  Spider Systems

080041  DCA Digital Comm. Assoc.

080045  ???? (maybe Xylogics, but they claim not to know this number)

080046  Sony

080047  Sequent

080049  Univation

08004C  Encore

08004E  BICC

080056  Stanford University

080058  ???             DECsystem-20

08005A  IBM

080067  Comdesign

080068  Ridge

080069  Silicon Graphics

08006E  Concurrent      Masscomp

080075  DDE (Danish Data Elektronik A/S)

08007C  Vitalink        TransLAN III

080080  XIOS

080086  Imagen/QMS

080087  Xyplex          terminal servers

080089  Kinetics        AppleTalk-Ethernet interface

08008B  Pyramid

08008D  XyVision        XyVision machines

080090  Retix Inc       Bridges

484453  HDS ???

800010  AT&T

AA0000  DEC             obsolete

AA0001  DEC             obsolete

AA0002  DEC             obsolete

AA0003  DEC             Global physical address for some DEC machines

AA0004  DEC             Local logical address for systems running DECNET

Data value (hexadecimal):  00:00:E6: 34:ED:A3

Data values in other bases: Not Applicable

Start Bit: 64

Length: 48

ARP PDU > Sender Protocol Address > for the selected ARP PDU

Field Name:  Sender Protocol Address

Description:  The protocol of the sender computer. This is used to identify the senders Protocol.

Data value (decimal): 192.168.0.101

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 6 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0110 | 0101 |

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 1100 0000 1010 1000 0000 0000 0001 0110

Start Bit: 112

Length: 32

ARP PDU > Target Hardware > for the selected ARP PDU

Field Name:  Target Hardware

Description: The Physical address or MAC address of the network adapter of the target terminal.

00000C  Cisco

00000E  Fujitsu

00000F  NeXT

000010  Sytek

00001D  Cabletron

000020  DIAB (Data Intdustrier AB)

000022  Visual Technology

00002A  TRW

000032  GPT Limited (reassigned from GEC Computers Ltd)

00005A  S & Koch

00005E  IANA

000065  Network General

00006B  MIPS

000077  MIPS

00007A  Ardent

000089  Cayman Systems  Gatorbox

000093  Proteon

00009F  Ameristar Technology

0000A2  Wellfleet

0000A3  Network Application Technology

0000A6  Network General (internal assignment, not for products)

0000A7  NCD             X-terminals

0000A9  Network Systems

0000AA  Xerox           Xerox machines

0000B3  CIMLinc

0000B7  Dove            Fastnet

0000BC  Allen-Bradley

0000C0  Western Digital

0000C5  Farallon phone net card

0000C6  HP Intelligent Networks Operation (formerly Eon Systems)

0000C8  Altos

0000C9  Emulex          Terminal Servers

0000D7  Dartmouth College (NED Router)

0000D8  3Com? Novell?   PS/2

0000DD  Gould

0000DE  Unigraph

0000E2  Acer Counterpoint

0000EF  Alantec

0000FD  High Level Hardvare (Orion, UK)

000102  BBN             BBN internal usage (not registered)

0020AF  3COM ???

001700  Kabel

008064  Wyse Technology / Link Technologies

00802B  IMAC ???

00802D  Xylogics, Inc.  Annex terminal servers

00808C  Frontier Software Development

0080C2  IEEE 802.1 Committee

0080D3  Shiva

00AA00  Intel

00DD00  Ungermann-Bass

00DD01  Ungermann-Bass

020701  Racal InterLan

020406  BBN             BBN internal usage (not registered)

026086  Satelcom MegaPac (UK)

02608C  3Com            IBM PC; Imagen; Valid; Cisco

02CF1F  CMC             Masscomp; Silicon Graphics; Prime EXL

080002  3Com (Formerly Bridge)

080003  ACC (Advanced Computer Communications)

080005  Symbolics       Symbolics LISP machines

080008  BBN

080009  Hewlett-Packard

08000A  Nestar Systems

08000B  Unisys

080011  Tektronix, Inc.

080014  Excelan         BBN Butterfly, Masscomp, Silicon Graphics

080017  NSC

08001A  Data General

08001B  Data General

08001E  Apollo

080020  Sun             Sun machines

080022  NBI

080025  CDC

080026  Norsk Data (Nord)

080027  PCS Computer Systems GmbH

080028  TI              Explorer

08002B  DEC

08002E  Metaphor

08002F  Prime Computer  Prime 50-Series LHC300

080036  Intergraph      CAE stations

080037  Fujitsu-Xerox

080038  Bull

080039  Spider Systems

080041  DCA Digital Comm. Assoc.

080045  ???? (maybe Xylogics, but they claim not to know this number)

080046  Sony

080047  Sequent

080049  Univation

08004C  Encore

08004E  BICC

080056  Stanford University

080058  ???             DECsystem-20

08005A  IBM

080067  Comdesign

080068  Ridge

080069  Silicon Graphics

08006E  Concurrent      Masscomp

080075  DDE (Danish Data Elektronik A/S)

08007C  Vitalink        TransLAN III

080080  XIOS

080086  Imagen/QMS

080087  Xyplex          terminal servers

080089  Kinetics        AppleTalk-Ethernet interface

08008B  Pyramid

08008D  XyVision        XyVision machines

080090  Retix Inc       Bridges

484453  HDS ???

800010  AT&T

AA0000  DEC             obsolete

AA0001  DEC             obsolete

AA0002  DEC             obsolete

AA0003  DEC             Global physical address for some DEC machines

AA0004  DEC             Local logical address for systems running DECNET

Data value (hexadecimal): 00:00:00:00:00:00

Data values in other bases: Not applicable

Start Bit: 144

Length: 48

ARP PDU>Target Protocol Address> for the selected ARP PDU

Field Name: Target Protocol Address

Description: The protocol of the sender computer. This is used to identify the targets Protocol.

Data value (decimal): 192.168.0.145

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 9 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 1001 | 0001 |

Start Bit: 196

Length: 32

2.2.18 IP PDU for the selected UPD PDU

IP PDU > IP Version for the selected UDP PDU

Field Name: IP Version

Description:  Version is a 4-bit field that indicates the format of the Internet header.

Data value (decimal):  4

Data values in other bases:

| Hexadecimal | 4 |
| --- | --- |
| Binary | 0100 |

Start Bit: 0

Length: 4

IP PDU > Header Length for the selected UDP PDU

Field Name:  Header Length

Description:  The IHL field is a 4-bit field indicating the length of the internet header in 32 bit words, and thus points to the beginning of the data.  The minimum value of a correct header is 5.

Data value (decimal):  5.

Data values in other bases:

| Hexadecimal | 0 | 5 |
| --- | --- | --- |
| Binary | 0000 | 0101 |

Start Bit: 4

Length: 4

IP PDU > Type of Service for the selected UDP PDU

Field Name:  Type of Service

Description:  Type of Service is an 8-bit field that provides and indication of the abstract parameters of the quality of service desired.  These parameters guide the selection of the actual service parameters when transmitting a datagram through a particular network.

Bits 0-2: Precedence

Bit 3: (D)  0 = Normal Delay		1 = Low Delay

Bit 4: (T)  0 = Normal Throughput	1 = High Throughput

Bit 5: (R)  0 = Normal Reliability	1 = High Reliability

Precedence:

111 = Network Control		011 = Flash

110 = Internetwork Control		010 = Immediate

101 = CRITIC/ECP			001 = Priority

100 = Flash Overrided		000 = Routine

Data value (decimal): 16

Data values in other bases:

| Hexadecimal | 1 | 0 |
| --- | --- | --- |
| Binary | 0001 | 0000 |

Start Bit: 8

Length: 8

IP PDU > Total Length for the selected UDP PDU

Field Name: Total Length

Description: Total Length is a 16-bit field that indicates the length of the frame, measured in octets, including Internet header and data.  The maximum size is 216-1 or 65,535 octets; however, the recommended maximum size is 576 octets.

Data values (decimal):  296

Data values in other bases:

| Hexadecimal | 0 | 1 | 2 | 8 |
| --- | --- | --- | --- | --- |
| Binary | 0000 | 0001 | 0010 | 1000 |

Start Bit: 16

Length: 16

IP PDU > Identification for the selected UDP PDU

Field Name:  Identification

Description:  Identification is a 16-bit field.  An identifying value is assigned by the sender to aid in assembling the fragments of a data gram.  The identifier is chosen based on the need to provide a way to uniquely identify the fragments and protocol for the time the data gram or any fragment could be alive in the Internet.

Data value (decimal): 48087

Data values in other bases:

| Hexadecimal | B | B | D | 7 |
| --- | --- | --- | --- | --- |
| Binary | 1011 | 1011 | 1101 | 0111 |

Start Bit: 32

Length: 16

IP PDU > Flags for the selected UDP PDU

Field Name:  Flags

Description:  Flags is a 3-bit field that indicates directions for fragmentation.

Bit 0: reserved, must be 0

Bit 1: (DF)  0 = May Fragment		1 = Don’t Fragment

Bit 2: (MF) 0 = Last Fragment		1 = More Fragment

Data value (binary): 000

Data values in other bases:  Not applicable

Start Bit: 48

Length: 3

IP PDU > Fragment Offset for the selected UDP PDU

Field Name:  Fragment Offset

Description:  The Fragment Offset is a 13- bit field indicating where in the Ethernet frame this fragment begins.  The Fragment Offset is measured in units of 8 octets, and the first fragment has offset 0.

Data value (decimal): 0

Data values in other bases:

| Hexadecimal | 0 | 0 |
| --- | --- | --- |
| Binary | 0000 | 0000 |

Start Bit: 51

Length: 13

IP PDU > Time to Live for the selected UDP PDU

Field Name: Time to Live

Description:  Time to Live is an 8-bit field that indicates the maximum time the data gram is allowed to remain in the Internet.  If this field contains the value 0, then the data gram must be destroyed.  This field is modified in Internet header processing.  The time is measure in units of seconds, and is set by the sender to the maximum time the data gram is allowed to be in the Internet.  This field is decreased at each point that the Internet header is processed.  The intention is to cause undeliverable packets to be discarded, and to bind the maximum data gram lifetime.

Data value (decimal): 60

Data values in other bases:

| Hexadecimal | 3 | C |
| --- | --- | --- |
| Binary | 0011 | 1100 |

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 0010 0000

Start Bit: 64

Length: 8

IP PDU > Protocol for the selected UDP PDU

Field Name:  Protocol

Description:  Protocol is an 8-bit field that indicates the next level protocol that is used in the data portion of the Internet diagram.

# Dec Hex	Protocol					Dec		Hex	   Protocol

0 	  00	Reserved					22		16	   Multiplexing

1 	  01	ICMP						23		17	   DCN

2	  02	Unassigned					24		18	   TAC Monitoring

3 	  03	Gateway-to-Gateway				25-76		19-4C	   Unassigned

4 	  04	CMCC Gateway Monitoring Message	77		4D	   Any local network

5	  05	ST						100		64	   SATNET and 
  											   Backroom EXPAK

6	  06	TCP						101		65	   MIT Subnet     
 											   Support

7	  07	UCL						102-104	66-68	   Unassigned

10	  0A	Unassigned					105		69	   SATNET 
 											   Monitoring

11	  0B	Secure						106		6A	   Unassigned

12	  0C	BBN RCC Monitoring			107		6B	   Internet Packet Core 
 											   Utility

13	  0D	NVP						110-113	6E-71	   Unassigned

14	  0E	PUP						114		72	   Backroom SATNET 
 											   Monitoring

15	  0F	Pluribus					115		73	   Unassigned

16	  10	Telnet						116		74	   WIDEBAND 
 											   Monitoring

17	  11	XNET						117		75	   WIDEBAND 
 											   EXPAK

20	  14	Chaos						120-376	78-0178  Unassigned

21	  15	User Datagram				377		0179	    Reserved

Data value (decimal): 17

Data values in other bases:

| Hexadecimal | 1 | 1 |
| --- | --- | --- |
| Binary | 0001 | 0001 |

Start Bit: 72

Length: 8

RFC Link: http://www.faqs.org/rfcs/rfc790.html

IP PDU > Header Checksum for the selected UDP PDU

Field Name:  Header Checksum

Description:  The Header Checksum is a 16-bit field.  The Checksum is the 16-bit one’s complement sum of all 16-bit words in the header.  For purposes of computing the checksum, the initial value of its field is zero.  When both header checksums are equal, then the header bits are correct.  If either checksums vary, then a new, correct packet will need to be sent.

This is a simple way to compute the checksum and experimental evidence indicates that it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.

Data value (decimal): 16199

Data values in other bases:

| Hexadecimal | 3 | F | 4 | 7 |
| --- | --- | --- | --- | --- |
| Binary | 0011 | 1111 | 0100 | 0111 |

Start Bit: 80

Length: 16

IP PDU > Source IP Address for the selected UDP PDU

Field Name:  Source IP Address

Description:  The Source Address is a 32-bit field that contains the IP address of the host that sent the IP Packet.

The source address of the sender of the IP data gram:
NET ID ADDRESS RANGE
000-127 Class A 10.0.0.0-10.225.225
128-191 Class B 172.16.0.0-172.31.255.255
192-223 Class C 192.168.0.0-192.168.255.255
224-239 Class D (multicast)
240-255 Class E (experimental)
HOST ID
0 Network value; broadcast(old)
255 Broadcast

Data value (decimal):  192.168.0.71

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | 4 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 0100 | 0111 |

Start Bit: 96

Length: 32

IP PDU > Destination IP Address for the selected UDP PDU

Field Name:  Destination IP Address

Description:  The Destination Address is a 32-bit field that contains the address of the host that is to receive the data contained within the IP packet.

The IP address of the host where this data gram is being sent:
NET ID ADDRESS RANGE
000-127 Class A 10.0.0.0-10.225.225
128-191 Class B 172.16.0.0-172.31.255.255
192-223 Class C 192.168.0.0-192.168.255.255
224-239 Class D (multicast)
240-255 Class E (experimental)
HOST ID
0 Network value; broadcast(old)
255 Broadcast

Data value (decimal):  192.168.0.255

Data values in other bases:

| Hexadecimal | C | 0 | A | 8 | 0 | 0 | F | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary | 1100 | 0000 | 1010 | 1000 | 0000 | 0000 | 1111 | 1111 |

Start Bit: 128

Length: 32 bits

IP PDU > Options for the selected UDP PDU

Field Name:  Options

Description:  The options may or may not appear in Ethernet packets.  They have to be implemented by all IP modules (host and gateways).  What is optional is their transmission in any particular packet, not their implementation.

The option field is variable in length.  There may be zero or more options.  There are two cases for the format of an option.

Case 1: A single octet of option type

Case 2: An option-type octet, an option-length octet, and the actual option-data 			octets.

Data values:  Not applicable

Data values in other bases:  Not applicable

Start Bit: 160

Length: Variable (0-40 bits)

IP PDU > Data for the selected UDP PDU

Description:  The Data is a variable length field, which contains the actual data that is being sent from one host to another.  The data field may start with a Layer 4 header, which will give additional instructions to the application that will be receiving the data; alternately, it may be an ICMP header and not contain any user data at all.

Data values (hexadecimal):  (UDP) FF FF FF FF FF FF 08 00 69 07 9A C5 08 00 45 10

01 28 BB D7 00 00 3C 11 3F 47 C0 A8 00 47 C0 A8 00 FF 02 0D 01 14 E9 DB 18 01 C2 5A 0A FF 13 D0 0 00 00 00 00 69 6E 64 79 00 00 00 00 7F FF 11 DB 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 13 F0 00 00 00 00 7F FF 11 F6 00 00 00 00 00 00 00 00 00 00 00 00 7F FF FF FF 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 17 E3 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 10 05 9D D8 00 00 00 00 10 00 DB A8 00 00 00 00 0F B5 B1 74 00 00 00 00 0F AB 01 C8 00 00 00 00 10 05 9D F8 00 00 00 00 0F B5 9D D8 00 00 00 00 10 05 9D FC 00 00 00 00 0F B5 B1 74 00 00 00 00 10 05 9B 18 00 00 00 00 0F AB 02 80 00 00 00 00 00 00 00 00 00 00 00 00 00 00

Data values in other bases:

Not Applicable

Start Bit: 0

Length: 268

IP PDU > Source Port Number for the selected UDP PDU

Field Name: Source Port Number

Description:  Source Port is an optional field, when meaningful, it indicates the port of the sending process, and may be assumed  to be the port  to which a  reply should  be addressed  in the absence of any other information.  If not used, a value of zero is inserted.

Data value (decimal): 525

Data values in other bases:

| Hexadecimal | 02 | 0D |
| --- | --- | --- |
| Binary | 0010 | 1101 |

Start Bit: 0

Length: 16 bits

RFC Link: http://www.ietf.org/rfc/rfc0768.txt?number=768

IP PDU > Destination Port Number for the selected UDP PDU

Field Name: Destination Port Number

Description:  Destination Port has a meaning within the context of a particular Internet destination address.

Data value (decimal): 525

Data values in other bases:

| Hexadecimal | 02 | 0D |
| --- | --- | --- |
| Binary | 0010 | 1101 |

Start Bit: 16

Length: 16 bits

IP PDU > Length for the selected UDP PDU

Field Name: Length

Description:  Length is the length in octets of this user data gram including this header and the data (This means the minimum value of the length is eight).

Data value (decimal): 276

Data values in other bases:

| Hexadecimal | 01 | 14 |
| --- | --- | --- |
| Binary | 0000 0001 | 0001 0100 |

- The Binary sequence used here is that of Blue Technology’s data.  Blue’s data matches up with the dump file from ethereal while Mirage’s doesn’t.

- Mirage’s binary sequence was 0000 0001 0000 0100

Start Bit: 32

Length: 16 bits

IP PDU > Checksum for the selected UDP PDU

Field Name: Checksum

Description:  Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the UDP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.

Data value (decimal): 59867

Data values in other bases:

| Hexadecimal | E | 9 | D | B |
| --- | --- | --- | --- | --- |
| Binary | 1110 | 1001 | 1101 | 1011 |

Start Bit: 48

Length: 16 bits

IP PDU > Data for the selected UDP PDU

Field Name: Data

Description: Source Port is an optional field, when meaningful, it indicates the port of the sending process, and may be assumed to be the port to which a reply should be addressed in the absence of any other information. If not used, a value of zero is inserted.

Data value (hexadecimal): 18 01 C2 5A 0A FF 13 D0 00 00 00 00 69 6E 64 79 00 00 00 00 7F FF 11 DB 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 13 F0 00 00 00 00 7F FF 11 F6 00 00 00 00 00 00 00 00 00 00 00 00 7F FF FF FF 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 7F FF 17 E3 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 09 00 00 00 10 05 9D D8 00 00 00 00 10 00 DB A8 00 00 00 00 0F B5 B1 74 00 00 00 00 0F AB 01 C8 00 00 00 00 10 05 9D F8 00 00 00 00 0F B5 9D D8 00 00 00 00 10 05 9D FC 00 00 00 00 0F B5 B1 74 00 00 00 00 10 05 9B 18 00 00 00 00 0F AB 02 80 00 00 00 00 00 00 00 00 00 00 00 00 00 00

Data values in other bases: Not Applicable

Start Bit: 0

Length: 268 bits

Section 3 Data Storage

Section 3.1 Naming convention

The data session files will have a naming convention that will distinguish the type of the file and the chosen name to represent the file.  The type of file will end in the *.dat format.  The date does not have to be given in the file as Paradigm will be writing a script to find it using Perl as the scripting language.  All files will be stored in the same directory named Files, as they will be sorted by type through the Packet Descriptor.  An example of an ftp packet using the file name convention is ftp_file01.dat.

Section 3.2 Physical location of data

The files will be stored and maintained on Siena’s Oraserv server in the “/home/csis4100405/EtherealSessions” directory.  The files in this directory will have -rw-r--r-- permissions while the directory will have drwxrwxr-x permissions.

Section 4 Testing Requirements

During the unit and functional testing phase, Black Box testing will be used. With Black Box testing, possible inputs are inserted into the program, and a successful test includes observing expected outputs. For functionality testing, there will be no need to look at what is happening inside the program itself. For this testing phase, the testing subset of the team will test every facet of the program.

Section 4.1 Testing Specifications

- The web site will contain four screens:

  - Protocol Selector Screen

  - Packet Selector Screen

  - Information Display Screen

  - History Page

The list of “active” protocols (those that the user can select) are as follows:

- SNMP

- FTP

- SMTP

- HTTP

- PING

- TELNET

- ARP

- SSH

The list of “inactive” protocols (those that show up in the protocol hierarchy, but cannot be chosen for viewing) are as follows:

- SCP

- DHCP

- DNS

- RSVP

- LDAP

- NTP

The protocol hierarchy display will be available at any time while the web site is being accessed. When the hierarchy is accessed, a picture will appear with the hierarchy and active links. Once a selection is made, a drop down menu will appear to allow the user to select an Ethereal data session.

- When the user first accesses the TCP/IP Descriptor, this is the first screen he or she will see.

- Within the protocol hierarchy display, a picture of the TCP/IP and Open Systems Interconnection (OSI) layers will be displayed alongside the protocol hierarchy, with an emphasis on which protocols reside within each layer.

- There will be a button that will link the user to the History Page.  This page will display all groups that have worked on the project, both past and present.

- Selecting a protocol will cause a drop down menu containing all ethereal data sessions in the /home/csis4100405/EtherealSessions folder of Oraserv.

- Selecting one of those data sessions will move the user to the Packet Selector screen.

- Selecting a protocol will cause a picture of that protocol, and any lower level protocols, to be displayed in the Protocol Display Zone of the TCP/IP Packet Descriptor.

The Packet Selector of the TCP/IP Packet Descriptor will display the selected data session’s packets.  Only the packets of the selected protocol will be displayed for the user to select.

- If there are more packets than our displaying window will allow the user will be able to scroll down and highlight a different packet.

- There will be a button that will link the user to the History Page.  This page will display all groups that have worked on the project, both past and present.

- The user is able to return to the Protocol Selector Screen by clicking on the “Choose Protocol” button.

- To select a highlighted packet, the user will be able to either double-click the packet, or click the “View Packet” button.

- Selecting a packet will bring the user to the Information Display window where a picture of that protocol, and any lower level protocols, will be displayed.

The Information Display Screen of the TCP/IP Packet Descriptor will display the selected packet in the selected protocol, with a breakdown of the protocol’s appropriate fields, in a colorful and informative matter.

- The user is able to return to the Protocol Selector Screen by clicking on the “Choose Protocol” button.

- The user is able to return to the Packet Selector Screen by clicking on the “Choose Packet” button.

- There will be a button that will link the user to the History Page.  This page will display all groups that have worked on the project, both past and present.

- Each PDU picture will be broken up into its component fields. Bit and octet positions will be shown.

- Each picture of each protocol will show the Request for Comments (RFC) number. The number will be a link to a homepage containing comprehensive information about that protocol.

- There will be a protocol stack displayed in the upper right section of the Information Display Screen, allowing the user to be able to switch between the selected protocol and any of the lower level protocols.

- In each picture, field names and protocol data will be displayed.

- Selecting a field in one of the displayed units will cause information about that field to be displayed in the Information Box on the left side of the screen.

The Information Box, which is part of the Information Display Screen, will display field specific information for the various PDUs.

- When a field is selected, that field will be highlighted, and a picture of that field, with the contained data and bit positions, will be displayed.

- Along with the picture, information about the selected field will also be displayed.

- The information will be displayed in all appropriate radices.

The History Page will contain information about groups, both past and present, that have worked on the TCP/IP Descriptor.

- This page will contain links to every group’s home page as well as to the Software Engineering website, and back to the TCP/IP Packed Descriptor.

- This page will also contain a description of the project as given to us by Mr. Ken Swarner.

Other Requirements:

- The Descriptor Home Page will be viewable in Microsoft Internet Explorer and Netscape Navigator in full screen mode at 1024 x 768 screen resolution.

Section 4.2 Testing Forms

Unit Testing Form

| What being tested | Tested for | Expected Outcome | Pass or Fail | Comments |
| --- | --- | --- | --- | --- |
| Protocol Selector Screen (PrSS) | Does it load? | The PrSS page loads when access is attempted |  |  |
| PrSS | Is the protocol tree displayed correctly? | The connecting lines on the protocol tree connected are correctly and contains both active and inactive protocols |  |  |
| PrSS | Is the TCP/IP Model present? | The TCP/IP Model appears to the right of the protocol tree |  |  |
| PrSS | Is the OSI Model present? | The OSI Model appears to the right of the TCP/IP Model |  |  |
| PrSS | Is the History Button present? | The History Button is on the page on the lower right hand corner |  |  |
| PrSS Active Protocols* | Does drop down appear when clicked? | When the user clicks an active protocol the drop down menu containing a list of Ethereal data sessions is displayed |  |  |
| PrSS Drop Down Menu* | Does drop down contain all the correct files named correctly? | The names of the Ethereal data sessions are correct |  |  |
| PrSS Active Protocol Buttons* | Correct box color? | The color of the active protocol boxes are consistent and different from the inactive protocol boxes |  |  |
| PrSS Active Protocol Buttons* | Correct font color? | The color of the active protocol font is readable, consistent, and different from that of the inactive protocol font |  |  |
| PrSS Inactive Protocols* | Correct box color? | The color of the inactive protocol boxes are consistent and different from the active protocol boxes |  |  |
| PrSS Inactive Protocols* | Correct font color? | The color of the inactive protocol font is readable, consistent, and different from that of the active protocol font |  |  |
| PrSS Information Box | Is it present? | The Information Box appears below the protocol screen when the PrSS loads |  |  |
| PrSS Information Box* | Does it display the correct information when you select a protocol? | When a protocol is selected, information about that protocol appears in the information box |  |  |
| PrSS | Is the RFC link present? | The RFC link is present in the Ethernet Frame at the top of the screen |  |  |
| PrSS | Does the RFC link bring you to the correct site? | The RFC link brings the user to the appropriate RFC page |  |  |
| PrSS | Does the link to the History page work? | Upon clicking the history page button we are brought to the History Page |  |  |
| PrSS | Does the link to the History Page appear? | The History Page button appears on the bottom right of the screen |  |  |
| Packet Selector Screen (PaSS) | Does it load? | The PaSS page loads once a protocol and data session are selected |  |  |
| PaSS | Is the data session parsed correctly? | The packets for the data session are displayed properly |  |  |
| PaSS | Is the default packet highlighted upon load? | The first packet in the list of packets is highlighted upon page load |  |  |
| PaSS | Is the box scrollable if there is more than a page worth of packets in the data session? | If more than a page of packets is in the selected session, a scroll bar allows the user to go through the entire list |  |  |
| PaSS* | Is the title correct for the selected protocol? | The title of the selected protocol appears above the packet selection box in the center of the page |  |  |
| PaSS | Are we allowed to highlight different packets? | The user can change the highlighted packet from the default to others |  |  |
| PaSS | Does the link to the History page work? | Upon clicking the history page button we are brought to the History Page |  |  |
| PaSS | Does the link to the History Page appear? | The History Page button appears on the bottom right of the screen |  |  |
| Information Display Screen (IDS) | Does it load? | The IDS page loads once a packet is selected |  |  |
| IDS* | Do the correct number of fields show up in their correct positions and lengths? | All the fields for the selected protocol show up and are the proper length and in their correct positions |  |  |
| IDS* | Does the top bar load correctly? | Upon page load does the Ethernet Bar load with the proper information |  |  |
| IDS* | Does the link to the History Page appear? | Upon clicking the history page button we are brought to the History Page |  |  |
| IDS* | Does the link to the History page work? | The History Page button appears on the bottom right of the screen |  |  |
| IDS* | Does the protocol stack for the selected protocol and its lower level protocols display properly? | The selected protocol and its lower level protocols are displayed in a stack to the right of the Ethernet Bar |  |  |
| IDS* | Is the data in each field displayed correctly? | The data in each field is correct and displayed in a coherent manner |  |  |
| IDS* | Upon clicking a field, is the information about that field displayed in the Information Box? | When a field is selected, information about it appears in the Information Box |  |  |
| IDS* | Does the background color of the Information Box match the color of the selected field? | The background of the Information Box matched that of the field it is displaying information about |  |  |
| IDS* | Does the RFC link point to the correct location? | The RFC link brings the user to more information about the protocol |  |  |
| IDS* | Can we navigate between the protocols using the protocol stack? | Clicking the protocol stack allows the user to change view the lower level protocols or return to the starting protocol |  |  |
| History Page | Does everything appear correctly? | The project description, title, and links all appear in a neat and coherent manner |  |  |
| History Page | Do the links work? | All the links bring the user to the location that that say they do |  |  |

*  Note:	For the steps that require testing more than one object, separate sub-test forms will be created.  These sub-test forms will be modeled to encompass each of the separate protocol’s unique attributes.

Functional Testing Form

| What being tested | Tested for | Expected Outcome | Pass or Fail | Comments |
| --- | --- | --- | --- | --- |
| PrSS | Upon click of a data session from drop down menu does it go to the PaSS? | When a data session from the drop down menu is clicked, it brings the user to the PaSS |  |  |
| PaSS | Is the correct protocol from the PrSS displayed at the top of the screen? | The title of the selected protocol appears above the packet selection box in the center of the page |  |  |
| PaSS | Are the packets displayed the correct ones for the data session chosen in PrSS? | The packets displayed in the PaSS are for the selected data session and protocol |  |  |
| PaSS | Does Choose Protocol button take us to PrSS? | Pressing the Choose Protocol button brings the user back to the PrSS |  |  |
| PaSS | Does double clicking a packet take us to IDS? | Double clicking a packet brings the user to the IDS |  |  |
| PaSS | Does the View Packet button take us to IDS? | Highlighting a packet and pressing the View Packet button brings the user to the IDS |  |  |
| IDS | Is the correct packet displayed as given to us by the PaSS? (by double clicking or View Packet button) | The packet whose information is displayed on the IDS is the packet that the user selected |  |  |
| IDS | Does Choose Protocol button take us to PrSS? | Pressing the Choose Protocol button brings the user back to the PrSS |  |  |
| IDS | Does Choose Packet button take us to PaSS? (check to make sure still in same data session) | Pressing the Choose Packer button brings the user back to the PaSS for the selected data session and protocol |  |  |
| History Page Button* | Does clicking the History Page button take us there? | Upon clicking the History Page button the user is brought to the History Page |  |  |
| History Page | Does the Back link on the History Page bring us back to where we left off? | The Back link brings the user back to the point from which the History Button was selected |  |  |
| History Page | Does the Blue Technologies link on the History Page bring us to their website? | Clicking the Blue Technologies link brings us to their website |  |  |
| History Page | Does the Mirage Inc. link on the History Page bring us to their website? | Clicking the Mirage Inc. link brings us to their website |  |  |
| History Page | Does the Paradigm Solutions link on the History Page bring us to their website? | Clicking the Paradigm Solutions link brings us to their website |  |  |
| History Page | Does the Software Engineering link on the History Page bring us to the Software Engineering webpage? | Clicking the Software Engineering link brings us to the Software Engineering webpage |  |  |

*  Note:	For the steps that require testing more than one object, separate sub-test forms will be created.  These sub-test forms will be modeled to encompass each of the separate protocol’s unique attributes.

5.0 Appendix

5.1 Glossary

Gantt Chart - A chart that depicts progress in relation to time, often used in planning and tracking a project.

GUI - (Graphical user interface) An interface, which uses text boxes and buttons to allow easy access of information by use of a mouse or other pointing device.

HTML – (Hypertext markup language) A markup language used to structure text and multimedia documents and to set up hypertext links between documents, used extensively on the World Wide Web.

Internet - An interconnected system of networks that connects computers around the world via the TCP/IP protocol.

Linear Sequential Model / Classic Waterfall Model – A systematic, sequential approach to software development that begins at the system level and progresses through analysis, design, coding, testing, and support.

Macromedia Dreamweaver MX 2004 - Website development environment.

(http://www.macromedia.com)

Open Systems Interconnection Reference Model - A model of network architecture and a suite of protocols (a protocol stack) to implement it, developed by the International Organization for Standardization (ISO) in 1978 as a framework for international standards in heterogeneous computer network architecture.

PDU- (Protocol Data Unit) Information that is delivered as a unit among peer entities of a network that may contain control information, address information, and/or data.

PHP – (PHP: Hypertext Preprocessor) A server-side embedded scripting language. The PHP commands, which are embedded in the web page's HTML, are executed on the web server to generate dynamic HTML pages.

RFC- (Request for Comments) number.  A formal document from the Internet Engineering Task Force (IETF) that is the result of committee drafting and subsequent review by interested parties.

Software - Written programs or procedures or rules and associated documentation pertaining to the operation of a computer system and that are stored in read/write memory.

TCP/IP – (Transmission Control Protocol / Internet Protocol) The suite of communications protocols used to connect hosts on the Internet. TCP/IP uses several protocols, the two main ones being TCP and IP. TCP/IP is built into the UNIX operating system and is used by the Internet, making it the primary standard for transmitting data over networks.

5.2 Gantt Chart